# added risk BY RAINY WEATHER

# on the roads of Normandie-Centre Region in France

# Some elements for the French IRCAD-SARI traffic monitoring and information system for drivers and operators

Maurice ARON, Ruth Bergel-Hayat, Guillaume Saint Pierre, Eric Violette

Maurice Aron,

INRETS (The French National Institute for Transportation and Safety Research)

2 av. du Général Malleret-Joinville, 94114, Arcueil, France

Phone number + 33 1 47407131

Fax number + 33 1 45475606

maurice.aron@inrets.fr

Ruth Bergel-Hayat,

INRETS (The French National Institute for Transportation and Safety Research)

2 av. du Général Malleret-Joinville, 94114, Arcueil, France

Phone number + 33 1 47407160

Fax number + 33 1 45475606

ruth.bergel@inrets.fr

Guillaume Saint-Pierre,

ENPC LIVIC,

route de la Minière, Satory 78000 Versailles France

Phone number + 33 1 40432901

Fax number + 33 1 40432930

saint@cict.fr

Eric Violette,

CETE de Normandie-Centre, Chemin de la Poudrière - BP 245 76121 Le Grand Quevilly, France

Phone number + 33 2 35688133

Fax number + 33 2 35675901

Eric.violette@equipement.gouv.fr

# added risk BY RAINY WEATHER

# Some elements for the French IRCAD-SARI traffic monitoring and information system for drivers and operators

Maurice ARON (1), Ruth Bergel-Hayat (1), Guillaume Saint Pierre (2), Eric Violette (3)

(1) maurice.aron@inrets.fr, ruth.bergel@inrets.fr

INRETS, 2 av. du Général Malleret-Joinville, 94114, Arcueil, France www.inrets.fr

(2) saint@cict.fr

ENPC LIVIC, route de la Minière, Satory 78000 Versailles France

(3) eric.violette@equipement.gouv.fr

CETE de Normandie-Centre, Chemin de la Poudrière - BP 245 76121 Le Grand Quevilly, France

## SUMMARY

The project “IRCAD-SARI”, funded by the French Ministry of Transport, will experiment on some rural roads in France a warning sign system during adverse weather conditions. The safety stake is assessed by computing the added-risk in case of adverse weather conditions, and especially in case of rain on bends. The method for estimating rain exposure takes into account several types of meteorological information, and the additional weather information of the accident database. The traffic database, when available, enables to drop the approximate assumption that traffic is not correlated with rain. A method for computing the added risk due to rain is proposed and some related results are given in this paper.

## Keywords

Weather conditions, road accidents, traffic database, added-risk, rain, rural roads.

## ACKNOWLEDGMENTS

This work was made possible thanks to the PREDIT and DRAST departments of the French Ministry of Transport, which funded this research in the framework of the experimental research project IRCAD (Informing drivers of risks during inclement weather) of the SARI program (Automated Monitoring of Roads and Infrastructures). We would like to thank Maryline Gallene and Minh-Tan Do from LCPC (the French Public Works Research Laboratory) representatives who initiated and manage this project.

## 1. Introduction

The French program SARI, funded by the French Ministry of Transport and managed by LCPC (the French Public Works Research Laboratory) will install on the road network a warning sign system to alert drivers at the moments  there is a risk of running off the road, in particular due to a poor adherence between the road and the tires. The sub-project IRCAD addresses the meteorological risk. Preliminarily to the experiment, this project develops  researches in three directions: the drying of the roadway after the rain, the probability of running off the road according to the vehicle and driver’s characteristics and according to the dynamic of the vehicle during rain, wind and wet roadway, and the added-risk due to rain –see Aron et al., (2006). This third topic is the subject of this paper.

J. Andrey (2003), after reviewing 14 studies addressing the relative risk due to rain or snow, found a 70% increase in the risk of injury due to rainfall in Canada.

K. Keay & I. Simmonds (2006) found that, in Melbourne, the rain has an effect on the accident frequency. This effect varies with the period in the day. They also observed, as Lee & Saccomanno (2002) did before, that the amount of rainfall has a significant impact on accident occurrence. The duration of the dry spell before the rainfall and the season have also been identified as contributory factors by Eisenberg (2004) and Shankar (2004)

In France the French National Road Safety Observatory (ONISR, 2005) estimates that, in the period from 1995 to 2004, the proportion of road collisions during inclement weather was around 16%, and that 86% of these accidents occurred during rainfall.

Previous studies stated that the added-risk due to rain is equal to two (Le Breton 1990) or comprised between two and three (Brodsky and Hakkert, 1988). Other studies (CETE, 2005) led by CETE of Normandie-Centre (the Technical Study and Engineering Centre of the French Ministry of Transport) and LCPC showed that the speed behavior of French drivers does not change sufficiently, during adverse weather conditions, regarding the decrease of the braking performances of the vehicles. Because of the availability of accurate and various weather data and of a huge traffic volume data set collected by CETE, the identification of the added-risk during rain is enhanced.

The paper is organized as follows. The weather data are first described according to different sources, in section 2. The accident data are then described in section 3 and a data fusion method is also presented, which enables to reconstruct the “best” weather data, with regard to the accident data file. The traffic volume data, when available, is described in section 4. Finally, risk and added risk formulae are given in section 5 with related numerical results.

## 2. The weather data

Brodsky and Hakkert (1988) estimated that knowledge on rain is not sufficient. Météo-France, the French meteorological operator, provided two sources of weather data, the first one using a rain gauge, the second one based on a human observer; the first source is quantitative and provides the number of rain millimeters every six minutes; the second one is qualitative - a few categories of rainfalls or snowfalls are considered.

### The rain gauge: six minutes data and hourly data

The minimum rainfall height measured by a rain gauge is 0.2 mm. Rain gauge movements, in France, are recorded either every six minutes or every hour.

#### Six minutes data

At least on one site by French département, a meteorological station is equipped with a rain gauge providing six-minute records.

The two following graphs presented in Figures 1 and 2 are based on rain gauge records for the period 1997-2003. They show the average development of rain in the day, measured in occurrence (percentage of rainy time) and in rainfall height (number of millimeters) every six minutes of the day.

#### Hourly data

In addition, on three sites (Octeville, La Hève, Dieppe), hourly rain gauge records give the rain level (in millimeters), unfortunately without providing the number of minutes of rainfall by hour. This aggregation causes a bias on the estimation of the rainy period: when considering as a whole rainy hour every hour where some rain falls, the total rainy period will be too long. This induces an under-estimation of the rain risk. This bias has been estimated on Rouen by aggregating the minute data in hourly data, and then by matching the initial source of data with the aggregated one. We found that there were:

- 16,1 % rainy hours instead of 10,1%, computed with disaggregated data (from human observation)

- 12.6% rainy hours instead of 6.1%, computed with disaggregated data (from rain gauges).

#### Variability of the rain in Normandy

The (geographical) variability of rain is important, which limits the use of weather data to areas around each meteorological station. This is illustrated by matching weather information from two distant meteorological stations.

We propose, for identifying the level of matching of the two data sources, a dissymmetric criterion C named “concurrence” which focuses on rain: its value is 100% when the matching is perfect and 0% when rain is never simultaneously observed on both sources:

Note  	“a” the period where both sources indicate no-rain

“b” the period where the first station indicates rain, and the second station indicates no-rain

“c” the period where the first station indicates no-rain, and the second station indicates rain

“d” the period where both sources indicate rain

(1)

Figure 3 provides the matching criterion according to the distance between the stations: The values are rather low,  for the stations  “Octeville”-and “La Hève” which are 10 km  away from one another.

### The human observation: one minute data and hourly data

Meteo-France provides at every hour two informations the « present weather » which describes the weather for the ten last minutes and the « past weather » which describes the weather for the fifty previous minutes

These data are available in one station by French département (here in Rouen and Evreux)

### This second source, although qualitative, is more accurate thanks to the qualities of the human observer.

In addition, the raw data (the list of rainfall events, with the hours and minutes of beginning and ending) were fortunately available at Rouen and Evreux for a part of the studied period (January 1997-August 2002).

### Matching rain gauge and human observation at Rouen

The coincidence between human observation and rain gauge has been matched for 49,656 hours covering the period January 1997- August 2002, the results are given in Table 1.

Note that the one-minute human information has been aggregated on a 6 minutes basis for this match with the 6-minutes rain gauge data. In the following part, the same 6-minutes aggregation is used.

The value of the concurrence criterion is:

(2)

This low value is due to the fact that human observation is more precise, the percentage of rainy time periods according to the human observation is 10.1% against 6,1% from rain gauges at Rouen.

#### Data fusion between rain gauge and human observation

Two logistic regression models have been calibrated – the first at Rouen, the second at Eveux, (Saint Pierre et al., 2007)- in order to determine the “best” rain periods from the 6-minute rain gauge records (existence of rain and rainfall height), and  from the hourly present weather and the hourly past weather. As the temporal scale of present weather and past weather is too large , we expanded present weather and past weather data in a new 6-minute series which is either equal to the past weather (from h-48 minutes to h-12 minutes)  or to the past weather (from h-12 to h+12 minutes). This logistic regression model has been calibrated thanks to the six-minute human observations.

Table 2 provides the rain duration according to the different data sources including the “reconstructed” rain from the logistic regression models.

Note that the logistic regression provides a probability of rain for every period. Then, according whether this probability is larger or smaller than a specified probability threshold of cutting-off, rain is assumed or not for the period. This is the reason why four thresholds, giving four estimations of the rainfall duration, have been considered in the previous table 2.

## 3 The accident data file

8,952 accidents occurred between January 1997 and December 2003 on rural roads of the two French départements (Eure & Seine-Maritime which constitute Haute Normandie region), outside agglomerations or inside small agglomerations of less than 5,000 inhabitants.

### Accidents and weather conditions

Most accidents (6427 accidents, i.e. 71.8% out of the 8952 accidents) occurred during normal weather conditions. Figure 2 provides the distribution related to the weather conditions of the 2525 (28.2%) accidents which occurred during adverse weather conditions – accidents with normal weather conditions have been removed for readability. Among them, the most part (16.1%) is accidents during rain.

### Accidents and infrastructure (bends)

Table 3 gives the distribution of the 8952 accidents according to the occurrence of (light or heavy) rain and according to the existence of a bend.

Without knowing the relative length of bends on the network, neither the relative duration of rain, it is possible to compute a “relative frequency” of accidents during rain against during no-rain weather as:

R=

The restricted relative frequency on straight sections only is Rstraight= =18.1%   	(3)

The restricted relative frequency on bends only is Rbend==22.6%			(4),

These two relative frequencies have not by themselves a special interest, but Rbend / Rstraight (here equal to 1.3) is the odd-ratio of the previous table 3 and confirms that the effect of rain is larger on bends than on straight sections.  According to this result, the warning sign system of our IRCAD-SARI project will focus on bends.

### Matching weather information from the meteorological station and from the accident database

The accident database is to a certain extent a third source of meteorological data, stating the weather conditions at the moment when the accident occurs. This information is different from the weather information of the meteorological station since:

- the location of the accident is more or less remote from the meteorological station, matching this information with the weather information of the meteorological station must be made according to the “flight” distance between the accident location and the meteorological station.

- the information in the accident data file is not made by meteorologists, but by police officers

- these police officers arrive on the accident site only a few minutes after the crash, and their statement might be influenced by drivers, since rain is an exculpation of accident.

Matching weather information from the accident database and from the meteorological station is necessary, since consistency between both sources of information is required in order to compute the risk in the rain

As an example, in order to provide real time crashes forecasts, Abdel-Aty and Pemmanaboina (2007) matched via a logistic regression model the information of the five nearest to the studied highway section weather stations, with the weather information provided by the accident database... A “rain index” was derived from this modeling, and appeared to be highly significant for forecasting the probability of an accident.

In our case, we compute the risk of accident due to rain. The numerator of the risk (the number of accidents in the rain) is linked to the first source (accident data base) whereas the denominator (the number of vehicle-kilometers in the rain) is linked to the second source (weather station).

As the distance from the accident location to the meteorological station is a relevant parameter  for this match, table 4 gives  the distribution of accidents around Rouen according to the occurrence of rain (source accident database) and according to their distance to Rouen by 5-km wide rings (the table is limited to an area of 40 km around Rouen).

The match of the two sources, for each ring, is evaluated by the concurrence criterion of formula (1):

“a” is the number of accidents at moments where both sources indicate no-rain

“b” is the number of accidents where the meteorological station indicates no rain, and the accident data base indicates -rain

“c” is the number of accidents at moments where the meteorological station indicates rain, and the accident data base indicates no-rain

“d” is the number of accidents at moments where both sources indicate rain

The values of this criterion according to the distance from Rouen are displayed on Figure 5.

Note that as there are several series of weather data (rain gauge, human detailed observation and reconstructed rain), the criterion has been computed three times.

In Figure 5 the”reconstructed rain” is the output of the binomial logistic regression model with a probability threshold of 0.2, which minimizes the concurrence criterion. Note that this threshold does not optimize the match between the reconstructed rain and the learning set (the human detailed observation). With the selected concurrence criterion, it minimizes the discrepancy between the human detailed observation and accident data base.

This figure 5 is based on 3842 accidents which occurred in the 40 km area around Rouen (data in Table 3 and in table 5)

Incidentally, this shows that the criterion does not decrease so much with the distance and that “reconstructed” rain is better than “human meteorologist” information, itself better than rain gauge.

## 4 The traffic data

The CETE of Normandy-Centre has collected for year 2003 an important traffic database on these two French departments: hourly volumes for 32 national road sections and 22 departmental roads, for both directions. CETE estimated hourly patterns for each site.  These 54 counted sections represents 598 km, i.e. 5.5% of the national and departmental networks in Eure and Seine Maritime.

Figure 6 gives the evolution of the hourly traffic volume at Veules les Roses (Departmental Road n° 925, road point 74.4) in Seine Maritime.

The average daily traffic on that section is 5000 vehicles, with a percentage of trucks of 7%.

The (relatively low) standard deviation of the traffic volume for each type of days shows the amount of accuracy on the traffic volume which is lost by aggregation.

The impact of rain on the traffic volume has been studied on urban highways (Chung 2005) and in cities (Khattak, 1997), (Keay and Simmonds, 2005). Chung (2005) for instance found a reduction of 3% of the traffic volume by rain on a Tokyo expressway. Keay and Simmonds found a smaller reduction of 1.3% in Melbourne. Maze Agarwal, Burchett (2006) reviewed the literature and presented recent researches on weather impact on traffic demand, traffic safety, and traffic flow relationships.

However little research is dedicated to rural main and departemental roads. On the network studied in this paper, Saint Pierre et al. (2007) found a reduction of 1% to 2% in the traffic volume.

## 5. The risk and the added-risk due to rain

### Risk and added risk formulas

For a set of road sections A, and for a set of hours hH, let:

be the traffic volume for the hour h on the section r

Qr 	be the total traffic volume on the section for the period H

(w) be the number of accidents for the hour h and weather condition w

be the proportion of the time during the hour h where the weather condition w prevails

Lr	 be the length of the road section r.

The risk (number of accidents by vehicle kilometer for that condition w is:

(5)

The added risk due to rain, noted ρ is the ratio of R(rain)/R(no-rain),i.e.:

(6)

For a set of road kB where the traffic volume Qk is unknown but where the traffic volume pattern can be set to be equal to the traffic pattern of a counted road section r0, and where the weather conditions can be set to the weather conditions valid for the same road section r0, (with known traffic volume Qr0), i.e.

,

though computing the risk R(w) is not possible, it is possible to compute the ratio of the risk for the two weather conditions R(w)/R(w’) (w represents the rain and w’ the normal weather condition):

(7)

with Qk unknown. This quantity Qk which appears in the factor into brakes is not linked to w or w’ and thus disappears in the ratio:

(8)

By assuming that in an area of 40 km around Rouen, the meteorological conditions observed at the meteorological station are valid, (the same for Evreux) we estimated the risk in the rain and the added risk due to rain in a manner which will be described now.

### Determination of the best estimation of rain duration using the accident database

The best probability threshold of cut-off for estimating rain duration via logistic regression can be improved when the traffic database is available.  Indeed, with a few assumptions, we found an additional  relation between ρ, and   b & c, the two numbers of accidents used in formula (1’) corresponding to the mismatches (b when accident data indicates rain whereas the meteorological station indicates no rain, c when accident data indicates no-rain whereas the meteorological station indicates rain).

This additional relation is: ρ= b/c				(9)

This relation was discussed in (Saint Pierre et al., 2007).

When varying the probability threshold, ρ, b and c varies. Only the probability threshold of 0.3 satisfies this equation. However the added risk might be over-estimated since

- the occurrence of a wet road (just after the rain) with a larger number of accidents than on a  dry road implies that the rain exposure obtained through formula (5)  might be under-estimated

- the occurrence of rain when an occident occurs might be over-estimated

Table 5 gives some numerical values of the numbers of accidents and on the numbers of vehicle-kilometers traveled in different conditions

The risk of injury accident in rain per vehicle kilometer –i.e. the ratio between the number of accidents that occurred and the number of vehicle-kilometers traveled during rain on these sections– is equal to 20,8 accidents per 100 millions vehicle-kilometers in rain whereas the risk in no-rain is equal to 9.8. Note that afterwards, to take into account some non-located accidents, 8 accidents in the rain and 35 accidents in no-rain were added, the final risks in the rain and in no-rain are 21.9 and 10.4.

### Added risk estimation

Using aggregated data for the whole of France, P. LeBreton (1990) estimated that the added risk due to rain is 2. Our computation leads to an added risk of 2.1 (on the equipped sections of Haute-Normandie. It increases to 2.4 if considering the accidents located on bends only, bearing in mind the remark on “wet road”: this value is an over estimation of the added risk.

For the part of the network in Haute Normandie which is at less than 40 km from Rouen or Evreux (whatever traffic flow is available or not). The risk cannot be estimated, and only the added risk due to rain can be estimated. Assuming that the percentage of vehicle-kilometers traveled in the rain on these roads is equal to the percentage of vehicle-kilometers traveled in the rain on the 54 equipped sections, the added risk is estimated by the following formula:

(10)

We found Nrain=780 accidents in rain and Nno_rain =3996 accidents in no-rain in the 40 km wide areas near Rouen and Evreux (on all sections, equipped or not with a traffic sensor). The added risk has been estimated at 1.6.

Using the whole set of accidents of Haute Normandie (whatever the distance from Rouen and Evreux is and whatever the traffic flow is available or not) the estimation of added risk is still 1.6. Using table 3 and its odd-ratio estimated to 1.3, the added risk due to rain is estimated at 1.9 on bends and at 1.5 on straight sections.

Shankar also (1995) found a significant relationship between rear-end collision occurrence, rainfall and geometric characteristics of roadway on rural freeway sections.

## 6. Conclusion

Because of the availability of accurate and various weather data, and of a huge traffic volume data set on two French départements (Eure & Seine-Maritime, which together constitute the Haute Normandie region), the knowledge of risk and added-risk due to rain is enhanced. This is useful for road safety management and information for drivers.

The following results were obtained for the period 1997-2003.

On rural roads equipped with traffic sensors and located within a distance of 40 km from the two meteorological stations (Rouen or Evreux), the risk of injury accident in rain –i.e. the ratio between the number of accidents that occurred in the rain and the number of vehicle-kilometers traveled during rain on these sections – is equal to 20.8 accidents per 100 millions vehicle-kilometers, whereas the risk out of rain is equal to 9.8. Consequently, the added risk due to rain is 2.1. On bends, the added risk due to rain is even larger and is estimated at 2.4. However, these added risk values might be over-estimated, and this is due to an overstatement of rain occurrence in the accident database.

On the whole rural roads network (including the roads not equipped with traffic sensors), the risk cannot be computed. When assuming that the proportion of vehicle-kilometers traveled during rain on equipped roads is also valid on non equipped roads, the added risk due to rain on the whole Haute Normandie region is estimated at 1.6 – and more precisely at 1.5 on straight sections and at 1.9 on bends.

## 7. References

Abdel-Aty M.A. and R. Pemmanaboina (2007)  ‘Calibrating a Real-Time Traffic Crash Prediction Model Using Archived Weather and ITS Traffic Data. IEEE Transactions on ITS, Vol. 7, n°2,  pp. 167-174..

Andrey J., B. Mills, M. Leahy and J. Suggett. (2003) Weather as a Chronic Hazard for Road Transportation in Canadian Cities. Natural Hazards, Vol. 28, pp. 319-343.

Aron M., R. Bergel, G. Saint Pierre and E. Violette (2006) Added risk due to rain. Project IRCAD, program SARI, report of WBS 1.6 (in French).

Brodsky H. and S. Hakkert (1988) Risk of road accident in rainy weather. Accident Analysis and Prevention, Vol. 20, n°3,  pp. 161-176.

CETE de Normandie Centre, DESGI (Division exploitation Sécurité Gestion des infrastructures) (2001). Accidents by rainy weather. Drivers behaviour. Bends on two-lanes road/ Departmental road RD928.

Chung, E., Ohtani, O., Warita, H., Kuwahara, M. and Morita, H. (2005).  Effect of rain on travel demand and traffic accident.  8th IEEE Intelligent Transportation Systems Conference, Vienna, Austria.

Eisenberg D. (2004) The mixed effects of precipitation on traffic crashes. Accident Analysis and Prevention, Vol. 36. n°4, pp. 637-647.

Keay, K. and SIMMONDS, I. (2005) The association of rainfall and other weather variables with road traffic volume in Melbourne, Australia. Accident Analysis and Prevention, 37 pp 109-124.

Keay and Simmonds. (2006) Road accidents and rainfall in a large Australian city. Accident Analysis and Prevention, Vol. 38, pp.  445-454.

Khattak, A.J., DePalma, A., (1997). The impact of adverse weather conditions on the propensity to change travel decisions: a survey of Brussels commuters. Transportation Res. A Policy Pract. 31 (3), 181–203.

Le Breton P. (1990) Study of the rain impact on road safety (main roads and motorways). Statistical analysis. Note d’information SETRA-CSTR N° 77.

Lee C., F. Saccomanno and B. Hellinga. (2002) Analysis of Crash Precursors on Instrumented Freeways. In Transportation Research Record 1784, TRB, National Research Council, Washington D.C., Paper n°02- 3790

Maze T.H, Agarwal M.,Burchett G. Whether (2006) Weather Matters To Traffic Demand, Traffic Tafety and Traffic Operations and Flow, TRB, paper 06-0808, Washington

ONISR(2005 )The major themes of road safety - rain (results 1995-2004) (in French) http://www.securiteroutiere.equipement.gouv.fr/IMG/Synthese/Pluie.pdf Accessed July 25. 2006.

Saint Pierre G., M. Aron M., R. Bergel (2007) Reconstruction from various weather-related data sets using logistic regression: methodology and applications, proposed paper n°07-0916, TRB, 2007

Shankar V.N et al. (1995) Effect of roadway geometrics and environmental factors on rural freeway accidents frequencies. Accident Analysis and Prevention, 27 n°3  pp 371-389

Shankar V.N. et al. (2004) l Impacts of Design, Traffic, Weather, and Related Interactions on Roadside Crashes. In Transportation Research Record 1897, TRB, National Research Council, Washington D.C., pp. 156-163.

| Rouen (six years) | Time percentage |
| --- | --- |
| a- normal weather (both sources) | 88,7% |
| b- Rain (only rain gauge) | 1,2% |
| c- Rain (only human observer) | 4,9% |
| d- Rain (both sources) | 5,2% |
| Total | 100,0% |

Table 1. Human and rain gauge weather information at Rouen

| Source | Time scale | Percentage of rainfall periods over the year |
| --- | --- | --- |
|  |  | Rouen | Evreux |
| Rain gauge | Six minutes | 6.1% | 4.5% |
| human observation (Past weather and past weather) | One hour | 10,0% |  |
| Detailed human observation | One minute | 10.1% | 8.3% |
| Reconstructed rain: Probability threshold 0.1 | Six minutes | 15.2 |  |
| 0.2 |  | 14.2 |  |
| 0.3 |  | 11.2% | 8.6% |
| 0.4 |  | 9.7% |  |

Table 2. Measured and reconstructed rain periods at Rouen and Evreux

|  | Number | Percentages |
| --- | --- | --- |
|  | No rain | Rain | Total | No rain | Rain | Total |
| Straight section | 5649 | 1019 | 6668 | 63,1% | 11,4% | 74,5% |
| Bend | 1860 | 424 | 2284 | 20,8% | 4,7% | 25,5% |
| Total | 7509 | 1443 | 8952 | 83,9% | 16,1% | 100,0% |

Table 3. Numbers and frequency of accidents according to weather conditions and infrastructure (on the two départements of Haute-Normandie)

| Distance(km) | No-Rain | Rain | Total |
| --- | --- | --- | --- |
| 5. | 147 | 51 | 198 |
| 10. | 357 | 95 | 452 |
| 15. | 353 | 107 | 460 |
| 20. | 407 | 76 | 483 |
| 25. | 363 | 66 | 429 |
| 30. | 447 | 58 | 505 |
| 35. | 405 | 68 | 473 |
| 40. | 714 | 128 | 842 |
| Total | 3193 | 649 | 3842 |

Table 4. Numbers of accidents by class of distance from Rouen (Source accident database)

| Condition | Accidents | vehicle-kilometer (billions)s |
| --- | --- | --- |
|  | %rain | %No rain | Total number | %Rain | % No rain | Total number |
| Both départements | 16,1% | 83,9% | 8952 | Unavailable |
| 40 km around Rouen or Evreux |  |  | 4776 | Unavailable |
| 40 km around Rouen only | 82,1% | 17,9% | 3842 | Unavailable |
| (*) | 82,9% | 17,1% |  |  |
| 40 km around Rouen or Evreux only on counted stations | 15,6% | 84,4% | 773 | 10.5% | 89.5% | 7.046 |
| (*) | 20,0% | 80% |  |  |  |  |
| 10 km around Rouen or Evreux only on counted stations | 21,6% | 78,4% | 153 | 12,0% | 88,0% | 2,0 |

Table 5.  Accidents and vehicle-kilometres for different areas around Rouen and Evreux according to rain and no-rain conditions from the two sources of weather information on equipped sections in 40 km wide areas around Rouen or Evreux

(*) according to the weather conditions at the meteorological station when the accident occur

Captions to illustrations

Figure 1: Average percentage of rainy time every six minutes of the day for the period 1997-2003.

Figure 2 : Average rainfall height, in millimeters, every six minutes of the day for the period 1997-2003

Figure 3.  Matching weather data (rain gauge of two meteorological stations, according to their distance)

Figure 4 . Frequency of accidents by rainy weather (on the two départements of Haute-Normandie)	19

Figure 5 “Concurrence” between the accident file and various meteorological sources.

Figure 6. Patterns of the hourly traffic volume and of its standard deviation, according to the time in the day and to the type of a day for the VEULES-LES-ROSES station.

###### Figure 1: Average percentage of rainy time every six minutes of the day for the period 1997-2003.

###### Figure 2 : Average rainfall height, in millimeters, every six minutes of the day for the period 1997-2003

###### Figure 3.  Matching weather data (rain gauge of two meteorological stations, according to their distance).

###### Figure 4 . Frequency of accidents by rainy weather (on the two départements of Haute-Normandie)

###### Figure 5 “Concurrence” between the accident file and various meteorological sources.

Figure 6. Patterns of the hourly traffic volume and of its standard deviation, according to the time in the day and to the type of a day for the VEULES-LES-ROSES station.