Simulation Model Development and Analysis of an Unconventional Traffic Circle

Kaan Ozbaya,  Bekir Bartina

Department of Civil and Environmental Engineering, Rutgers, The State University of New Jersey,  NJ  08854 USA

Abstract

This paper deals with the development of a credible and valid simulation model of Clark Circle in New Jersey. Clark Circle is located at exit 135 of Garden State Parkway.

The objectives of this paper is to demonstrate: (1) the validation and calibration steps of developing a credible simulation model of the circle in PARAMICS simulation software, (2) development of location specific gap acceptance models of vehicles using the ground truth data, and (3) the comparison of various operational and geometric alternatives of the circle with respect to the selected measure of effectiveness.

The main concern of the officials is the queue spill back vehicles on to the mainline GSP. Therefore, the selected measure of effectiveness is the probability of a queue spill over on to the mainline. The comparison of various alternative designs is compared based on the reduction of this probability value.

# Introduction

Traffic circles have been used in the United States since 1905. However, their use has been limited since the 1950s owing to the realization that they worked neither efficiently nor safely (NCHRP Report, 2004).  Many existing traffic circles that were designed to handle lower traffic volumes than today's volumes fall under this category of traffic circles that need to be improved, because they are faced with increasing congestion and safety problems. Only in New Jersey 30 of the 67 traffic circles built during the 1920s were replaced until 2001.

Although the replacement of these traffic circles with more efficient facility types appears to be a viable option, time and money needed for the construction of alternative solutions can be prohibitive. The next best option appears to be the implementation of operational alternatives that can extend the life of these circles until they can be rebuilt in the next 10 to 20 years.

Recently, there has been an increasing interest in improving existing traffic circles to address related efficiency and safety problems. Several States are in the process of exploring effective operational alternatives for enhancing the safety and efficiency of the traffic circles that were built in the early 20th century. For example, in recent years, New Jersey Department of Transportation (NJDOT) has been interested in alleviating congestion and increasing safety at three major traffic circles in New Jersey (Ozbay et al., 2005).

Reliable computerized analysis tools can offer invaluable capabilities for assessing the benefits of the operational alternatives for these facilities. Several deterministic and stochastic computer tools now provide extended capacity and delay analysis, and compare various operational alternatives. The choice of the appropriate tool should be based on the scope of the project. Various off-the-shelf computer tools are compared in the Selection of Analysis Tool section.

This paper deals with simulation modeling and analysis of Clark Circle in New Jersey. The novelty of the approach adopted in this simulation modeling study is the use of actual vehicle gap acceptance behavior models. These models were developed using the ground truth data. PARAMICS simulation software is capable of applying these models for individual vehicles at the yield and stop controlled intersections in the circle. The details about the gap acceptance model are given in the Model Validation and Calibration section.

Details of site-specific data are presented in the Simulation Model Development section.  This section also presents the simulation modeling and analysis of Clark Circle using PARAMICS micro simulation software. Simulation Analysis Results section presents the suggested design alternatives for the study circle, and compares their effectiveness in reducing queues in the circle.

# BACKGROUND AND OBJECTIVES

Clark Circle is located at exit 135 of Garden State Parkway (GSP). Traffic congestion at this circle has long been a nuisance for both motorists and businesses in the area. Clark officials considered constructing another exit from the GSP, since exit 135 is the last exit in Union county, and there is not another exit until 4 miles on the southbound direction. However, this proposal has been disputed by the officials of the nearby townships because of the anticipated adverse effects of an additional exit on their neighborhoods. Increased commercial and residential development around the circle is the leading cause of congestion in the facility. Shoprite, Target, Barnes and Noble and other major retailers have been substantial sources of attraction for motorists, and caused increased vehicular demand in and around the circle. The last improvement at the circle was in 1999, which was the expansion of two lanes in the northbound exit at 135, and realignment of the southbound exit (The Star Ledger, 2004).

Figure 1 demonstrates the sketch of Clark Circle and the connecting roadways. Clark Circle is located at the intersection of GSP, Central Avenue, Brent Road and Valley Road. There are 3 yield-controlled intersections and 2 stop-controlled intersections. Traffic coming from Brant avenue, Valley Road, and inside-circle traffic yields to oncoming traffic. These locations are shown by numbers 1, 3 and 4, respectively in Figure 1. Northbound and southbound exits from GSP, denoted by number 2 and 5, respectively make a full stop before merging the circle.

Insert Figure 1 here

The roadways in and around the circle (except the GSP) are two-lane wide, without striping. Therefore, operationally the roadways serve as one lane.

The circle does not have a common operational and geometric design. Priority movements in the circles do not follow modern roundabout operational restrictions. As shown in Figure 1, Clark Circle has an elliptic shape with varying traffic control signs at the approaches and within the circle (location 4). Moreover, the grades at and around the circle vary considerably. For example, GSP sits on a higher elevation than the circle. The circulating traffic within the circle passes through a tunnel under the GSP mainline

After several meetings with the GSP officials, it was identified that the major problem with the Clark Circle is the long queue spillbacks from the circle to the mainline GSP. This is directly related to the stop / yield controlled intersections at the circle entrances. The size of the queue depends on the circulating traffic volume, the traffic volume at the circle entrance and the gap acceptance behavior of vehicles at these intersections.

The objective of this paper is to develop a credible simulation model of the Clark Circle. Ground truth data are collected at the circle to build a validated simulation model of the circle. Details of the simulation model development are presented in the Simulation Model Development section. This model is then used to compare various operational and geometric alternatives based on the reduction in congestion in the circle. There are two design alternatives as suggested by the GSP officials and one design alternative as suggested by the Rutgers Team. The modeling details of these alternatives are also discussed in the Simulation Analysis Results section.

# Selection of Analysis Tool

There are various deterministic tools that can analyze the capacity of roundabouts such as RODEL, aaSIDRA and Highway Capacity Software (HCS). These tools are based on empirical equations that were developed using field data collected at various roundabouts in Britain and Australia. An ongoing project conducted by National Cooperative Highway Research Program is aimed at calibrating the model parameters of aaSIDRA and RODEL based on various roundabouts in the U.S (NCHRP Report, 2004). However, it should be emphasized that microscopic simulation tools such as VISSIM, SYNCHRO, PARAMICS that are commonly used to model roundabouts are too based on empirical models. Therefore, there is not a clear-cut comparison of the reliability of various computer-modeling tools for local conditions. Therefore, regardless of the selected tool, the traffic engineer is responsible for further calibration of the input parameters to ensure the reliability of the predictions of the developed models. S/he should determine the most important variables that affect the efficiency of the facility and improve the model parameters based on actual data, if available.

More importantly, it should be emphasized that the commonly used deterministic tools such as aaSIDRA, HCS, RODEL, are used specifically for roundabouts. They are capable of modeling a limited range of geometric and operational designs. Therefore, they cannot be used for traffic circles, especially for the unconventional ones with unusual geometric and operational characteristics, such as Clark Circle.

PARAMICS is selected for the simulation modeling and analysis of Clark Circle.  PARAMICS is one of the few simulation software packages that can model and analyze such unconventional traffic circles. The use of a microscopic simulation tool offers various analysis capabilities. Instead of analyzing the system as a series of approaches, the system can be evaluated as a complete network. For instance, the signalized and unsignalized intersections located in the vicinity of the circle can be included in the system, and the arrival patterns of the vehicles into the circles can be modeled realistically. The impact of various changes to the operational and geometric designs can be evaluated using vehicle-by-vehicle data not only at the traffic circle, but also at the network level.

Although microscopic simulation tools offer a variety of input-output analysis options, the analyst should still assess and ensure the validity of the model input parameters. Every traffic facility has distinct characteristics whether it is a traffic circle, roundabout, an intersection or a freeway corridor. Extensive validation/calibration efforts might be required when the system is evaluated by using either deterministic or stochastic tools. Regardless of which simulation software is used, the model should be validated and calibrated based on the ground truth data. The extent of these efforts depends on the characteristics of the facility and the scope of the analysis.

The following section presents the steps of a comprehensive simulation analysis.

# Simulation Model Development

This section presents the simulation model development of Clark Circle in PARAMICS micro simulation software. The steps of building a valid and reliable simulation model, as explained in the previous section, are applied in the modeling process. Description of data, and verification, validation / calibration efforts are explained in detail.

## Description of Data

Data collection at the circle was performed on December 7th and 8th 2005, and January 11th and 12th 2006. The circle traffic is recorded from 7 a.m. – 6 p.m.

A portable tower video surveillance system (POGO), and two camcorders were used to collect data at the circle. GSP mainline overpass divides the circle and restricts the visibility of one side of the circle from the other side. Therefore, POGO is located on the east portion of the circle to record Exit 135 northbound entrance and Valley Road and Brant Road entrance. POGO has an extractable mast of 27 feet tall with two dome cameras and two infrared cameras (Figure 2).

Insert Figure 2 here.

Two camcorders were set up on the west side of the circle to record Exit 135 southbound entrance and the inside-circle (location 4 in Figure 1).

Ground truth data were then extracted in the Rutgers Intelligent Transportation Systems Laboratory to obtain (1) traffic volume, (2) inter arrival times of vehicles in the major traffic stream, and (3) vehicles’ gap acceptance behavior at yield and stop controlled intersections in the medium and minor traffic streams.

Vehicle counts and signal timings at the 4 traffic signals in the vicinity of the circle were obtained from Vollmer Associates LLP.

## Model Verification

Model inputs related to infrastructure such as number of lanes, speed limits, signposting distances, barred turns, and jug handles were collected during the site visits. The models were then simulated at varying levels of traffic volume and using different random number streams to observe whether vehicles actually behave reasonably (i.e., correct turns, accepting priority movements at junctions, proper lane changing, using correct lanes while exiting the roadway, etc). This step is crucial in detecting any obvious errors in the model.

PARAMICS is an advanced suite of software tools for microscopic traffic simulation. It is used to model the movement and behavior of individual vehicles on urban and highway road networks. It allows users to customize many features of the underlying simulation model through Application Programming Interface (API) feature of PARAMICS. Figure 3 shows the simulation models of the current design of the circle developed in PARAMICS. The model includes the circle, the GSP mainline, and the surrounding streets and driveways with full operational details. It consists of 141 nodes, 138 links and 28 origin-destination (OD) demand zones (shown by rectangles in Figure 3).

Insert Figure 3 here.

## Model Validation and Calibration

The simulation model is compared with the real world circle via utilizing various tests: (1) subjective tests and (2) objective tests. Subjective tests involve experts of the system who can make judgments about the model and its outputs. Therefore, the developed model were shown to GSP staff and Vollmer Associates in several meetings, and their feedbacks were incorporated in the subsequent steps of the model development. This interactive validation (i.e. face validation) is extremely important in model development because it allows the modeler to incorporate expert judgment, which is not easily attainable. Objective tests require ground truth data to be used in statistical tests to compare various aspects of the system data with the same aspects of the model data set. These statistical tests will be shown in the Simulation Analysis Results section.

### Modeling OD Demand Matrices

The OD demand matrices are extracted using the vehicle routing and vehicle counts at the 4 signalized intersections provided by the Vollmer Associated LLD.  The vehicle routing data include the volume splits from each circle legs to other legs. For example, if the total volume entering the circle from 135 NB entrance is X number of vehicles per hour, the percentage split of X vehicles to Brant road, Valley road, Central Avenue were collected by the Vollmer Associates during their site visits using license plate matching method. Figure 4 shows the vehicle routing data for 135 southbound entrance during the afternoon peak period.

It can be seen in Figure 4 that the vehicle routing data are only for the circle. However, as shown in Figure 4, the simulation model covers a larger area than the circle. Therefore, using the vehicle count data at the 4 signalized intersections located in the vicinity of the circle are used to extract the OD demand matrices for the 18 zones in the simulation model.

Insert Figure 4 here.

### Modeling Inter Arrival Times

Because of its operational design, the operational efficiency of the circle is closely related to the inter-arrival times of vehicles on Central Avenue eastbound and westbound (going through the underpass tunnel) before Exit 135 northbound and southbound entrances, as well as the gap acceptance of vehicles at each five locations in Figure 1. Clearly if the inter-arrival times of vehicles are increased, vehicles at stop and yield controlled locations will have difficulty in finding acceptable gaps to continue. Hence, it is important to run the simulation using correct inter-arrival times and gap acceptance behavior to develop a reliable model.

The shape of the histogram plotted using the inter-arrival data resembles very much that of an exponential probability distribution, but with a rather longer tail. Chi-square and Kolmogorov-Smirnoff tests were used to test the goodness-of-fit of the data, however the Ho hypothesis was rejected at 10% level of significance. It was then realized that the inter-arrival times of vehicle approaching the circle were largely affected by the traffic signals located in the vicinity of the circle. Vehicles arrive at the circle in batches and in certain order.

The signal timing plans of the 4 traffic signals were obtained from Vollmer Associates. These intersections are Central Avenue – Raritan Avenue intersection, Central Avenue and ShopRite Drive, Walnut Avenue – Valley Road intersection, and Brant Avenue – Westfield Avenue intersection. Except Walnut Avenue – Valley Road intersection, all signalized intersections are controlled by vehicle-actuated traffic signals.  These signal timings were coded by using actuated signals feature of PARAMICS.

### Gap Acceptance Models

The gap acceptance behavior of vehicles at uncontrolled intersections was analyzed using binary choice model. There are two choices available to the driver waiting for an acceptable gap: (a) accept the gap and enter to the intersection, or (b) reject the gap and wait for the next available gap. To estimate the gap acceptance probability, a binary probit model is considered. The utility obtained from accepting/rejecting a gap can be decomposed into observed and unobserved parts (Train, 2003).

(1)

where,

n = Index for driver, j = Index for gap acceptance behavior (1 if gap is accepted and 0 if gap is rejected), Unj= Total utility function, Vnj = Observed part of the utility function,  εnj= Unobserved part of the utility function (random error components)

In binary probit model  is assumed to be normally distributed with a mean vector of zero, and a covariance matrix “” which can depend on variables faced by driver n. Then, the probability of accepting a gap can be formulated as  (Ben-Akiva and Lerman, 1985):

(2)

(3)

where, Pn1=Probability of driver n accepts the available gap

and=Standardized cumulative normal distribution

The variables of the probit model are (a) Accept: Dummy variable for acceptance behavior  (1 if the gap is accepted, 0 otherwise) and (b) Gap: Time between consecutive vehicles at the approach (milliseconds).

Gap acceptance/rejection data are extracted in the form of time stamps of vehicle actions at each yield or stop controlled junctions. As a vehicle in the minor traffic stream arrives at a yield or stop sign, its time is recorded using a simple computer script.  The same is repeated as the vehicles in the major traffic stream pass the location, and the vehicle in the minor traffic stream leaves the location. Different keys are assigned to each of these vehicle actions. A MATLAB code is developed to read the data in this format and extract each vehicle’s acceptance and rejection time, wait time, waiting lane index, approaching lane index, etc.

The estimation of the probit model using the extracted data is performed in STATA statistical package (STATA Software Website, 2005). Table 1 demonstrates the results and the model performance of the binary probit models for the circle during morning and afternoon peak periods. The number of observations for each location is also given in Table 1. It should be mentioned that the probability of accepting the null hypothesis that the parameter coefficient is equal to zero is less than 0.01 for all the coefficients in Table 1.

Insert Table 1 here.

It should be mentioned that during the data extraction, it was often difficult to discern the lane indices of vehicles at yield signs and at the approaches for certain locations. There were other variables that were incorporated in the probit model such as the approach lane index, wait time, the frequency of approach vehicles. However, these variables were not statistically significant even at 10% significance level during the morning peak period.  Mahmassani and Sheffi (1981), Polus et al. (2003), Hamed et al. (1997), Shiftan et al. (2003) presented gap acceptance models with significant impact of waiting times on vehicles’ critical gaps. Namely, their estimation results shows that drivers’ average waiting times reduce the average critical gap. This result, however, is not observed in this present study. Teply et al. (1997a) and Teply et al. (1997b) reported that complex gap acceptance models with several variables present a better descriptive and predictive power of capturing the drivers’ behavior. They developed a binary logit model, which considers the nature of opposing traffic such as the type, time gap, space gap, speed of approaching vehicles, and minor traffic characteristics such as queue delay, front delay, and also driver age.  They conclude that gap value only alone can yield reasonable approximations in modeling drivers’ entry behavior for uncontrolled intersections.

The probit models in this study are based on an exhaustive dataset as shown in Table 1. For the probit models developed, 18,570 gap data points were used. Note that this dataset size includes both rejected and accepted gaps. Also note that, for the probit estimation model only the logical gaps are taken into consideration. For example, it is obvious that the probability of accepting a gap of 0.1 second is 0.0. Likewise, the probability of accepting a gap of 15 seconds is 1.0. Therefore, only the gaps that can provide information on how drivers will behave were taken into consideration. This approach was also adopted by Gattis and Low (1999).

The dataset is far more extensive than most of the ones employed in the literature.  For instance, Mahmassani and Sheffi (1981) and Daganzo (1981) used the same dataset of 406 data points for their probit models; Hamed et al. (1997) employed 592 data points for developing a binary probit model; Shiftan et al. (2003) used a dataset of 743 observations to develop a logit model of critical gaps at roundabouts. Teply et al. (1997a) and Teply et al. (1997b) used a dataset of 8,652 gap values with the above-mentioned variables.

### PARAMICS API

PARAMICS API enables users to simulate the site-specific gap acceptance models given in Table 1. Basically, at each time step if the vehicle is within the link that has a yield (such as locations 1, 3 or 4 in Figure 1) or a stop sign (such as location 2 and 5 in Figure 1), the model checks the approach link associated with that sign. It then detects the leading vehicle on the approach link and calculates the approximate time, g, it would take the approaching vehicle to arrive at that location. Thus, for every approaching vehicle the model calculates the probability of accepting the gap g at each location at each simulation time step. While calculating the probability of acceptance, instead of using the mean value of parameter values given in Table 1, a random value from the confidence interval is drawn. In other words, a random number based on a N(0,1) distribution is drawn. Using this random number the value of the parameter is drawn from its confidence interval.  Figure 5 demonstrates the flowchart of the implementation of the gap acceptance models in PARAMICS API.

There is abundant number of studies in the literature that focus on gap acceptance models and critical gaps at uncontrolled intersections and at roundabouts. However, to the best of our knowledge, there are no guidelines on how to implement these models using microscopic simulation tools. For example, at location 2 shown in Figure 1, suppose that the estimated gap is 3 seconds (300 milliseconds). A random value for each parameter of the probit model is drawn from a N(0,1) distribution. Further suppose that these random values for both parameters are 0.5 (So that the mean value of the parameter can be used for the sake of simplicity). Then the Vn1 value can be estimated as -0.88 using the model parameters given in Table 1 for the afternoon peak period. Using the standard normal table this value corresponds to an acceptance probability of 0.19. As mentioned above, there are no guidelines as to how to drive the simulation using this probability value.

A random value between 0 and 1 is drawn using a uniform distribution function, U(0,1). If the random value is greater than the estimated gap acceptance probability, the vehicle is restricted to wait; otherwise it accepts the gap.

Without the gap rejection model developed using API, the default gap rejection model of PARAMICS does not yield realistic entry wait times. Without a location specific gap rejection model it is not possible to model the circle accurately, because the capacity of the circle is closely related to vehicle’s gap rejection times.

Driver characteristics are expected to affect the model considerably. However, it is not possible to gather such extensive individual level data. Thus, during the calibration process aggressiveness, awareness and familiarity of vehicles were modified to be able to obtain simulation outputs close to observed system outputs. This kind of calibration is needed because of the lack of individual driver data.

Insert Figure 5 here.

# Simulation Analysis Results

Average wait times at the selected locations are used as output variables for the simulation model validation. As a direct result of the central limit theorem, it is known that the sampling distributions of the output variables follow a Gaussian distribution with unknown variances regardless of their initial distributions. The model is simulated with independent replications until model outputs attain a confidence level of 95% with a relative error of 5% for all the selected locations. The obtained values of the selected output variables are then used to construct the 95% confidence interval for the population mean using a Student t-distribution. Table 2 presents the simulated and the observed system outputs for the morning and afternoon peak periods for the study circle.

Insert Table 2 here.

Table 2 shows that some of the output ranges do not cover the corresponding observed output values. However, it should be pointed out that the output collection of PARAMICS and the analyst’s data extraction methods are never identical. Furthermore, it can be seen in Table 2 that none of the simulated output values are substantially out of range. Therefore, the outputs of the simulation model can be assumed valid.

Note that without the extensive gap acceptance behavior models of vehicles at the stop and yield controlled intersections, the outputs overestimate the performance of the circle. For example, it is observed that without these parameters, the default PARAMICS model gives an average wait time of 2 seconds for the 135 northbound exit ramp during the morning peak period. Whereas the ground truth data show an average of 6.1 seconds wait time. Similarly, during the afternoon peak period, the default model gives 2.5 seconds of average wait time, while the observed value is 13.7 seconds. It is clear that the default PARAMICS model overestimates the efficiency of the circle. With the use of customized gap acceptance models, the Rutgers team improved the validity of the simulation model.

The alternative design models as suggested by Vollmer Associates, namely Alternative 1 and Alternative 2 were also modeled and analyzed in PARAMICS simulation software (See Figure 6 and Figure 7). However, the signal timings and offsets of the suggested traffic signals at the circle were modeled using PARAMICS instead of SYCHRO. The main reason is due to the fact that the validated/calibrated simulation model in PARAMICS better represents the study facility.

Insert Figure 6 here.

Insert Figure 7 here.

An additional design scenario was also considered by the Rutgers Team. This design is called Alternative A. This design involves the deployment of traffic signals for metering the traffic coming from the GSP to the circle. Note that there are no suggested changes to the geometry of the circle in this scenario. Figure 3 below demonstrates this alternative.

Insert Figure 2 here.

The signal timings of the two suggested traffic signals were modeled using PARAMICS. The signal timings of the two suggested traffic signals are shown in Table 3 and Table 4.

Insert Table 3 here.

Insert Table 4 here.

The main inefficiency of the Clark Circle is the queue spillover from the circle to the GSP mainline. Therefore, the comparison of operational performances for the alternative designs should be based on the percentage reduction in queue spillovers.

PARAMICS API enables users to record the queue lengths at various locations in the network. Queue length can be updated as vehicles join or leave the queue. This feature can be helpful in understanding the effect of various operational alternatives on the average queue length.

For each design scenario, multiple simulations runs were executed to ensure a statistically valid range of output, and the averages of queue lengths were calculated for each scenario. Figure 9 and Figure 10 show the average queue lengths in each scenario for the two off ramps during the morning and afternoon peak periods, respectively. Table 5 shows the percentage reduction in queue spillovers in Alternative 1, Alternative 2 and Alternative A. These results reflect the percentage change in the average queue lengths during the peak period with respect to the current operational design of the circle.

Insert Figure 9 here.

Insert Figure 10 here.

Insert Table 5 here.

It can be seen that all alternatives have substantial benefits in reducing the queue spillover to the mainline. Note that there are negative impacts of Alternative 1 and Alternative A on the 135 southbound queue length. However, the current queue length during the AM peak period is around 20 meters at this location. In these alternative designs, the queue length becomes no more than 30 meters, which does not affect the mainline GSP.

Figure 11 and Figure 12 show the frequency plots of the current 135 northbound exit queue length during the morning and afternoon peak periods.

Insert Figure 11 here.

Insert Figure 12 here.

The analyses based on these frequency plots show that the probability of 135 northbound queue length exceeding 300 meters is 0.13 in the morning peak period, and 0.12 in the afternoon peak period. On the other hand these probabilities decrease down to zero in Alternative 1, Alternative 2 and Alternative A. Similarly, the probability of 135 southbound queue length exceeding 300 meters during the afternoon peak period is 0.11. This probability decreases to zero in Alternative 1, Alternative 2 and Alternative A.

# Summary

Several major difficulties are faced when using traffic simulation for project evaluation. First, this task involves understanding human behavior. The efficiency of traffic networks is largely affected by driver characteristics, as well as infrastructure characteristics. Thus, both in computer modeling of the simulation and in validation steps, the simulation model development becomes quite complicated. Second, and more importantly, while developing a statistically valid simulation model, the analyst must remember that as the size of the network increases, the data requirements increase even more. Because collecting system data is costly and time consuming, most traffic simulation practitioners resort to calibration, which reduces the confidence in model results. However, a slight increase in the available system data increases the model confidence considerably (Sargent, 2000).

Gap acceptance behavior of vehicles in Clark Circle is found to have a dominating impact on the performance of the developed simulation models. It is observed that the default gap acceptance behavior model of PARAMICS fails to simulate the study circles accurately. Extensive field data are required to represent site-specific gap acceptance/rejection behavior of drivers.

The results of the simulation analysis of Clark Circle can be summarized briefly as follows:

The major concern of the current operation of the circle is the queue spillbacks from the circle to the mainline GSP during the peak periods. This is directly related to the vehicles’ gap acceptance behavior at the circle entrances. Extensive data collection and extraction was performed to model the correct traffic volumes and gap acceptance behavior of vehicles.

Two alternative operational and geometric designs were suggested by the Vollmer Associates. Another alternative was also suggested by the Rutgers Team. These alternative designs of the circle were also modeled in PARAMICS. These alternatives were aimed at regulating the traffic within the circle using several traffic signals. The signal timings were obtained using PARAMICS.

The efficiency of the alternatives was compared based on the reduction in queue lengths at the circle entrances from the GSP mainline. It was observed that all of the scenarios substantially reduced the queue lengths as shown in Table 5.

Based on the simulation results, all three alternatives perform satisfactorily in terms of achieving the major goals of this study.  It is important to use the customized the simulation model to further analyze the best alternative in the short and long runs in terms of costs and expected benefits of all three alternatives.

In conclusion, this paper presents a development and analysis of simulation models of the current and proposed designs of Clark Circle using PARAMICS simulation software. The simulation model is validated using ground truth data collected at each circle. The novelty of the analyses presented lies in (1) Statistically valid simulation model development and sensitivity analysis of the circles and (2) The integration of the developed probabilistic gap rejection models at the yield controlled approaches using the API feature of PARAMICS.

# References

- National Cooperative Highway Research Program Report, “NCHRP 3-65: Applying Roundabouts in the United States,” 2004.

- Ozbay, K., List, G., Bartin, B., Rathi, N., Brown, R., Demeris, A. and Wojtowicz, J. “Operational Improvements at Traffic Circles”. New Jersey Department of Transportation Project, 2005.

- The Star Ledger. “Clark looks for help to ease traffic jams.” February 1, 2004.

- Train K. “Discrete Choice Methods with Simulation”, Cambridge University Press, 2003.

- Ben-Akiva, M. and Lerman S., “Discrete Choice Analysis: Theory and Application to Travel Demand”, MIT Press, Cambridge Mass., 1985.

- STATA Software Website (2005) http://www.stata.com/products/overview.html

- Mahmassani, H. and Sheffi, Y. (1981). “Using gap accepance sequences to estimate gap acceptance functions,” Transportation Research Part B, Vol 15B, pp. 143-148.

- Polus, A., Lazar, S. S. and Livneh, M. (2003), “Critical gap as a function of waiting time in determining roundabout capacity.” Journal of Transportation Engineering. September/October

- Hamed, M.M., Easa, S. M. and Batayneh, R.R. (1997). “Disaggregate gap-acceptance model for unsignalized T-intersections” Journal of Transportation Engineering, January/February.

- Shiftan, Y., Polus, A. and Lazar-Shmueli, S. (2003). “Evaluation of the waiting-time effect on critical gaps at roundabouts by a logit model,” Presented at the 82nd Annual Transportation Research Meeting, Washington D.C.

- Gattis, J. L. and Low, S., (1999). “Gap acceptance at atypical stop-controlled intersections.” Journal of Transportation Engineering. May/June.

- Teply, S., Abou-Henaidy, M. and Hunt, J. D. (1997) “Gap acceptance behavior – aggregate and logit perspectives: Part 1.” Traffic Engineering and Control. Vol. 37. No.9, pp. 474-482.

- Teply, S., Abou-Henaidy, M. and Hunt, J. D. (1997) “Gap acceptance behavior – aggregate and logit perspectives: Part 2.” Traffic Engineering and Control. Vol. 37. No.9, pp. 544-544.

- Daganzo, C. (1981). “Estimation of gap acceptance parameters within and across the population from direct roadside observation” Transportation Research Part B, Vol 15B, pp. 1-15.

- Sargent, R. G. Verification, Validation and Accreditation of Simulation Models, Proceedings of the 2000 Winter Simulation Conference, 2000.

Table 1. Results of Gap Acceptance Binary Probit Model

|  |  | Clark Circle morning peak probit model |  |  |
| --- | --- | --- | --- | --- |
| Location | Variable | Coefficient | Number of Observations | Std. Err. | z | Log Likelihood | Pseudo R2 |
| 1 | Constant (α) | -3.2997 | 1230 | 0.1301 | -24.27 | -416.51 | 0.52 |
|  | Gap (g) | 0.0112 |  | 0.0004 | 24.50 |  |  |
| 2 | Constant | -3.3750 | 1620 | 0.1418 | -23.79 | -397.81 | 0.58 |
|  | Gap | 0.0098 |  | 0.0005 | 20.24 |  |  |
| 3 | Constant | -3.2149 | 1603 | 0.1303 | -24.68 | -465.55 | 0.53 |
|  | Gap | 0.01185 |  | 0.0005 | 21.97 |  |  |
| 4 | Constant | -2.1412 | 966 | 0.1358 | -15.76 | -336.69 | 0.49 |
|  | Gap | 0.0083 |  | 0.0005 | 15.18 |  |  |
| 5 | Constant | -1.5095 | 2016 | 0.0828 | -18.22 | -636.11 | 0.49 |
|  | Gap | 0.0050 |  | 0.0003 | 19.93 |  |  |
|  |  | Clark Circle Afternoon peak probit model |  |  |
| Location | Variable | Coefficient | Number of Observations | Std. Err. | z | Log Likelihood | R2 |
| 1 | Constant (α) | -3.5998 | 1834 | 0.1405 | -25.63 | -499.37 | 0.58 |
|  | Gap (g) | 0.0123 |  | 0.0005 | 23.53 |  |  |
| 2 | Constant | -3.8822 | 1964 | 0.1591 | -24.40 | -329.75 | 0.55 |
|  | Gap | 0.0100 |  | 0.0005 | 19.52 |  |  |
| 3 | Constant | -4.0332 | 3519 | 0.0140 | -34.80 | -763.04 | 0.61 |
|  | Gap | 0.0139 |  | 0.0004 | 31.16 |  |  |
| 4 | Constant | -3.4464 | 1556 | 0.1474 | -23.38 | -436.87 | 0.57 |
|  | Gap | 0.0113 |  | 0.0005 | 21.56 |  |  |
| 5 | Constant | -3.7274 | 2262 | 0.1393 | -26.77 | -551.48 | 0.63 |
|  | Gap | 0.0089 |  | 0.0004 | 25.30 |  |  |

Table 2. Comparison of Simulated and Observed Entry Wait Times

|  | Morning Peak Period | Afternoon Peak Period |
| --- | --- | --- |
| Location | Simulated | Observed | Simulated | Observed |
| 1 | [2.66,2.96] | 3.20 | [3.21,3.41] | 4.03 |
| 2 | [6.13,6.71] | 6.14 | [11.5,12.9] | 13.68 |
| 3 | [4.66,5.33] | 4.55 | [4.72,5.36] | 5.80 |
| 4 | [2.20,2.43] | 2.15 | [3.89,4.45] | 4.34 |
| 5 | [2.34,3.20] | 2.03 | [5.05,5.59] | 5.06 |

Table 3. Traffic signal timings in the morning peak period

| Phase | Direction | Time (seconds) |
| --- | --- | --- |
| A. | 135 Northbound | 18 |
|  | Change | 1 |
|  | Clearance | 1 |
| B. | Circulating traffic | 38 |
|  | Change | 1 |
|  | Clearance | 1 |
| Phase | Direction | Time (seconds) |
| A. | 135 Southbound | 21 |
|  | Change | 1 |
|  | Clearance | 1 |
| B. | Circulating traffic | 35 |
|  | Change | 1 |
|  | Clearance | 1 |

Table 4. Traffic signal timings in the afternoon peak period

| Phase | Direction | Time (seconds) |
| --- | --- | --- |
| A. | 135 Northbound | 9 |
|  | Change | 4 |
|  | Clearance | 1 |
| B. | Circulating traffic | 44 |
|  | Change | 1 |
|  | Clearance | 1 |
| Phase | Direction | Time (seconds) |
| A. | 135 Southbound | 21 |
|  | Change | 1 |
|  | Clearance | 1 |
| B. | Circulating traffic | 35 |
|  | Change | 1 |
|  | Clearance | 1 |

Table 5. Percentage reduction in queue spillovers at exit ramps

|  | 135 Northbound | 135 Southbound |
| --- | --- | --- |
|  | AM peak | PM peak | AM peak | PM peak |
| Alternative 1 | 68.6 % | 83.9 % | -16.6 % | 83.2 % |
| Alternative 2 | 78.1 | 84.4 | 6.3 | 84.2 |
| Alternative A | 65.9 | 63.5 | -38.2 | 61.2 |

Captions for Illustrations

Figure 1. A sketch of Clark Circle

Figure 2. Portable tower video surveillance system (POGO)

Figure 3. Clark Circle PARAMICS model

Figure 4. Vehicle Routing Data for 135 Southbound Entrance

Figure 5. PARAMICS API Gap acceptance/ rejection flowchart

Figure 6. Alternative 1

Figure 7. Alternative 2

Figure 8. Alternative A

Figure 9. Average queue lengths during the morning peak period

Figure 10. Average queue lengths during the afternoon peak period

Figure 11. Frequency plot of 135 northbound queue lengths during morning peak

Figure 12. Frequency plot of 135 northbound queue lengths during afternoon peak

# Text boxes

5

4

3

2

1

##### GSP

SB

##### GSP

NB

##### Brant Avenue

##### Valley Road

##### Garden State Parkway

##### Central Avenue