TRANSIT-BASED SMART PARKING:

A BEFORE-AND-AFTER EVALUATION OF FIELD TEST RESULTS

Caroline J. Rodier, Ph.D. and Susan A. Shaheen, Ph.D.

Caroline J. Rodier, Ph.D.

Assistant Research Engineer, California PATH

University of California, Berkeley

1357 S. 46th Street, Bldg 190; Richmond, CA 94804-4648;

##### 510-665-3467 (O); 916-451-8188 (F); cjrodier@path.berkeley.edu

and

##### Susan A. Shaheen, Ph.D

Honda Distinguished Scholar in Transportation, University of California, Davis &

Policy & Behavioral Research Program Leader, California PATH,

University of California, Berkeley;

1357 S. 46th Street, Bldg 190; Richmond, CA 94804-4648

510-665-4648 (O); 510-665-3537 (F); sashaheen@path.berkeley.edu

TRANSIT-BASED SMART PARKING:

A BEFORE-AND-AFTER EVALUATION OF FIELD TEST RESULTS

###### ABSTRACT

This paper presents an early exploratory analysis of participant surveys results from a transit-based smart parking field test in the U.S. at the Rockridge BART station in Oakland, California. The results suggest possible effects of the field test on participant commute travel behavior including: (1) increased transit mode share and drive access to BART stations; (2) reduced drive alone mode, carpooling, and bus mode share; and (3) decreased average commute time and total VKT.

ACKNOWLEDGEMENTS

The authors would like to thank the California Department of Transportation, California PATH, the BART District, ParkingCarmaTM, Quixote Corporation, Intel, and Microsoft for their generous contributions to the smart parking program. The Institute of Transportation Studies-Berkeley faculty, staff, and students also deserve special credit for their assistance with smart parking project (between 2002 and 2006), including Martin Wachs, Linda Novick, Elliot Martin, Amanda Eaken, Megan Smirti, Joshua Seelig, and Jade Benjamin-Chung. The contents of this report reflect the views of the authors, who are responsible for the facts and the accuracy of the data presented herein.

KEY WORDS: Parking management, travel behavior, intelligent transportation systems

INTRODUCTION

In suburban areas, quick convenient auto access to park-and-ride lots can be essential to making transit competitive with the auto. Most people will only walk about one quarter of a mile to transit stations or stops, and fixed route bus or shuttle feeder services can be expensive and less convenient than the auto. Smart parking management technologies may provide a cost-effective tool to address near-term parking constraints at transit stations. Smart parking can be defined broadly as the use of advanced technologies to help motorists locate, reserve, and pay for parking. Smart parking management systems have been implemented in numerous European, British, and Japanese cities to more efficiently use parking capacity at transit stations. These smart parking systems typically provide real-time information via changeable message signs (CMS) to motorists about the number of available parking spaces in park-and-ride lots, departure time of the next train, and downstream roadway traffic conditions (e.g., accidents and delays).

A review of the literature suggests that parking shortages at suburban rail stations may significantly constrain transit ridership (Merriman, 1998; Ferguson, 2000). Thus, more effective use of station parking may increase transit use and revenues. In addition, motorists may respond to pre-trip and en-route information on parking availability at transit stations by increasing their transit use (Ferguson, 2000). Finally, regular commuters appear to be more responsive to parking information in conjunction with transit than more basic parking guidance systems because this type of real-time information has greater relevance to their commute trip (e.g., transit station parking availability, next train information, and/or roadway accident downstream) (Rodier, Shaheen, and Eaken, 2004).

To evaluate the effectiveness of transit-based smart parking, public and private partners jointly launched a field operational test at the Rockridge Bay Area Rapid Transit (BART) District station in Oakland, California, on December 8, 2004. In the San Francisco Bay Area, peak hour parking at most of the 31 suburban BART District stations has recently been at or near capacity. This field test was the first transit-based smart parking system implemented in the U.S.; however, since its launch two other transit-based smart parking systems are planned—one at the Glenmont Metro Station in Montgomery County, Maryland, and two at Chicago Metra stations in Illinois.

This paper presents the results of an early exploratory analysis of post smart parking participant surveys and suggests possible effects of the smart parking field test on participant commute travel behavior, including changes in transit ridership, auto access to transit, and vehicles kilometers traveled (VKT). This paper begins with a general review of the literature on smart parking. Next, the smart parking field test is described, surveys results are then discussed, and conclusions are drawn from the analysis.

Transit-Based Smart Parking Field Test: San Francisco Bay Area

To evaluate the feasibility of the smart parking concept in a transit context, the California Department of Transportation, the BART District, California Partners for Advanced Transit and Highways (PATH), Acme Innovation Inc.’s ParkingCarma(, Quixote Corporation, Intel, and Microsoft jointly launched a smart parking field test at the Rockridge BART station in Oakland, California, on December 8, 2004. BART provided 50 spaces to be used in the field test.

The Rockridge BART smart parking field test involved two real-time user interfaces: 1) two CMSs that displayed parking availability information to motorists on an adjacent commute corridor into downtown Oakland and San Francisco (Highway 24), and 2) a centralized intelligent reservation system that permitted commuters to check parking availability and reserve a space via telephone, mobile phone, Internet, or PDA. Those who used the system for en-route reservations called in their license plate number via mobile phone when they parked in the smart parking lot. BART enforcement personnel ensured that those parking in the smart parking lot either had: 1) an advanced reservation parking permit or 2) a license plate number, which matched one of the numbers provided real-time to enforcement personnel via PDA, for en-route reservations.

The smart parking system integrated traffic count data from entrance and exit sensors at the BART station parking lot with an intelligent reservation system to provide accurate up-to-the-minute counts of parking availability. Smart parking facilitated pre-trip planning by permitting users to reserve a space up to two weeks in advance, but it also enabled en-route decision making, providing real-time parking availability information to encourage motorists to use transit. If a motorist confronted congestion on Highway 24, she could check parking availability on the CMS and drive off of the freeway and park in the smart parking area at the Rockridge BART station. Reservations were initially free of charge. A pricing structure was introduced for both types of parking reservations in October 2005. Users who made en-route reservations were charged $1.00 for this service, while those making pre-trip reservations were charged $4.50. The smart parking field test ended on April 7, 2006. To the authors’ knowledge, this smart parking system, integrating real-time traffic sensor data from a transit station parking lot with a web-based reservation system and two CMSs on an adjacent highway, was the first of its kind. Similar transit-based systems in Europe and Japan provide motorists with en-route information, but the literature suggests that there is no other program that currently enables both pre-trip planning (via a web-based reservation system) and en-route planning (through real-time parking information on CMSs on highways).

INSERT FIGURE 1 ABOUT HERE

The smart parking field test was the first transit-based program implemented in the U.S., but two other transit-based systems are currently nearing implementation in conjunction with the Chicago Metra Commuter Rail system and the Washington, D.C. Metro. In Chicago, the system under development plans to collect real-time data to provide en-route information via CMSs to travelers about parking availability, the location of parking spaces in large lots or garages, departure times for the next train, and advice to use transit when alternate roadway routes are congested (Kopp, Havinoviski, Scheuring, and Johnston, 2001). Northeastern Illinois’ Regional Transportation Authority, Metra Commuter Rail Division, and the Illinois Department of Transportation in the Gary-Chicago-Milwaukee corridor are sponsoring the project (Orski, 2003). This system includes electronic guidance signs located along expressways and arterials that lead up to commuter rail stations to provide real-time information for motorists on the availability of parking (Orski, 2003). In addition, a “Smart Park” project has been proposed in Montgomery County, Maryland, at the Glenmont station of the Washington, D.C. Metro system. This project plans to incorporate video cameras in park-and-ride lots to encourage drivers to use the spillover parking lot, with the goal of decreasing parking search time and congestion. The Federal Transit Administration will be evaluating the effectiveness of both these systems with respect to increased transit use and passenger satisfaction.

SURVEY AND RESULTS

The analysis presented here is based on 177 surveys completed by participants in the smart parking field test in February and March 2006, after the implementation of the smart parking field test. Approximately 35.8% of field test participants who used the system with some regularity (i.e., more than one time) completed the voluntary survey. The survey was designed to gauge respondents’ demographic and employment attributes and commute travel pattern changes. The validity of the analysis of the survey results may be affected by errors due to sample size, self-reporting, and variation in interpretation.

Demographic and Employment Attributes

Table 1 describes the demographic attributes of survey respondents. Respondents’ ages are fairly evenly divided over the range of 31 to 60 years. Generally, they are highly educated and no respondent have less than a high school education. They also have a relatively high-income level. The most common household type includes one or two adults with a child or children. The demographic distribution of respondents to this survey is relatively consistent with that of all field test participants who used the system with some regularity (i.e., more than one time) (less than five percentage points).

The survey also examined the attributes of participants’ employment. More than half of the respondents are not required to be at work at a certain time (57.1%). However, despite the potential opportunity to work flexible hours, it seems that most respondents work during regular business hours, five days per week. More than half (53.7%) work more than 40 hours per week, and most work five days a week (81.4%). Free employer provided parking is rarely provided to respondents at their place of work and off-site work locations.

INSERT TABLE 1 ABOUT HERE

Primary Commute Mode

Table 2 describes participants’ modal shares, and for those who use BART, the access mode shares by frequency of use. Across frequencies, BART is the primary long-haul commute mode (67.8%), followed by driving alone (17.0%), and then carpooling and bus (11.3%). Over half (54.8%) of respondents, across frequencies, take BART as their commute mode three or more days per week. Driving alone is the most common BART access mode (83.7%), followed by carpooling and bus (13.5%), and walking and biking (2.7%).

INSERT TABLE 2 ABOUT HERE

Smart Parking Use

Figure 2 presents the frequency of smart parking and BART use by respondents to travel to their on-site and/or off-site work location. Most respondents used smart parking to travel to their on-site work location one to three days per month. Close to half of respondents used smart parking to travel to off-site work locations with some frequency. The majority of survey respondents used smart parking and BART for on-site or off-site work trips (88.7%) and the remaining (11.3%), used the service for other trip purposes, such as shopping or volunteering.

INSERT FIGURE 2 ABOUT HERE

## Change in Commute Modal Shares

The survey asked participants to state how frequently they used smart parking and BART to commute to work both at their place of work and to off-site work locations (e.g., client meetings). Survey respondents were also asked, if smart parking at BART was not available, what mode they would typically use to commute. If respondents indicated that they would still use BART, even without smart parking, they were asked how they would travel to the BART station in the absence of smart parking.

For commute to place of work, Table 3 presents the results of a cross tabulation of the responses to the following questions:

- How frequently do you use smart parking to commute to your place of work?

- If smart parking were not available, how would you commute to your place of work?

Also for commute to place of work, Table 4 presents the results of a cross tabulation of responses among those who indicated that they would commute by BART with and without smart parking to the following questions:

1) How frequently do you use smart parking to commute to your place of work (only respondents who would take BART with or without smart parking)?

2)  If smart parking were not available, how would you commute to your place of work (only respondents who would take BART with or without smart parking)?

Tables 5 and 6 are the same as 3 and 4, respectively, except that commute travel is to the off-site work location.

Across frequencies, the survey results suggest that smart parking encouraged 30.8% of respondents to use BART instead of driving alone to their on-site work location and 13.3% to divert to BART from carpooling (Table 3). Smart parking may have also increased drive alone access to the BART station; 14.3% of users, across frequencies, drove alone and parked at the BART station instead of taking the bus or using non-motorized modes (Table 4). On average, smart parking respondents (n = 143) increased BART use by 5.5 trips per month for on-site work commutes.

INSERT TABLES 3 AND 4 ABOUT HERE

The survey results suggest that more respondents, across frequencies, shifted commute modes from drive alone to smart parking and BART when commuting to off-site work locations compared to on-site work locations (Table 5). It appears that given the availability of smart parking, 55.9% of users, across smart parking frequencies, shifted their long-haul commute mode from drive alone to BART for off-site work commutes (Table 5). Again, smart parking may have encouraged some users to access the BART station by auto instead of taking the bus or walking (15.3%) (Table 6). On average, those who used smart parking to access their off-site work location (n = 75) appear to have increased BART use by four trips per month.

INSERT TABLES 5 AND 6 ABOUT HERE

The smart parking service likely improved auto accessibility to the Rockridge BART station and thus may have encouraged some respondents (11.2%) to use this station instead of one that was closer or farther from their home. Among these 16 respondents, 62.5% traveled further, and 37.5% traveled a shorter distance to the Rockridge station from the station they had used previously.

Change in Travel Time

Smart parking appears to have decreased time spent commuting for respondents. Overall, the survey results suggest that for participants who used smart parking with some frequency to travel to their on-site work location, commute minutes per month dropped from 43,652 to 40,394 minutes per month. Using a paired sample T-test for dependent samples, it was determined that there was a statistically significant difference (p = 0.002) in commute time to work using smart parking and BART (47.5 minutes) in comparison to commute time to work if smart parking at BART was not available (50.1 minutes). This result suggests that the availability of smart parking at BART contributed to decreased commute times.

## Change in Vehicle Miles Traveled

A number of factors affected the may have influenced VKT commute change to on-site work locations for field test participants:

- Riding BART as their primary mode instead of driving alone;

- Driving to BART instead of taking the bus, walking, or biking; and

- Driving to Rockridge to access smart parking instead of driving to a BART station that was closer to or farther from their home.

Those who indicated a change in commute mode from drive alone to BART, a change in access mode from a non-motorized mode to drive alone, and a change in primary BART station are shown in Table 7. The change in VKT was calculated by multiplying each user’s one-way VKT by the frequency per month of their commute method with and without smart parking and then taking the difference between these two values. It is estimated that an average participant reduced their monthly VKT by 15.6 miles. Approximately 33% of the reduction in VKT was offset by an increase in drive access mode to the BART station and driving further to the Rockridge BART station instead of a BART station closer to home. This distance calculation uses home and work zip codes.

###### INSERT TABLE 7 ABOUT HERE

CONCLUSION

In this paper, the authors presented the commute travel effects of the first transit-based smart parking project in the U.S. at the Rockridge BART station in Oakland, California. The following are the general trends suggested from this exploratory analysis of participant survey travel results: (1) increased transit mode share and drive access to BART stations; (2) reduced drive alone mode, carpooling, and bus mode share; (3) decreased average commute time and total VKT.

References

Ferguson, E. (2000) ‘Parking Management And Commuter Rail: The Case Of Northeastern Illinois’, Journal of Public Transportation, 3(2), pp. 99-121.

Kopp, J.C., Havinoviski, G. N., Scheuring, G. and Johnston, A. (2001) ‘Real Time Parking Management dor Transit Stations’. Preprint. Transportation Research Board of the National Academies, Washington D.C, 2001.

Merriman, D. (1998) ‘How Many Parking Spaces Does It Take to Create One Additional Transit Passenger?’, Regional Science and Urban Economics, 28, pp. 565-584.

Orski, K (2003) ‘Best Space Scenario’, Traffic Technology International, February/March, 2003, pp. 54-56.

Rodier, C., Shaheen, S. and Eaken, A. (2004) ‘Transit-Based Smart Parking in the San Francisco Bay Area: an Assessment of User Demand and Behavioral Effects’. Publication UCB-ITS-RR-2004-7. Institute of Transportation Studies, University of California, Berkeley, 2004.

##### TABLE 1  Demographic Attributes

| Age (n = 177) | Percent |
| --- | --- |
| 0 – 30 | 9.0% |
| 31 – 40 | 30.5% |
| 41 – 50 | 26.6% |
| 51 – 60 | 27.7% |
| 61 – or older | 6.2% |
| Household Structure (n = 176) | Percent |
| Self only | 20.5% |
| Self with spouse/partner only | 31.8% |
| Self with or without spouse/partner and child(ren) | 40.3% |
| Self with roommate(s) or other | 7.4% |
| Education (n = 177) | Percent |
| Graduate/Professional | 57.1% |
| College | 41.8% |
| High School | 1.1% |
| Income (n = 154) | Percent |
| Under $49,999 | 7.1% |
| $50,000 - $79,999 | 13.6% |
| $80,000 - $109,999 | 19.5% |
| $110,000 or more | 59.7% |

Total income categories sum to 99.9% rather than 100% due to rounding error.

##### TABLE 2  Primary Commute Mode and BART Station Access Mode

| Mode Shares by Frequency of Use |
| --- |
| Primary (n = 177) | BART | Drive Alone | Carpool/Bus | Other | Total |
| Less than 1 day a week | 6.8% | 0.6% | 0.0% | 0.0% | 7.4% |
| 1 to 2 days a week | 6.2% | 2.3% | 0.0% | 0.6% | 9.1% |
| 3 to 4 days a week | 29.4% | 6.8% | 7.9% | 1.7% | 45.8% |
| 5 or more days a week | 25.4% | 7.3% | 3.4% | 1.7% | 37.8% |
| Total | 67.8% | 17.0% | 11.3% | 4.0% | 100.1% |
| BART Access Mode Shares by Frequency of Use |
| Primary (n = 110) | Drive Alone & Park | Carpool/Bus | Walk/Bike | Total |
| Less than 1 day a week | 7.2% | 0.9% | 0.0% | 8.1% |
| 1 to 2 days a week | 9.9% | 0.0% | 0.0% | 9.9% |
| 3 to 4 days a week | 36.0% | 7.2% | 0.9% | 44.1% |
| 5 or more days a week | 30.6% | 5.4% | 1.8% | 37.8% |
| Total | 83.7% | 13.5% | 2.7% | 99.9% |

Total mode shares by frequency of use sum to 100.1% rather than 100% due to rounding error.

Total BART access mode shares, by frequency of use, sum to 99.9% rather than 100% due to a rounding error.

TABLE 3  Cross Tabulation of Stated Frequency of Smart Parking/BART Use by Commute Mode Used if Smart Parking is Not Available To Your On-Site Work Location

| If smart parking were not available, how would you commute to your place of work? | How frequently do you use smart parking to commute to on-site work? |
| --- | --- |
|  | < 1 day per month | 1-3 days per month | 1-2 days per week | 3-4 days per week | 5 days per week | Total |
| BART (without smart parking) | 11.9% | 10.5% | 11.9% | 10.5% | 6.3% | 51.1% |
| Drive Alone | 12.6% | 9.1% | 6.3% | 2.1% | 0.7% | 30.8% |
| Carpool | 1.4% | 6.3% | 1.4% | 2.1% | 2.1% | 13.3% |
| Bus | 0.7% | 2.1% | 0.7% | 0.0% | 0.0% | 3.5% |
| Walk | 0.0% | 0.7% | 0.7% | 0.0% | 0.0% | 1.4% |
| Total | 26.6% | 28.7% | 21.0% | 14.7% | 9.1% | 100.1% |

Total commute mode to on-site place of work sums to 100.1% rather than 100% due to rounding error.

TABLE 4  Cross Tabulation of Stated Frequency of Smart Parking/BART Use of Those Respondents Who Would Have Used BART Without Smart Parking (First Row Of Table 3) by Station Access Mode if Smart Parking is Not Available To Your On-Site Work Location

| If you would use BART without smart parking, how would you travel to the BART station? | How frequently do you use smart parking to commute to on-site work? |
| --- | --- |
|  | < 1 day per month | 1-3 days per month | 1-2 days per week | 3-4 days per week | 5 days per week | Total |
| Drive Alone & Park in regular parking area | 17.4% | 15.9% | 21.7% | 15.9% | 11.6% | 82.5% |
| Walk/Bike | 4.3% | 4.3% | 1.4% | 2.9% | 0.0% | 12.9% |
| Driven as passenger | 0.0% | 0.0% | 0.0% | 1.4% | 1.4% | 2.8% |
| Bus | 1.4% | 0.0% | 0.0% | 0.0% | 0.0% | 1.4% |
| Total | 23.1% | 20.2% | 23.1% | 20.2% | 13.0% | 99.6% |

Total BART access mode to on-site place of work sums to 99.6% rather than 100% due to rounding error.

TABLE 5  Cross Tabulation of Stated Frequency of Smart Parking/BART Use by Commute Mode Used if Smart Parking is Not Available To Your Off-Site Work Location

| If smart parking were not available, how would you commute to your place of work? | How frequently do you use smart parking to commute to off-site work? |
| --- | --- |
|  | < 1 day per month | 1-3 days per month | 1-2 days per week | 3-4 days per week | 5 days per week | Total |
| BART (without Smart parking) | 21.3% | 12.0% | 0.0% | 1.3% | 1.3% | 35.9% |
| Drive Alone | 29.3% | 20.0% | 5.3% | 0.0% | 1.3% | 55.9% |
| Carpool | 4.0% | 1.3% | 0.0% | 0.0% | 0.0% | 5.3% |
| Bus | 1.3% | 0.0% | 0.0% | 0.0% | 0.0% | 1.3% |
| Walk | 1.3% | 0.0% | 0.0% | 0.0% | 0.0% | 1.3% |
| Total | 57.2% | 33.3% | 5.3% | 1.3% | 2.6% | 99.7% |

Total commute mode to off-site work location sums to 99.7% rather than 100% due to rounding error.

TABLE 6  Cross Tabulation of Stated Frequency of Smart Parking /BART Use of Those Respondents Who Would Have Used BART Without Smart Parking (First Row Of Table 5) by Station Access Mode if Smart Parking is Not Available To Your Off-Site Work Location

| If you would use BART without smart parking, how would you travel to the BART station? | How frequently do you use smart parking to commute to off-site work? |
| --- | --- |
|  | < 1 day per month | 1-3 days per month | 3-4 days per week | 5 days per week | Total |
| Drive Alone & Park in regular parking area | 46.2% | 30.8% | 3.8% | 3.8% | 84.6% |
| Walk | 11.5% | 0.0% | 0.0% | 0.0% | 11.5% |
| Bus | 0.0% | 3.8% | 0.0% | 0.0% | 3.8% |
| Total | 57.7% | 34.6% | 3.8% | 3.8% | 99.9% |

Total BART access mode to off-site work location sums to 99.9% rather than 100% due to rounding error.

## TABLE 7  Change in Vehicle Miles Traveled with Smart Parking

| Reason for Behavioral Change | Effect on Total VKT | Change in VKT Per Month Due to Change |
| --- | --- | --- |
| Modal shift from drive alone to BART (n = 143) | Decrease | 3352.1 VKT total 19.0 VKT per person |
| Access mode shift to BART from bus, carpool, walk, or bike to driving alone (n = 69) | Increase | 555.2 VKT total 8.0 VKT per person |
| Shift to smart parking at Rockridge BART station from another station closer to or farther from home (n = 16) | Increase | 551.8 VKT total 34.4 VKT per person |

FIGURE 1  Images of smart parking field test.

FIGURE 2  Frequency of smart parking use.