Simulating bus priority system for an urban corridor in Mumbai City

By

Jigesh N. Bhavsar,

Deputy Manager,

Traffic & Transportation Division,

I.C.T. Pvt. Ltd., A-8 Green Park,

New Delhi 110016

Email: jnbhavsar@ictonline.com

Sushant Sharma

Research Scholar

Indian Institute of Technology Bombay

India, Mumbai-400076

P: +91-22-2576-7349

F: +91-22-2576-7302

Email: sushantsharma@iitb.ac.in

Prof. S L Dhingra

Professor of Civil Engineering

Indian Institute of Technology Bombay

India, Mumbai-400076

P: +91-22-2576-7329

F: +91-22-2576-7302

Email: sl.dhingra@gmail.com

Simulating bus priority system for an urban corridor in Mumbai City

Jigesh N. Bhavsar+   Sushant Sharma* S. L. Dhingra*

+I.C.T. Pvt. Ltd., A-8 Green Park, New Delhi 110016

*Civil Engineering Department, I.I.T., Powai, Mumbai 400076

# Abstract

Inefficient management of public transportation has led to increase in the travel times for public transport and increase in number of private vehicle users. This condition implies the need of improving the public transit performance. High Capacity Bus System (HCBS) is one of the measures which can drastically improve the performance for public transportation. This includes providing exclusive lanes and traffic signal priority to buses. The aim of this study is to carry out simulation study on Western Express Highway for estimating travel time benefits, due to provision of exclusive bus lane with various alternatives and to evaluate change in delay to non-priority vehicles at intersection due to signal priority to the buses traveling on exclusive bus lane, using simulation package VISSIM 4.0. A study corridor was selected in such a way that it covers all the major types of intersections, level intersection, non-signalized intersections and a pedestrian crossing. Necessary data was collected like turning movement at intersections, delay, spot speed, signal timings, and time headways on the selected study corridor on Western Express Highway, Mumbai (India). Video recording was done at a mid-block stretch to get volume, spot speed and time headway of vehicles. The study corridor was simulated without exclusive bus lane to represent the existing road network with various input parameters obtained from data collection and analysis. Simulation of the corridor was done with software package VISSIM4. Model validation was done by comparing simulated headways with the observed ones at a mid-block. Comparing the travel time of present bus system with the articulated bus traveling on bus lane shows a significant reduction in travel time. This may attract many private vehicle users towards the proposed high capacity bus system. The increase in delay to non-priority vehicles at intersections is decisive in understanding the feasibility of signal priority to buses, and to choose a reasonable frequency of buses traveling in the lane.

Keywords: High Capacity Bus System, Simulation, Bus Priority.

1. Introduction

The current bus transit system in Mumbai, known as BEST (Brihan Mumbai Electricity Supply & Transport), is catering about 4.5 million commuters per day, which is about 40% of the total commuters in the Mumbai city. But this transit system is becoming inadequate to serve increasing number of passengers due to congestion problem. Buses share the lane with other vehicles, which affects their speed, capacity, reliability, and quality of service. Because of the presence of a large number of vehicles (of various modes) on road a lot of time is spent in queues and thus travel has become increasingly unattractive. Because of the inefficient management of the BEST fleet, travel times are very high. This gives rise to the need of improving the public transit performance by developing a bus system that gives priority to the buses by providing exclusive bus lanes, traffic signal priority and at the same time takes into account the convenience of passengers.

Moreover, a normal bus is required to be on curb lane for boarding and alighting of passengers, making it even more difficult for merging & diverging. Without a deliberate policy and action on priority of buses in the traffic stream, more and more commuters are gradually shifting to private modes. While provision of exclusive lanes for buses will ameliorate some of the problems, lack of sufficient carriageway width often needs serious evaluation to justify reservation of lanes. The benefits to the buses can be increased further by priority in signals along with the bus lanes.

For the present study a major corridor in Mumbai has been chosen, where the BEST buses are being operated with mixed traffic. Mumbai Metropolitan Region Development Authority (MMRDA) has identified six major corridors for implementation of high capacity corridors with exclusive bus lanes.

The selection of the study area for present work has been based upon the information obtained from MMRDA, on the road width available so as to incorporate one bus priority lane on either side on the corridor. It has been assumed that a minimum of 27.5m width is available throughout the corridor. This width is either available currently or it has been planned to be provided in the future. Six potential corridors for implementation of high capacity corridor with exclusive bus lane are; 1) Western Express Highway, 2) Eastern Express Highway, 3) LBS Marg, 4) SV Marg, 5) Jogeshvari – Vikhroli Link Road & 6) Santacruz – Chembur Link Road.

The present study examines the suitability of such operation over a shorter stretch of western express highway. This evaluates the benefits of providing the exclusive curbside bus lanes with signal priority to buses at all the intersections, as well as to evaluate the increase in delay to the non-priority traffic. With the help of micro simulation it is possible to test different options and to evaluate various measures of effectiveness as performance. Micro simulation software VISSIM is used, which is a tool to simulate signalized/non-signalized intersections with ‘fixed time’, ‘fully actuated’ or ‘semi actuated’ type controller, for transit signal priority.

2. Study Corridor & Data Collection

For the study, a stretch of 6.2 km starting from ‘Magathane Depot, Borivali’ near Borivali Station to ‘Goregaon Cheknaka’ has been taken. The selected corridor consists of eight junctions out of which one is signalized pedestrian crossing, three signalized junctions and others are non-signalized junctions. The study corridor is selected in such a way that it covers all the major types of intersections, viz. intersection below the fly-over where buses will be more, at-grade intersection, non-signalized intersections and a signalized pedestrian crossing. Moreover, the Mahindra & Mahindra intersection and Goregaon Cheknaka at the two ends of the study section are also the major intersections on the Western Express Highway. A map showing the study corridor and all the major intersections is given in Figure 1, and the details of these intersections are as follows,

- Goregaon cheknaka intersection below fly-over (4-legged), Goregaon E.

- Dindoshi intersection below fly-over (3-legged), near Dindoshi bus depot, Malad E.

- Pathanwadi intersection below fly-over (3-legged), near Pathanwadi, Malad E.

- Jai Narayan Vyas Road intersection (merging/diverging traffic), Malad E.

- Times intersection (3-legged), near Times Suburban Press, Kandivali E.

- Station Road intersection (merging/diverging traffic), Kandivali E.

- Mahindra intersection (4-legged), near Mahindra & Mahindra Ltd., Kandivali E.

- Pedestrian crossing near Gokul Concord Apt., Kandivali E

The length of the study corridor has been restricted to 7 km for achieving effective simulation of all traffic in this section. The data collected are used for designing the inputs for micro simulation, as well as for validation of the selected simulation model. Classified volume count at various locations was done and categorised total delay at one intersection was observed under the existing condition. Time headway was measured with the help of videography and a computer program developed to get the time headway at mid-block sections, travel time along the corridor in peak hour from Borivali to Goregaon Cheknaka intersection was obtained from some other Speed-Delay study done using GPS receiver.

2.1 Traffic volume count at mid-block and intersections

Mid-block volume count data was collected at Jogeshwari fly-over for 3 hours in the morning peak period by videography. The data collected was analysed with the help of a computer program to get the mode wise hourly traffic volume, and it reveals that half an hour before peak hour, the traffic is about 65% to 70% of peak volume, shown in Table 1. Turning movement counts were done at all the eight intersections in the morning peak hour 9:00AM to 10:00AM (Figure 2). In addition, mid-block volume count was done at Jogeshwari. The traffic on the selected corridor was classified in six different distinct types of vehicles, viz cars, two-wheelers, three-wheelers, BEST buses, other buses, and trucks/LCV.

All the volume counts were done manually, except Times intersection and the mid-block volume counts were done by videography. The data collected by videography was analyzed later with the help of a computer program to obtain the classified volume count as well as spot speed and time headways at the mid-block. The traffic composition varies at each location, both mid-block and intersection, and an average composition has been considered for simulation as shown in Table 2. At the same time, it is very important to model exact turning movement of buses at all the intersections, and therefore, separate input has been designed for buses.

2.2 Total delay

Total delay for BEST buses and cars were measured at “Goregaon Cheknaka” intersection for straight and left turning movements. Start point for delay measurement was fixed near starting of the fly-over while the end point was fixed approximately 30 meters from the stop line where the vehicles gain its desired speed. The delay consists of the time lost due to deceleration, stopping at signal and acceleration.  The optimal drive time (at speed of 45 kmph) between start and end point of reference is deducted from the actual time measured to obtain total delay.

2.3 Spot Speed at mid-block

At Jogeshwari mid-block traffic data was collected by videography. This data is analyzed to get the spot speeds of the vehicles over a base length of 60 m. A computer program was used to get the spot speeds of different modes (Table 3). The speed data thus obtained is further analyzed and cumulative frequency distribution is obtained. The speed distribution of each type of vehicle is given as input for simulation. Also, the signal cycle and phase timings for the four signalized intersections were measured and provided as input. The vehicle sizes were noted for exact simulation analysis. The lengths of certain types of vehicles are varying and average is adopted for those; each size will have some share in the total number of vehicles to be generated. The articulated buses traveling on the exclusive bus lanes are proposed to be 20 m long and 2.5 m wide with carrying capacity 100 – 120 persons.

3. Research Methodology

VISSIM was chosen as simulation model, which is a microscopic, time step and behavior based simulation model developed to analyze the full range of functionally classified roadways and public transportation operations. VISSIM can model integrated operations of roadway networks found in a typical corridor as well as various modes consisting of general purpose traffic, like buses, light rail, heavy rail, trucks, pedestrians, and bicyclists. It uses the psycho-physical driver behavior model of car following developed by Wiedemann (1974, 1999). The basic concept of this model is that the driver of a faster moving vehicle starts to decelerate as he reaches his individual perception threshold to a slower moving vehicle. Since he cannot exactly determine the speed of that vehicle, his speed will fall below that vehicle’s speed until he starts to slightly accelerate again after reaching another perception threshold. This results in an iterative process of acceleration and deceleration. It uses an interval-based simulation approach and simulates traffic flow by moving “driver-vehicle units” through a network. Stochastic distributions are used to replicate individual driver-vehicle unit behavior and dynamic headway such that, every driver with his specific behavior characteristics is assigned to a specific vehicle.

The study corridor was created in VISSIM with the help of available digitized map of Mumbai road network. Sufficient data was collected on site to give the inputs for generating traffic in the simulation network such that the simulated traffic replicates the real traffic situation in the corridor. The simulated traffic for the existing situation was validated by comparing a few selected measures of effectiveness. Since no simulation model can be expected to capture real behavior exactly, formulating appropriate performance measures is fundamental to the validation process (Arasan & Reebu, 2004). The model can be validated for various performance measures such as, journey speeds, time headways, traffic density, and number of overtaking performed. (Marwah & Singh,1997). For the present study, model validation was done by comparing headways simulated with observed data at a mid-block section, total delay at a particular intersection, and travel time along the corridor simulated with measured values. The driving behavior parameters and other simulation parameters were fine tuned in order to match the selected measures of effectiveness with the simulated. The network was then modified with the proposed bus lanes and the signals were modified from ‘fixed time’ to ‘semi actuated’ (VAP controller) type to provide signal priority to the buses operating on the bus lanes. With different bus frequencies the total delay to buses as well as the non-priority traffic was simulated. Also, the benefit in the travel time of the buses operating on the exclusive lane as compared to the travel time of the BEST buses with mixed traffic was evaluated. The methodology is shown in the form of a flow chart in Figure 3.

4. Simulation Study

The study corridor was simulated with all the eight intersections to represent the existing traffic situation. The non-signalized intersections were simulated based on priority rules while the signalized intersections were simulated with ‘pre-timed or fixed time’ signal controller. The proposed exclusive bus lanes were incorporated in the network, after validation of the simulation model in respect of representing existing traffic. The input data given for simulating the study corridor are described in the following sections.

4.1 Input Data

Different vehicle types were generated with maximum and minimum length and their movement was created through stochastic distribution of acceleration and deceleration for each vehicle type represented through graph by defining minimum, mean and maximum values. The range of spot speed observed for different types of vehicle was given as desired speed distribution. The BEST buses were given separate traffic input to model the exact number of turning movements at the intersections. For this purpose two types of traffic compositions were created, one for the other traffic and one for the BEST buses. The traffic composition given for simulation is given in the Table 2 and the volume inputs given at each of the intersection are given in the Table 4.

The volumes given above are for simulation time of 1800 – 5400 seconds. For 0 – 1800 seconds and for course of 5400 – 7200 seconds, 70% of peak hour volume is given as traffic input. The first half hour is taken as warm up time for the network considering about 20 – 25 minutes travel time from Magathane to Goregaon Cheknaka intersection. In addition to the above traffic inputs, separate inputs are given for the traffic going over the fly-over. The simulation was based on Wiedemann’s (1999) car following model, and the different parameters, viz. standstill distance, minimum headway time, following variation distance etc. were used. For lane changing rule, the parameters like maximum and accepted deceleration of own and the trailing vehicles were defined. Other simulation parameter inputs are listed below,

- Period: Period of simulation in seconds. (7200 seconds)

- Start time: The time shown on the clock at the beginning of simulation

- Simulation resolution: The number of times the position of the vehicle is to be updated per simulated second.  (5 time steps per simulation second)

- Random seed: this parameter is to initialize the random number generator. Simulation with identical input files and identical random seed generates same outputs.

- Simulation speed: The number of the simulation seconds to a real time second. If maximum option is selected, then the simulation will run as fast as possible. (5 simulation seconds = 1 real time second)

4.2 Simulation Network

The study corridor was created from the digitized map of Greater Mumbai. VISSIM supports ‘ESRI shape’ file as background for tracing networks. The corridor was selected and exported to ‘ESRI shape’ file from TransCAD. The background was then scaled accurately and then the network was traced from the digitized map. Figure 2 shows digitized map of Greater Mumbai as background and the study corridor highlighted.

Intersections were created by connecting the appropriate lanes to facilitate all the turning movements. For the proposed High Capacity Bus System (HCBS), exclusive lanes for articulated buses were created on both the sides of road. Bus lanes were connected to the road network only at the intersections. Bus bays were created on the bus lanes downstream of all the intersections.

4.3 Routing Decision

Turning movements at intersections were modeled by creating routing decisions for the traffic and by defining proportion of the traffic on each route. A route is a fixed sequence of links and connectors from the routing decision point (red or stop line) to a destination point (green or exit line). Each routing decision point can have multiple destinations resembling a tree with multiple branches. At each intersection, one decision point was kept at the approaching leg and separate routes were created, with respect to this decision point, each for left turn, right turn, straight and U-turn (if any). Corresponding volumes were defined as relative flows for each of the routes created. With lane closure rules and routing decisions, the shoulder space (around 1.5m to 2.5m) was modeled as additional lane where only two wheelers and three wheelers were allowed to travel. Thus, the real chaotic situation were modeled where, two / three wheelers usually utilize the shoulder lane, and also change lane abruptly from median side lane to the curb side lane to reach up to the shoulder lane near signalized intersections.

#### 4.4 Non signalized intersections

Non signalized intersections were simulated based on priority rules. Priority rules were created by defining the right-of-way for conflicting movements. For each conflicting movement a stop line and one or more conflict markers were placed. The two main conditions to check at the conflict markers were,

- Minimum headway (distance), and

- Minimum gap time.

Typically the minimum headway is the length of the conflict area. During simulation the current headway is determined by the distance between the conflict marker and the first vehicle approaching it. If any part of a vehicle is located on the green bar the resulting headway is 0 m. Whenever the current headway is less than the minimum headway, the corresponding stop line stops any approaching vehicle (similar to a red signal). The following junctions were simulated based on priority rules,

- Dindoshi intersection (3-legged)

- Pathanwadi intersection (3-legged)

- Jai Narayan Vyas Road intersection

- Station Road intersection

#### 4.5 Signalized intersections

All the signalized intersections were coded as ‘fixed time’ controller for simulating the existing situation, where the signal controllers have a preset sequence of phases displayed in repetitive order (HCM, 2000). Total cycle time and its breakup into amber time, red time and green time were defined, as measured on site, for the corresponding signal controller. The following intersections were simulated as ‘fixed time’ controller,

- Goregaon intersection (4-legged)

- Dindoshi intersection (3-legged)

- Times intersection (3-legged)

- Mahindra intersection (4-legged)

4.6 Model Validation

The simulation model was validated by comparing headways simulated with observed values at a mid-block, total delay observed at a particular intersection, travel time measured along the corridor and the various driving behavior parameters were fine tuned appropriately. The comparison of simulated and observed headways at a particular mid-block stretch is shown in Figure 4. The volume of the traffic observed at this section was 2058 vehicles, while in VISSIM 2012 vehicles were generated. The total delay measured for BEST buses at ‘Goregaon Cheknaka’ intersection were 145 seconds and 123 seconds for straight and left turning movement respectively, while the simulated total delay for BEST buses, were 102.6 seconds and 90.6 seconds respectively. For measuring travel time through the study corridor, travel times of ten probe vehicles were measured. The actual travel time along the corridor was observed to be 17.5 minutes, while the simulated travel time (average of ten probe vehicles) along the corridor was 20 minutes. The above comparison between measures of performance reveals that the VISSIM simulation model is able to represent the observed traffic behavior quite reasonably.

4.7 Test of Bus Priority Options

For simulating the corridor with exclusive bus lanes and bus priority at intersections, various options were considered with the operating frequency of buses. Different frequencies were considered for peak direction and off-peak directions, the morning peak being towards Mumbai from Borivali. Also, the randomness in arrival of buses was simulated by putting a dummy bus stop just before the starting point of the corridor with normally distributed dwell time (instead of constant dwell time for all the buses) to make the bus line operation more realistic. The Table 5 shows three sets of frequencies chosen for buses running in peak direction as well as off-peak direction.

The buses traveling on exclusive lane were given signal priority at the intersection, and each of the signalized intersection was simulated as semi-actuated signal controller (HCM 2000). The signal controller logic used for simulating the signal priority is explained here. When a bus approaches any intersection, it is detected by a detector placed at about 120 m upstream (D1) of the stop line. If minimum green time for the ongoing phase is completed by the time, then the signal heads corresponding to the conflicting movements with bus lane turns amber and then red, and the signal head on bus lane turns green. If the green time for ongoing phase is not completed, when bus arrives then the signal head on bus lane will remain red until the minimum green time is completed. After the completion of minimum green time the waiting bus near the stop line is detected by another detector (D2), placed just upstream of the stop line, and the conflicting movement’s signal turns amber – red, and the bus signal turns green. When bus crosses the intersection, it is again detected by another detector (D3) placed 20 – 30m downstream of the intersection, and again the conflicting movements are given green signal. Figure 5 shows the vehicle detector setup and the conflicting movement with south bound buses, which will be turned red at a particular intersection.

4.8 Simulation Results

Travel time and total delays for different modes were simulated for the study corridor. Travel times were simulated for BEST buses and other traffic with and without bus lane priority at intersections. Total delay simulated are classified here as,

- Delay per passenger for traffic (other than BEST buses) for Leg 1 (South bound) and Leg 2 (East/West bound), with and without signal priority to exclusive bus lane. Without signal priority was taken as ‘Base case’ while with signal priority condition was simulated with three operating frequencies of HCBS on bus lane.

- Delay per passenger (as well as per bus) for BEST buses without bus lane priority and with bus lane priority to articulated buses traveling on exclusive bus lanes, for Leg 1 (South bound) and Leg 2 (East/West bound).

Table 6 shows the peak hour occupancy taken for getting total delay per passenger.

4.8.1 Link flows

The Table 7 shows simulated and observed link flows at various points in the study corridor.

4.8.2 Total delay

The total delay simulated was classified in two categories as below,

- Total delay simulated for other traffic (other than BEST buses) in seconds/passenger is shown in Table 8.

- Total delay simulated for BEST buses and articulated buses traveling on bus lanes with signal priority are shown in Table 9.

By examination of values shown in Table 8, it was revealed that the increase in delay to the non-priority vehicles (Leg 2) is excessive for Goregaon and Mahindra intersections. Hence, another option was tested in which the buses were not given signal priority at these two intersections and the travel time was compared with the previous option.

4.8.3 Travel time

The simulated average travel time from Magathane intersection, Borivali (E) to Goregaon Cheknaka intersection, Goregaon (E) are,

- 20 minutes, average of 10 probe vehicles along the corridor

- 23 minutes, for BEST buses (without considering dwell time)

- 6 minutes, for articulated bus on exclusive bus lane (without considering dwell time)

- 8.5 minutes, for articulated bus on exclusive bus lane (without giving signal priority at Mahindra and Goregaon Intersection)

However, it should be noted that the travel time for articulated bus on exclusive bus lane with dwell time is 11 minutes, i.e. average running speed of approximately 38 kmph.

5. DISCUSSION ON RESULTS

The results of total delay at four intersections reveal the increase in delay for non-priority vehicles. By comparing total delay values with and without bus lane, it becomes clear that frequency F1 results in excessive delay for non-priority vehicles, while with frequency F2 increase in delay is not as much. At Goregaon Cheknaka intersection, total delay for all the three frequencies is higher than the total delay without bus priority. Hence it becomes clear that at this intersection giving bus priority to buses will result in to excessive increase in delay for other traffic. At other three intersections total delay for ‘Leg 1’ even decreases with bus priority, which shall be considered as the positive effect of providing exclusive bus lanes. But for ‘Leg 2’ the delay increases with all the bus frequencies, which is obvious, because all the movements of this leg are conflicting with the bus lane.

Other alternative to signal priority to buses, in view of excessive increase in delay to non-priority vehicles, is not to give priority to buses at Mahindra and Goregaon intersection. This case was simulated separately and it gives travel time along the corridor, on exclusive bus lane, as 8.5 minutes as compared to the travel time with bus priority, which is 6 minutes. Also from the simulation it was visualized that at the Goregaon and Mahindra intersections, the left turning traffic conflicts with the buses traveling on bus lane when signal priority is not being provided to buses. Hence another alternative should be tested in which the left turn might be given delayed green compared to the buses on exclusive lane.

6. CONCLUSIONS

The results of total delay at four intersections reveal the increase in delay for non-priority vehicles. By comparing total delay values with and without bus lane it becomes clear that frequency F1 results in excessive delay for non-priority vehicles, while with frequency F2 increase in delay is not as much. At Goregaon Cheknaka intersection, total delay for all the three frequencies is greater than the total delay without bus priority. Hence it becomes clear that at this intersection giving bus priority to buses will result in to increase in delay for other traffic. At other three intersections total delay for ‘Leg 1’ even decreases with bus priority, it is due to more number of straight going buses in the total traffic composition. But for ‘Leg 2’ the delay increases with all the bus frequencies, which is obvious, because all the movements of this leg are conflicting with the bus lane. Other alternative to signal priority to buses, in view of excessive increase in delay to non-priority vehicles, is to provide no bus priority at Mahindra and Goregaon intersections. It gives the travel time along the corridor (on exclusive bus lane) as  8.5 minutes which is 41% more than the travel time with only bus priority. Hence, it can be concluded that this alternative is more feasible than the first alternative with bus operating frequency F2.

References:

Arasan, Thamizh V. & Reebu, Zachariah K. (2004), “Simulation of Heterogeneous Traffic to Derive Capacity and Service Volume Standards for Urban Roads”, Journal of the Indian Roads Congress, 65 (2),  Paper No. 500, pp 219-242.

Marwah, B. R. & Singh, Bhuvanesh (1997), “Level of Service Classification for Urban Heterogeneous Traffic: A Case Study of Kanpur Metropolis”, Transportation Research Circular E-C018: 4th International Symposium on Highway Capacity, pp. 271-286.

Reebu, Zachariah K. (2004), “Modeling Heterogeneous Traffic and Study of the Flow Characteristics on Urban Road Links”, Ph.D. thesis, Department of Civil Engineering, Indian Institute of Technology Madras.

Highway Capacity Manual (2000) Signalized Intersections (Chapter 16), Transportation Research Board, Washington DC.

Table 1 Traffic volume count data at mid-block.

Table 2 Traffic compositions.

Table 3 Spot speeds of vehicles at morning peak hour in km/hr.

Table 4 Volume inputs for simulation.

Table 5 Frequencies for articulated buses traveling on exclusive bus lanes.

Table 6 Occupancy values.

Table 7 Simulated and observed link flows.

Table 8 Total delay for other traffic

Table 9  Total delay for BEST buses and articulated buses traveling on bus lane

Table 1 Traffic volume count data at mid-block

| Peak Direction (Towards Mumbai) |
| --- |
| Time | Quarterly volume (veh) | Hourly volume (veh) |
| 0830 to 0845 | 1156 |  |
| 0845 to 0900 | 1203 | 5229 |
| 0900 to 0915 | 1401 | 5660 |
| 0915 to 0930 | 1469 | 5956 |
| 0930 to 0945 | 1587 | 5952 |
| 0945 to 1000 | 1499 | 5670 |
| 1000 to 1015 | 1397 | 5334 |
| 1015 to 1030 | 1187 | 5127 |
| 1030 to 1045 | 1251 | 4890 |
| 1045 to 1100 | 1292 | 4701 |
| 1100 to 1115 | 1160 |  |
| 1115 to 1130 | 998 |  |

Table 2 Traffic compositions

| Mode | Traffic Composition (%) |
| --- | --- |
|  | Below the fly-over | Through the fly-over | Average |
| Two-wheeler | 29.2 | 29.6 | 29.2 |
| Three-wheeler | 36.4 | 16.0 | 25.0 |
| Otherbus | 6.9 | 1.5 | 5.4 |
| Best bus | 2.7 | 1.1 | 2.7 |
| Car | 19.4 | 45.6 | 32.2 |
| Truck/LCV | 5.5 | 6.3 | 5.5 |

| Mode | Spot speed in km/hr |
| --- | --- |
|  | Minimum | Average | Maximum |
| Car | 40 | 44 | 56 |
| Two Wheelers | 35 | 44 | 63 |
| Three Wheelers | 16 | 38 | 55 |
| LCV's | 27 | 38 | 48 |
| BEST buses | 19 | 27 | 39 |
| Other buses | 20 | 32 | 44 |
| Truck | 23 | 32 | 43 |

Table 3 Spot speeds of vehicles at morning peak hour in km/hr

Table 4 Volume inputs for simulation

| Sr. No. | Place | Volume (Veh/hr) |
| --- | --- | --- |
|  |  | Other Traffic | BEST buses |
| 1 | Magathane intersection, Borivali E | 3050 | 56 |
| 2 | East leg of Mahindra intersection | 1200 | 17 |
| 3 | West leg of Mahindra intersection | 800 | 7 |
| 4 | East leg of Station road intersection | 800 | 6 |
| 5 | West leg of Station road intersection | 576 | 3 |
| 6 | West leg of Times intersection | 960 | 6 |
| 7 | East leg of J N Vyas road intersection | 800 | 3 |
| 8 | West leg of J N Vyas road intersection | 750 | 0 |
| 9 | East leg of Pathanwadi intersection | 2038 | 16 |
| 10 | East leg of Dindoshi Fly-over | 2135 | 52 |
| 11 | East leg of Goregaon cheknaka intersection | 1650 | 51 |
| 12 | West leg of Goregaon cheknaka intersection | 1200 | 51 |
| 13 | South of Goregaon cheknaka intersection | 3813 | 0 |

Table 5 Frequencies for articulated buses traveling on exclusive bus lanes

| Scheme | Peak direction (South bound) | Off-Peak direction (North bound) |
| --- | --- | --- |
|  | Frequency (seconds) | No. of buses per hour | Carrying Capacity | Frequency (seconds) | No. of buses per hour | Carrying Capacity |
| F1 | 60 | 60 | 7200 | 120 | 30 | 3600 |
| F2 | 120 | 30 | 3600 | 240 | 15 | 1800 |
| F3 | 180 | 20 | 2400 | 300 | 12 | 1440 |

Table 6  Occupancy values

| Mode | Occupancy |
| --- | --- |
| Two Wheeler | 1.2 |
| Three Wheeler | 1.92 |
| Car | 2.16 |
| Other bus | 32 |
| BEST bus | 53 |
| Articulated bus | 100 |

Table 7 Simulated and observed link flows

| Station No. | No. of Vehicles Simulated | No. of Vehicles Observed | Difference (%) |
| --- | --- | --- | --- |
|  | All Vehicles | BEST Buses | All Vehicles | BEST Buses | All Vehicles | BEST Buses |
| 1 | 2487 | 98 | 3000 | 105 | 17.1 | 6.7 |
| 2 | 1169 | 68 | 1140 | 71 | -2.5 | 4.2 |
| 3 | 4823 | 98 | 6000 | 105 | 19.6 | 6.7 |
| 4 | 4524 | 67 | 4340 | 71 | -4.2 | 5.6 |
| 5 | 1517 | 67 | 1490 | 71 | -1.8 | 5.6 |
| 6 | 4706 | 46 | 4612 | 50 | -2.0 | 8.0 |
| 7 | 6333 | 69 | 6375 | 71 | 0.7 | 2.8 |
| 8 | 4706 | 46 | 4612 | 50 | -2.0 | 8.0 |
| 9 | 1124 | 64 | 1260 | 77 | 10.8 | 16.9 |
| 10 | 254 | 57 | 260 | 60 | 2.3 | 5.0 |
| 11 | 4142 | 78 | 4628 | 84 | 10.5 | 7.1 |
| 12 | 3144 | 57 | 3134 | 60 | -0.3 | 5.0 |
| 13 | 4008 | 69 | 5223 | 78 | 23.3 | 11.5 |
| 14 | 2899 | 48 | 2864 | 53 | -1.2 | 9.4 |
| 15 | 4813 | 67 | 5343 | 75 | 9.9 | 10.7 |
| 16 | 2910 | 42 | 3128 | 50 | 7.0 | 16.0 |
| 17 | 2869 | 55 | 3050 | 56 | 5.9 | 1.8 |
| 18 | 1727 | 37 | 1782 | 40 | 3.1 | 7.5 |

Table 8 Total delay for other traffic

| Intersection | Leg 1 Delay (sec/pass) | Leg 2 Delay (sec/pass) |
| --- | --- | --- |
|  | Base | F1 | F2 | F3 | Base | F1 | F2 | F3 |
| Goregaon | 42.5 | 147.5 | 94.2 | 78.4 | 38.6 | 129.2 | 103.3 | 69.6 |
| Dindoshi | 29.6 | 25.1 | 23.1 | 15.5 | 7.2 | 10.7 | 9.5 | 8.6 |
| Times | 39.7 | 24.8 | 22.8 | 22.1 | 54.3 | 165.5 | 76.2 | 67.9 |
| Mahindra | 99.3 | 158.5 | 96.6 | 87.9 | 86.9 | 131.0 | 113.1 | 100.1 |

Table 9  Total delay for BEST buses and articulated buses traveling on bus lane

| Intersection |  | Leg1 | Leg2 |
| --- | --- | --- | --- |
|  |  | Total Delay (sec) | Avg. Total Delay sec./pass. | Total Delay (sec) | Avg. Total Delay sec./pass. |
|  |  | Left | Straight | Right |  | Left | Straight | Right |  |
| Goregaon | Base | 90.4 | 102.6 | 126.1 | 2.01 | 48 | 40.8 | 69.2 | 0.99 |
|  | F1 | 276 | 5.2 | 343 | 3.91 | 193.1 | 151.3 | 237.4 | 3.66 |
|  | F2 | 135 | 5 | 206 | 2.16 | 158.8 | 181.7 | 182.8 | 3.29 |
|  | F3 | 124 | 4.9 | 198 | 2.04 | 126.7 | 99.2 | 115.5 | 2.15 |
| Dindoshi | Base | 28.5 | 78.4 | - | 1.01 | 8.1 | - | 19.3 | 0.26 |
|  | F1 | 36.8 | 16.4 | - | 0.43 | 8.5 | - | 20.2 | 0.27 |
|  | F2 | 32.1 | 4.4 | - | 0.32 | 7.6 | - | 19.1 | 0.25 |
|  | F3 | 29.2 | 3.7 | - | 0.29 | 7.2 | - | 16.5 | 0.22 |
| Times | Base | - | 67.5 | - | 1.27 | - | - | 81.5 | 1.54 |
|  |  | - | 26.6 | - | 0.50 | - | - | 234.1 | 4.42 |
|  |  | - | 0 | - | 0.00 | - | - | 172.2 | 3.25 |
|  |  | - | - | - | - | - | - | 152.3 | 2.87 |
| Mahindra | Base | - | 179.4 | - | 3.38 | 53 | - | 131.3 | 1.74 |
|  | F1 | - | 6.1 | - | 0.06 | 69.3 | - | 190.9 | 2.45 |
|  | F2 | - | 4.1 | - | 0.04 | 61.2 | - | 171.1 | 2.19 |
|  | F3 | - | 3.8 | - | 0.04 | 58.7 | - | 164.2 | 2.10 |

(Note: Values in bold are total delay for articulated buses traveling on bus lane with signal priority)

List of Figures

Figure 1: Map of the study corridor and major intersections

Figure 2: Turning Movement count survey locations and study corridor

Figure 3: Overview of methodology for micro simulation of the study corridor

Figure 4: Comparison of time headway observed and generated by VISSIM

Figure 5:  Vehicle detector setup for bus signal priority at intersection and conflicting movements with South bound buses

Figure 1: Map of the study corridor and major intersections

Figure 2: Turning Movement count survey locations and study corridor

Figure 3: Overview of methodology for micro simulation of the study corridor

Figure 4: Comparison of time headway observed and generated by VISSIM

# Text boxes

Figure 5:  Vehicle detector setup for bus signal priority at intersection and conflicting movements with South bound buses

Mumbai

Borivali