Estimation of Collision Risk in Time-Based Spacing Air Traffic by Sequential Monte Carlo Simulation

Authors

Ítalo R. De Oliveira

Computer and Digital Systems Engineering Department (PCS), Polytechnic School, University of São Paulo.

Address: Av. Prof. Luciano Gualberto, trav. 3, no. 158, sala C2-32, 05508-900 São Paulo SP, Brazil

e-mail: italo.oliveira@poli.usp.br

Phone: +55 11 3091 5734

Paulo S. Cugnasca

Computer and Digital Systems Engineering Department (PCS), Polytechnic School, University of São Paulo.

Adress: Av. Prof. Luciano Gualberto, trav. 3, no. 158, sala C2-34, 05508-900 São Paulo SP, Brazil

e-mail: Paulo.cugnasca@poli.usp.br

Phone: +55 11 3091 5401

Henk A.P. Blom

National Aerospace Laboratory NLR

Address:  Anthony Fokkerweg 2, 1059 CM Amsterdam, The Netherlands

e-mail: blom@nlr.nl

Phone: +31 20 511 3544

G.J.(Bert) Bakker, Research Engineer

National Aerospace Laboratory NLR

Address:  Anthony Fokkerweg 2, 1059 CM Amsterdam, The Netherlands

e-mail: blom@nlr.nl

Phone: +31 20 511 3544

Estimation of Collision Risk in Time-Based Spacing Air Traffic by Sequential Monte Carlo Simulation

Ítalo R. De Oliveiraa,*, Paulo S. Cugnascaa, Henk A.P. Blomb, G.J. (Bert) Bakkerb

aComputer and Digital Systems Engineering Department (PCS), Polytechnic School, University of São Paulo. Av. Prof. Luciano Gualberto, trav. 3, no. 158, 05508-900 São Paulo SP, Brazil

bNational Aerospace Laboratory NLR, Anthony Fokkerweg 2, 1059 CM Amsterdam, The Netherlands

Abstract

Current air traffic largely depends of many controllers working in air traffic control centres on the ground, for assuring safe separations between aircraft. This organization concept forms a serious limitation towards a significant further growth of air traffic. This has triggered the research and development of advanced operational concepts that rely in the possibility of transferring (part of) the responsibility of maintaining safe separations to the pilots themselves, through technological enablers such as Airborne Separation Assistance System (ASAS). When applying ASAS in the Terminal Movement Area (TMA), it calculates in each moment the speed which the own aircraft must perform to remain behind the aircraft in front with a fixed spacing. This paper relates a study on the safety aspect of the ASAS Time-Based Spacing (TBS) operation, formulating the risk evaluation problem as the estimation for a large scale stochastic hybrid system of the probability of occurring a collision event. The large size of the system state space poses challenges to the straightforward Monte Carlo simulation of these rare events. This paper applies a recently developed novel method for speeding up rare event Monte Carlo simulations to the TBS concept of operations.

Keywords: Safety; Risk analysis; Air Traffic Control; Monte Carlo

- Introduction

The aim of this paper is to develop a collision risk simulation model of the Time-Based Spacing operation (Hoffman et al., 2003) that makes use of Airborne Separation Assistance System (ASAS). ASAS is seen as a promising option in the future ATM concept to provide an increase in capacity and flight efficiency, while enhancing flight safety. ASAS aims to exploit advances in flight deck technologies, such as the functions of Experimental Flight Management System (EFMS), Automatic Dependent Surveillance Broadcast (ADS-B), data link, etc., to improve the safety, capacity and efficiency of air traffic (CARE/ASAS, 2002).

In the current ATM system, the flight crews are in charge of a safe and efficient control and navigation of their individual aircraft. Unlike air traffic controllers, flight crews currently are not responsible for maintaining separation between aircraft, but only for considering the Traffic Advisories (TA) and obeying the Resolution Advisories (RA) from the Airborne Collision Avoidance System (ACAS). A new (proposed) allocation of tasks between air traffic controller and flight crew is envisaged as a possible option to improve ATM. It relies on a set of applications enabled by ASAS, such as: Airborne Situational Awareness, Airborne Spacing, Airborne Separation and Airborne Self Separation (ICAO, 2003), which transfer part or most of the responsibility of maintaining separation between aircraft, from the ATCo to the flight crew. ASAS may have a prediction time window of up to 15 minutes, which is much greater than the current ACAS time window, around 1 minute.

This different task allocation is expected to increase controller availability, which could lead to improved safety, enable better quality of service and more capacity (depending on airspace constraints). Also, it is expected that flight crews would gain in situation awareness and anticipation by taking an active part in the management of their situation with respect to a designated aircraft (Grimaud et al, 2005; Ivanescu et al., 2005).

Fig. 1: Airborne Spacing operational example.

Although efficiency and capacity are often the main reasons of the evolution in Air Traffic Management (ATM), safety is recognized as a key characteristic when designing advanced ATM concepts (FAA/Eurocontrol, 2004). ATM design teams try to obtain improvements in capacity and efficiency, through the exploitation of new technologies, procedures changes, introduction of new procedures, etc. However, the target safety level is intended to be “equal or better” as compared to the current practice. Quantitative risk analysis tries to put the several ATM applications in a continuous risk scale, enabling objective comparison and definition of minimum acceptable levels.

The quantitative risk analysis methodology chosen for this study is TOPAZ (Traffic Organization and Perturbation AnalyZer) (Blom et al., 2001a, 2006a) which has shown to work well in several previous risk assessment studies of novel ATM operations (Blom et al., 2003a,b; Everdij et al, 2006b). Two kinds of risks may play a role in the TBS operation considered: risk of collision between aircraft, and risk of an accident that is induced by encountering the wake vortex from a preceding aircraft. This study addresses the collision risk only.

This paper is organized as follows. Section 2 presents the ASAS Time-Based Spacing operational concept in the Extended-TMA, which is one of the applications of the Airborne Spacing class, recognized by ICAO (2003). Section 3 describes how this operational concept is mathematically modelled in this study, showing some key points of the model. Section 4 explains how the collision probability was evaluated, describing the Monte Carlo simulation method and an acceleration technique used that enables obtaining results in a reasonable computing time. Section 5 presents some final remarks.

- Description of Time-Based Spacing Operation

The present study considered ASAS Time-Based Spacing (TBS) application in TMA. ASAS TBS aims to delegate to the flight crew some tasks necessary to maintain a precise spacing between aircraft that are in converging or coincident arrival flows. It is expected that TBS application can provide more accurate spacing between arriving aircraft, minimize the idle runway time without violating the separation minima and increase the possibility for TMA to handle more aircraft (Grimaud et al., 2005; Ivanescu et al., 2005). The study of Cloarec et al. (2004) shows that there is a potential increase between 12% and 15% in the terminal airspace capacity when using ASAS TBS operations, due to the Air Traffic Controller workload reduction per flight.

  - Operational Concept for TBS Operation

The TBS procedure in this report focuses on the airspace before the final approach (Grimaud et al., 2005). It is assumed that TBS procedure may start between the Extended-TMA entry point (assumed here to be 60 nautical miles from the airport, after the top of descent) and the Final Approach Fix (FAF). In this phase of the flight, as in other phases, the flight crew must be aware of the surrounding traffic through the ASAS traffic synthesis provided in the Cockpit Display of Traffic Information (CDTI). It is also assumed that ASAS system will be working in Airborne Spacing mode (that is one of the available modes), and the conflict detection is a task of the ATCo.

To have a general idea of how it works, the following example of (RFG, 2005) is shown in Fig. 1. In this example, the controller builds the sequence of aircraft early in the sector by assigning a target aircraft to each aircraft in the sequence (i.e. E is a target for F, D is a target for E, etc). Sequencing and merging instructions are then given to ensure the appropriate spacing is achieved by the merging waypoint. Having built the sequence, and having given the aircraft instructions to maintain the sequence (by maintaining the spacing), the controller must now monitor the aircraft for compliance, as C spaces itself from its target B, and B spaces itself from its target A.

The example shows that the TBS operation involves two steps. In a first step, an ATCo instructs the flight crew to select a neighbouring aircraft as a target on the CDTI (Ivanescu et al., 2005), which will present a screen similar to Fig. 2. Aware of the required target, the flight crew must identify and select it in the ASAS system, and report the target identification to the ATCo. In case the flight crew finds that the target is not in a convenient position, or that the selection of the target might lead to an inconsistent flight execution, or even that they cannot find the target in the CDTI, then they ask the ATCo for clarification. In these cases, the procedure would be either delayed or aborted.

Fig. 2: CDTI screen for Airborne Spacing application.

In the second step, after the target identification read-back of the target identification instruction, ATCo instructs flight crew with one of the following options, depending on the trajectories of the flights involved:

- Merge behind - the flight crew is instructed to merge the own flight trajectory behind the trajectory of the target aircraft, in a chosen waypoint, maintaining at a given time spacing to the target aircraft. This is the case when the aircraft involved are executing converging approach routes. In Fig. 3, AFR123 is the target and DLH456 is instructed to merge behind, maintaining the spacing D.

- Direct-to then merge behind - the merge operation described above is executed, but preceded by a horizontal-path change, which consists in turning to the direction of the merging waypoint when the aircraft reaches the required spacing (this position is called resume point). This instruction is used when the follower aircraft has to achieve the desired spacing, then it follows a divergent path of the target aircraft to achieve a desired spacing, and when the spacing is achieved, the pilot must turn to the cleared merge waypoint. In Fig. 4, AFR123 is the target and DLH456 is instructed to go directly to the merge waypoint, merging behind AFR123 with spacing D.

Fig. 3: “Merge behind” (a) schema.

Fig. 4: “Direct-to then merge” (b) schema.

Fig. 5: “Remain behind” (c) schema.

- Remain behind – the flight crew is instructed to achieve and maintain a given time spacing behind the trajectory of the target, in a chosen waypoint, maintaining at this point a given time spacing to the target aircraft. This third option is applied when the own aircraft is already flying on the same trajectory of the target aircraft, like in Fig. 5.

After selecting one of the options (a), (b) or (c), the flight crew of the follower aircraft will monitor the evolution of the spacing to check if it tends to the desired spacing. Normally, the speed adjustments of the follower aircraft are done automatically, since the aircraft are equipped with the ASAS speed director, which automatically inputs the ASAS suggested speed in the Autopilot System. As an exception, in case of doing training or existing some equipment failure, the flight crew may have to manually apply speed adjustments suggested by the ASAS system.

The aircraft which is applying TBS is denominated the “follower” aircraft, in order to distinguish from the “target” aircraft, which is supposed to land in the same airport as the follower aircraft, but earlier. While monitoring the TBS procedure, flight crew will monitor the execution of the flight plan, and this execution must have RNP-1 (Required Navigation Performance Level 1) property.

Fig. 6: ATCo graphical interface for airborne spacing.

The Air Traffic Controller will have graphical system tools for aiding the task of mounting and monitoring chains of airborne spacing aircraft. The interface developed in (COSPACE, 2006) is shown in Fig. 6. In this figure, the aircraft selected as target by someone are indicated by the small circumferences, and the aircraft performing airborne spacing are indicated by the greater circumferences. The links between aircraft indicate which is the target of the other one.

The TBS procedure may normally finish after passing the Final Approach Fix, or eventually be interrupted, due to some failure in the ASAS system, or to some hazard detected by the flight crew or the ATCo. In cases of abnormal termination, the ATCo will execute conventional procedures for separating and sequencing aircraft. In this paper, only one single flow of arriving aircraft will be considered, with no other surrounding traffic.

- Development of Petri net model of the TBS operation

A prerequisite for running Monte Carlo simulations is to develop an appropriate mathematical model of the operation considered. Hence, as part of the evaluation of the expected number of aircraft accidents per flight hour in airborne spacing operation, a stochastic model is built that describes this accident risk under the influence of human behaviour, technical systems behaviour, communications environment, flight procedures, etc. In the context of the TOPAZ methodology, such a model has the form of a Stochastically and Dynamically Coloured Petri Net (SDCPN) (Everdij and Blom, 2005, 2006). This model is a stochastic hybrid system, which enables to evaluate the collision risk by means of Monte Carlo simulation. Because straightforward Monte Carlo simulation would be far too much time-consuming, we make use of importance sampling based acceleration methods that have recently been developed (Cérou et al., 2002; Krystul and Blom, 2005; Blom et al., 2006a,b).

For the ASAS TBS operation considered, a complete SDCPN model has been developed in (De Oliveira et al., 2006). The SDCPN model is developed using a compositional specification approach. First the relevant agents that play a role in the operation are identified. Next, each agent is modelled through a collection of agent specific Local Petri Nets (LPNs), where each LPN is a Petri net describing an agent specific process. Finally, the connections between LPNs within the same agent and between LPNs of different agents are specified, using a hierarchical specification approach (De Oliveira et al., 2006). In this Section, the main characteristics of the SDCPN model for ASAS TBS operation are summarized.

  - General Definition of SDCPN

The definition of a Stochastically and Dynamically Coloured Petri Net follows Everdij and Blom (2005, 2006), and the graphical representation of its elements are shown in Fig. 7.

The state of a SDCPN is determined by where the tokens are placed, and by the colours of the tokens. A token stays in one place until some transition connected to this place through an outgoing arc fires. This transition will consume at least one token from the input place, and may put tokens to the output place. Fig. 8 shows an example of SDCPN representing aircraft radio telecommunication equipment availability. At any moment, the Aircraft R/T system may be either in the state Working, i.e., working normally, or in the state Not working, i.e., in failure, with no possibility of performing communication.

Fig. 7: Graphical representation of the SDCPN elements.

Fig. 8: Example of two different states of a LPN.

SDCPN’s are very adequate to mathematically model ATM applications. The use of continuous variables called colours, in the SDCPN, enables the use of differential equations, as for example the aircraft physical behaviour and control law presented in subsection 3.4. However, because of the complexity of the model, the formalism of SDCPN is extended to allow hierarchical grouping of its basic elements in agents and LPNs.

  - Agents

An agent is defined as an entity that maintains some kind of situation awareness (Blom and Stroeve, 2004) and may play a role in the operation considered. For this particular application, in order to assess the accident risk, the following agents are adopted in the SDCPN model of the TBS operation (De Oliveira et al., 2006):

- Aircraft;

- Aircraft Guidance, Navigation and Control Systems (GNC), including Guidance Systems, Own Positioning System, and Communication Systems;

- ASAS System;

- Pilot Flying (PF);

- Pilot Not Flying (PNF);

- Air Traffic Services (ATS) System, including Ground Radio Telecommunication, Navigation Systems Global / GNSS (Global Navigation Satellite System), and ATS Surveillance System;

- Tactical Air Traffic Controller (ATCo).

A high level representation of the relations between agents is shown for two aircraft in Fig. 9.

Fig. 9: Relations between Petri Nets at Agent Level.

Each of the agents present in Fig. 9 is internally composed by LPNs.

  - Local Petri Nets (LPNs)

Each agent is modelled with multiple Local Petri Nets (LPN), which are mutually connected forming the SDCPN. The SDCPN model developed (De Oliveira et al., 2006) for ASAS TBS operation consists of 43 LPNs. Only a few of them will be presented in this paper, aiming to provide an idea of how they work.

The state of the LPN is determined by where the token is placed, and by the token colour. Some LPNs are shown in Fig. 10, representing some aircraft communication components. At any moment, one of these systems may be either in the state Working, i.e., working normally, or in the state Not working, i.e., in failure, not performing its communication functions. In these LPNs, the token switches between places through the delay transitions, non-deterministically, at exponentially distributed times. In the sake of simplicity, it was chosen in this project to allow only one token per LPN.

Fig. 10: Aircraft Communication LPNs.

  - Aircraft Guidance Behaviour LPN

The LPN that describes the aircraft physical dynamics is shown in Fig. 11. The possible places for the aircraft state are Level, when the aircraft is trying to keep a constant altitude, Climb/Desc. standard vertical speed, when the aircraft is changing the altitude, or Evasion, when the aircraft is leaving the approach route. The immediate transitions (indicated by I in Fig. 11) are triggered by tokens in other places (not shown in the figure) that represent commands input by the pilot in the aircraft guidance system. The aircraft equations in all the places of this LPN follow the model described by Van der Geest (2002). In this model, the basic aircraft dynamics is described by the following differential equation system:

where:

- and is the aircraft 3-D position, y4 is the aircraft true airspeed, y5  is the heading angle and y6 is the vertical path angle;

- is the control input vector, with u1 being the engine thrust, u2 the angle of attack and u3 the bank angle; these variables are evaluated using the control laws described by van der Geest (2002);

- is the wind vector;

- m is the aircraft mass, g is the gravity acceleration;

- is the aircraft drag function;

- is the aircraft lift function.

Fig. 11: Aircraft Guidance Behaviour LPN.

  - ASAS Agent LPNs

The LPNs composing the ASAS Agent are shown in Fig. 12. The ASAS Surveillance LPN has a token whose colour contains state information of all aircraft inside the range of the ADS-B receiver, plus the own aircraft state information.

The ASAS System Mode LPN has the places Working, which represents the nominal ASAS working state, Failure, where ASAS is not executing its functions, and Corrupted, where ASAS is working with some non-detectable fault. The enabling arc between the place Working and the ASAS Spacing LPN makes that the transitions between the places of ASAS Spacing occur only if there is a token in the Working place, i.e., if ASAS is correctly working.

The token ASAS Surveillance LPN has a colour containing state information of all aircraft inside the range of the ADS-B receiver, plus the own aircraft state information. The ASAS Spacing LPN determines the phase of execution of the ASAS spacing function. Target Acquisition is the initial phase, where the Pilot Not-Flying can select an aircraft as target through the CDTI. After this selection, the token moves to the Spacing Setting place, when the Pilot Not-Flying can give a spacing value to ASAS. Finished this phase, the token moves to the Remain place, where ASAS constantly calculates a required speed to maintain the required spacing. The calculation of this speed depends on the information in the ASAS Surveillance LPN, and is done in accordance with the feedback control design model of Van der Geest (2002).

  - LPNs of Human Operators

The Pilot Flying, the Pilot Not-Flying and the ATCo are the most complex agents in the model. Following the approach developed in (Blom et al., 2001b), the Petri Net model of the Pilot Flying Agent has been developed (De Oliveira et al., 2006). The resulting LPNs are jointly presented in Fig. 13. The LPN named Task Performance PF presents a pattern of stages for the human operator task execution. Each stage is represented by one place of this LPN:

(T1)	Monitoring: stage where the pilot gathers and integrates information about the current goal. For example, this stage may consist in reading the altimeter or the speed indicator.

(T2)	Monitoring and Decision: in this stage, using information provided by the instrumentation systems and, possibly, by other human operators, and based in his situational awareness, the pilot makes decisions about: (a) If he needs to query some other human operator and, if it is, what is the query to be done; (b) If a particular action is required and, in case it is, what are the parameter values for its concrete application.

(T3)	Coordination: stage where the pilot coordinates with other human operators, communicating, questioning and answering, and checking the consistence of his decisions.

Fig. 12: ASAS Agent LPNs.

Fig. 13: Pilot Flying Task Performance LPN.

(T4)	Execution: stage where the pilot is effectively operating the aircraft control, activating functions by means of the aircraft control devices.

(T5)	Execution Monitoring: stage on which the pilot observes the events resulting from the executed action.

(T6)	Monitoring and Goal Prioritization: stage in which the pilot gathers information and decides which of his goals most require attention in the following instant.

In this model, it is assumed that the pilot performs exclusively one of the stages T1-T6 per time. This is a simplification of the reality, because it is known that the human being is able to perform some mechanical, repetitive or even cognitive tasks simultaneously with decision-making tasks. However, the current design tries to keep the model simple.

Another LPN of the Pilot Flying Agent is Current Goal PF, which determines the goal assumed by the PF in a given instant. The Current Goal token may be moved in two different ways. By one side, through the “interrupt” transition, which is fired by audio alerts coming from the interaction place Audio alert. In this case, the next goal is decided based on the audio message received. By the other side, the Current Goal token may move through the transition “subsequent”, which is enabled at the end of a task performance cycle, and so the pilot must decide which the next goal is. The goals stored in the Goal Memory PF LPN are then taken in consideration.

The Mode & Intent SA PF LPN represents the aircraft desired state at a given moment (such as altitude and speed), by the PF. The State SA LPN models the knowledge of the currently active failure indicators in the aircraft, and Cognitive Mode is a simpler version of the contextual control mode model of Hollnagel (1993). When the pilot has few tasks to perform, the token stays in the Tactical mode, and this means that the pilot has a small probability of error or omission. In the opposite, when the pilot has too many tasks, the token goes to Opportunistic mode, raising his probability of error or omission.

The architecture of Petri Net models of the Pilot Not-Flying and of the ATCo agents are in a great extent similar to the LPNs of the PF agent.

  - Other Hazardous States in the LPNs

The set of LPNs in the model also includes several possible failure components in the system state, such as engine failure, noise in the aircraft instrumentation, failure in the ATC systems, etc. With the entire Petri net model, it is possible to simulate the execution of an ASAS TBS operation and check if a collision has occurred or not. Since the ASAS TBS operation is designed to be as safe as possible, a low probability of collision is expected, i.e., a significant number of collisions only occurs amongst a very large number of Monte Carlo simulated flight hours  The next section explains how this has been accomplished.

- Evaluation of Collision Probability

The probability of collision between two aircraft subject to airborne spacing operation is estimated over the SDCPN model, using Monte Carlo simulation that is accelerated through using a suitable type of importance sampling. This section explains the principles of this method and how it was optimized to allow its use in a reasonable computing time.

  - Monte Carlo Method

The Monte Carlo simulation method refers to a class of algorithms very commonly used for obtaining numerical approximations of complex functions. This method involves the generation of some implicit probability distribution and the use of the obtained sample to approximate the function of interest.

The basic idea of the Monte Carlo method is quite straightforward. It consists in randomly drawing a great number of samples from a sampling space, and counting how many of them fall into a particular set. The rate of the number of samples falling into that set over the total number of samples gives the estimated quantity. In the particular case of estimating the collision probability per a single ASAS TBS operation, define Ns as the number of sample simulated operations, and ci the collision indicator for the sample i, i.e.:

If all sampled operations have the same weight, Then the estimated probability of collision p is

Following this idea, if p is expected to be as low as 10exp-9, for example, then the number of simulated samples necessary for the Monte Carlo returning a valid result, i.e., a non-zero result, would be expected to be around 10exp9. Assuming that each simulation sample takes half a second to be executed, due to the large state space (several LPNs, hundreds of variables), the number of hours necessary to calculate p would be in the order of 2.8×10exp5, or equivalently over 15 years. Therefore, optimization techniques were used to speed up Monte Carlo Simulations.

  - Monte Carlo Speed Up

There are several optimization techniques to speed up the Monte Carlo method. The one used in this work is denominated Interacting Particle System (IPS), inspired in the genetic algorithm of Cérou et al. (2002), adapted to hybrid systems by Krystul and Blom (2005) and to air traffic situations by Blom et al. (2006a,b). The use of IPS can be applied in this study because each sample is a SDCPN equivalent to a strong Markov Process, as explained in (Everdij and Blom, 2006a,b). In a Strong Markov Process, the future state of the system depends only on the present state.

The IPS denominates a sample as a particle, and takes benefit of certain predictability in the state of each particle, i.e., the probability that an aircraft collides in the interval [t,Tmax] is higher for aircraft that have smaller separation distance at (present) time t. A filter selects only the particles with smaller distances between aircraft and stops them. In the beginning of the next prediction level, all particles are replications of the selected particles. The particles evolve separately and then a smaller separation distance is used to select particles and the process is repeated, until the aircraft dimensions are reached, meaning the occurrence of a collision event. This filtering process of IPS is depicted in Figs. 14 and 15. The first one shows the initial position of particles as small circles, and the number of sampled particles starting from that position, in each filtering level. Fig. 15 shows the final collision probability as the product of all the intermediate conditional evaluated probabilities.

The use of IPS for ASAS situations (Blom et al., 2006a,b) allows drastically reducing the computing time of collision probability. For the ASAS TBS operation, one IPS run of 50 thousand particles and 11 filtering levels, with the software written in Java, and running in the Java Virtual Machine, takes around 5.5 hours in an Intel Xeon 64 bits, 3 GHz dual processor machine, with a memory load of 2.7 GB. Some parallelism is used to take benefit of using multiple processors. In each level, the evolution of each particle can be computed simultaneously to the evolution of other particles in each processor.

Fig. 14: Example of three levels of particle filtering (showing relative aircraft distances along time).

Fig. 15: Schematic of Interacting Particle System algorithm.

  - Collision Probability Results

The set of Monte Carlo/IPS executions produced the results shown in Fig. 16. These results were obtained for an average flight time of 11 minutes and 7.2 seconds, in the approach airspace considered. These results suggest that the operation of airborne spacing in the ASAS TBS paradigm is, for a  spacing period greater than 47s, compliant with a Target Level of Safety (TLS) of 5x10exp-9 (ICAO, 1998), which is current ICAO TLS for the risk considered in each of the three possible collision geometries, and when TCAS is not taken into account.

  - Bias and Uncertainty Assessment

The model used for calculating the collision probabilities uses several simplifying assumptions, and so there may be bias and uncertainty in the result. Bias is a systematic deviation of the results estimated through the Monte Carlo method from the real collision probabilities; uncertainty is a spread around each estimated result that has to be assumed. Both bias and uncertainty exist due to structural assumptions, parameter value assumptions in the model, and also because of numerical assumptions. Bias and uncertainty assessment involves the estimation of parameter sensitivities (Everdij et al., 2006a). Despite IPS tremendously accelerates the Monte Carlo simulation, a large amount of extra Monte Carlo simulation is required for estimating these parameter sensitivities.

- Final Remarks

In addition to the bias and uncertainty assessment, the next steps suggested to continue this research work are:

- The further improvement of the IPS approach in accelerating Monte Carlo simulations of rare events,

- Identifying and using more adequate computer programming language, with high performance, optimal use of huge amounts of memory, and task parallelization;

- Wake turbulence modelling;

- The inclusion of ACAS in the model;

- Modelling and simulating chains with many aircraft in more complex route geometries, to better assess the risk of other possible encounter configurations. This will require larger amounts of computer memory and high processing power.

Fig. 16: Collision probabilities.

References

Blom, H.A.P., Bakker, G.J., Blanker, P.J.G., Daams, J., Everdij, M.H.C., Klompstra, M.B. (2001a), Accident risk assessment for advanced ATM, In:  Air Transportation Systems Engineering, edited by G.L. Donohue and A.G. Zellweger, Vol. 193 in Progress in Astronautics and Aeronautics, Paul Zarchan, Editor-in-Chief, 2001, Chapter 29, pp. 463-480.

Blom, H.A.P., J. Daams, H.B. Nijhuis (2001b), Human cognition modelling in air traffic management safety assessment, In:  Air Transportation Systems Engineering, edited by G.L. Donohue and A.G. Zellweger, Vol. 193 in Progress in Astronautics and Aeronautics, Paul Zarchan, Editor-in-Chief, 2001, Chapter 30, pp. 481-511.

Blom, H.A.P., S.H. Stroeve, M.H.C. Everdij and M.N.J. van der Park (2003a), Human cognition performance model to evaluate safe spacing in air traffic, Human Factors and Aerospace Safety, Vol. 3, 2003, pp. 59-82.

Blom, H.A.P., M.B. Klompstra, G.J. Bakker (2003b), Accident risk assessment of simultaneous converging instrument approaches, Air Traffic Control Quarterly, Vol. 11, 2003, pp. 123-155.

Blom, H. A. P. and S.H. Stroeve (2004), Multi-agent situation awareness error evolution in air traffic. Proceedings of Probabilistic Safety Assessment and Management Conference (PSAM 6), Berlin, Germany, June 2004, pp. 272-277.

Blom, H.A.P., G.J. Bakker, B. Klein Obbink, M.B. Klompstra (2006a), Free flight safety risk modelling and simulation, Proc. Int. Conf. on Research in Air Transport (ICRAT), Belgrade, June 26-28, 2006.

Blom, H.A.P., J. Krystul, G.J. Bakker (2006b), A particle filter system for safety verification of free flight in air traffic, Proc. IEEE Conf. on Decision and Control, San Diego, December 2006.

CARE/ASAS (2002) Activity 3: Airborne Separation Minima - Final Report CARE/ASAS/Sofréavia/01-018 - Version 2.1 - April 3, 2002.

Cérou, F., P. Del Moral, F. LeGland and P. Lezaud (2002) Genetic genealogical models in rare event analysis, Publications du Laboratoire de Statistiques et Probabilites, Toulouse III, 2002.

Cloarec, D., K., Purves and F. Vergne (2004) CoSpace 2003 Controller Model Based Study Assessment of Airborne Spacing Tasks in the Extended TMA. EEC Report no. 392. Eurocontrol Experimental Centre, Brétigny-sur-Orge, France, 2004.

COSPACE web site: http://www.eurocontrol.int/eec/public/standard_page/SSP_cospace_home.html. Last time accessed in 10-july, 2006.

De Oliveira, I. R., et al. (2006) Accident Risk Assessment Model for ASAS Time Based Spacing Operation in ATM”, NLR draft report, 2006.

Everdij, M.H.C. and H.A.P. Blom (2005), Piecewise deterministic Markov processes represented by dynamically coloured Petri nets, Stochastics, Vol. 77 2005, pp. 1-29.

Everdij, M.H.C., H.A.P. Blom (2006), Hybrid Petri nets with diffusion that have into-mappings with generalized stochastic hybrid processes, Eds.: H.A.P. Blom, J. Lygeros (eds.), Stochastic hybrid systems: Theory and safety critical applications, Springer, 2006, pp. 31-63.

Everdij,M.H.C., H.A.P. Blom, S.H. Stroeve (2006a), Structured assessment of bias and uncertainty in Monte Carlo simulated accident risk, Proc. 8th Int. Conf. on Probabilistic Safety Assessment and Management (PSAM8), May 2006, New Orleans, USA.

Everdij, M.H.C., H.A.P. Blom, G.J. Bakker (2006b), Modelling lateral spacing and separation for airborne separation assurance using Petri nets, Simulation: Transactions of the Society for Modelling and Simulation International, forthcoming in Vol. 82, 2006.

FAA/Eurocontrol (2004) Safety and ASAS applications, Co-operative R&D Action Plan 1 report, version 4.1, 2004.

Grimaud, I., E. Hoffman, L. Rognin, K. Zeghal (2005) Spacing Instructions in Approach: A Stepwise Design Approach. Air Traffic Control Quarterly, Vol. 13 (2), 2005, pp. 127-153.

Hoffman E., D. Ivanescu, C. Shaw, K. Zeghal (2003) Effect of Mixed Aircraft Types and Wind on Time Based Airborne Spacing. AIAA Guidance, Navigation, and Control Conference and Exhibit (AIAA 2003-5404), 2003.

Hollnagel (1993), E. Human reliability analysis, context and control. Academic Press, London, 1993.

ICAO (1998), International Standards and Recommended Practices – Air Traffic Services, Annex 11, 12-th edition, July 1998.

ICAO (2003) AN-Conf/11-IP/5 - ASAS Circular ICAO Airborne Separation Assistance System (ASAS) Circular Version 2.0E. International Civil Aviation Organization, September, 2003.

Ivanescu, D., C. Shaw, E. Hoffman, K. Zeghal (2005), A Pilot Decision Support Tool for Merging Behind a Lead Aircraft. Proceedings of the 44th IEEE Conference on Decision and Control, and the European Control Conference 2005, Seville, Spain, 2005.

Krystul, J. and H.A.P. Blom (2005), Sequential Monte Carlo simulation of rare event probability in stochastic hybrid systems, Proc. 16th IFAC World Congress, July 4-8, 2005.

RFG (2005) (Requirement Focus Group) SPR SG: Package I – Enhanced Sequencing and Merging Operations (ASPA-S&M) Application Description. 19th August 2005.

Van der Geest, P. J. (2002) The AMAAI Modelling Toolset for the Analysis of In-Trail Following Dynamics. AMAAI Deliverable D2: Description and User Guide. NLR-CR-2002-112, 2002.

# Footnotes

Corresponding author: italo.oliveira@poli.usp.br

# Text boxes

PF

T1

Aircraft

Aircraft j

GNC

ASAS

PNF

PF

Aircraft

Aircraft i

ATCo

ATS

Aircraft R/T Availability

(Not working)

Aircraft R/T Availability (Working)

Place

T2

P2

P1

D

G

Inhibiting arc

Enabling arc

Ordinary arc

Immediate transition

Guard transition

I

D

G

Token

Delay transition

1

1

Filter 3

Filter 2

Filter 1

1

5

5

5

5

1

1

1

1

1

1

Delay transition

Aircraft R/T Availability

(Not working)

Aircraft R/T Availability (Working)

T1

Place

T2

P2

P1

D

G

Inhibiting arc

Enabling arc

Ordinary arc

Immediate transition

Guard transition

I

D

G

Place

PNF

ASAS

GNC

1

1

1

1

1

1

1

5

5

5

5

1

Filter 1

Filter 2

Filter 3

1

1

p=p1. p2... .pn