Decision Support System for Dynamic Re-Scheduling of Trains under Disturbance

Professor John Preston and Dr John Armstrong, Transportation Research Group, University of Southampton.

Chris Bouch, Dr Colin Goodman, Dr Paul Weston, School of Engineering, University of Birmingham.

Dr Ryo Takagi, Department of Electrical Systems Engineering, Kogakuin University, Japan.

To be presented to the 11th World Conference on Transport Research, Berkeley, California, 25th – 28th June 2007.

This paper reports on work undertaken by Rail Research UK. It reviews existing approaches to the management of disruptions to railway operations in Britain. It finds that train control in such circumstances is largely manual, with use of a fairly simple train classification system and margin tables, and relatively limited use of computerised solutions such as ARS (automatic route setting).

The paper goes on to devise and assess revised methods of, and strategies for, disruption management, through the dynamic re-scheduling and re-routing of train movements. A series of real time computer tools are examined with reference to a specific junction on the British rail network, namely Abbotswood Junction on the Birmingham to Bristol line.  It is found that although classical linear programming approaches work well on simple urban rail networks, they work less well on complex mixed traffic networks. Alternative approaches based on genetic algorithms and a guided search procedure are found to provide better and faster solutions but still fall short of providing on-line support at a practical scale.  The alternative strategies for and methods of recovery from disruptive incidents are compared and evaluated, in order to determine the most promising ways forward.

1.	Introduction

This paper reports on work undertaken as part of project B1, Decision Support System for Dynamic Re-Scheduling of Trains Under Disturbance, for Rail Research UK (RRUK), a consortium of nine universities funded for six years by the Engineering and Physical Sciences Research Council. The work was undertaken by the universities of Birmingham and Southampton, as part of Phase One of RRUK and was completed in September 2006. It had the following objectives:

- To review existing approaches to the management of disruptions to railway operations.

2.	To devise and assess revised methods of, and strategies for, disruption management, though the dynamic re-scheduling and re-routing of train movements.

3.	To compare and evaluate the alternative strategies for and methods of recovery from disruptive incidents, in order to determine the most promising way(s) forward.

4.	To investigate different levels of detailed modelling for multi-train performance to support the strategy evaluation.

5.	To develop a facility to provide real-time decision support to railway control centre operators to assist with responding to disturbances such as delays, failed trains, etc.

Full details of this work are given in Goodman et al. (2006). The structure of this paper will be as follows. In the next section some contextual background will be provided.  In section 3, a detailed train simulator with classical optimisation techniques will be outlined. In section 4, alternative approaches based on genetic algorithms, guided search procedures and a simplified simulator are described. In section 5, these new approaches are evaluated. Lastly, in section 6 some conclusions are drawn and some recommendations for further research made.

2.	Background

A key feature of railways is their inherent inflexibility when compared with other modes.  As Armstrong (1998, p125) puts it, “the railroad is classified as a “single degree of freedom” mode of transport”, while De Fontgalland (1984, p7) describes the railway as “function[ing] in one-dimensional space.”  White (2003a, p16) summarises the situation as follows:

Among transportation modes, the railroad is made unique by the tracks.  Unlike the operator of any other general-use transportation vehicle, the operator of a train does not steer.  Trains can only go exactly where the tracks go.  They cannot swerve to avoid a collision, they cannot change routes or even lanes of the same route except where a track arrangement has been constructed for the purpose.

Compared with other modes, railways thus have an inherent lack of a straightforward ‘overtaking’ facility; i.e. when a track or section of line is obstructed, the flexibility to operate around the obstruction is dependent upon the number of parallel tracks, the proximity of crossovers, the nature of the signalling system (uni-directional or bi-directional), and the density of opposing and/or parallel traffic.  On a wider scale, further constraints include driver knowledge of and acceptance of train types on alternative, ‘parallel’ routes.

Another limiting factor is the typical requirement for trains, particularly passenger services, to make intermediate stops at scheduled times between their termini.  While these constraints obviously also apply to other public transport services, the relatively low density of rail networks compared with highway systems means that there are typically far fewer routeing alternatives available, and the more closely spaced are the scheduled stopping points, the greater the inherent constraint.

When disruptive incidents do occur, the comparatively restricted range of possible responses is compounded by the rate at which the knock-on effects can spread through affected parts of the network.  According to Network Rail (2003, p5):

with many parts of the network operating ever closer to full capacity, the railway is highly sensitive to even minor sources of disruption.  Whether the initial cause of disruption is an individual delay to a single train or an infrastructure fault, the knock-on consequences rapidly multiply and can result in significant disruption to train services in the area for some hours afterwards.  This results in an increase in the overall delay per incident, which lies behind a substantial part of the deterioration in performance since 1999/2000.  While the numbers of failures of signalling and other non-track assets have remained broadly unchanged, the total delay caused has increased substantially.

Such effects can also spread widely: this characteristic was illustrated by the derailment of a freight train at Quintinshill on the West Coast Main Line in Scotland on June 17 2002, when the following day’s edition of The Independent reported that “the knock-on effects for the network were so severe that disruption extended as far as the West Country [of England].”  This is partly a consequence of the nature of railway signalling systems, whereby the track is divided into successive linear sections, or blocks, which cannot usually be occupied by more than one train at a time.  This means that when a series of trains have to stop behind each other, they are quite widely separated, and any blockage can extend ‘upstream’ quickly and over a long distance.

The Network Code Schedule H provides guidance and instructions on how different types of delay should be handled (Network Rail, 2005).  Major delay is defined as delay having a material effect on the operation of the network and is managed by the implementation of pre-prepared contingency plans.  All other types of delay are defined as minor and in general are managed by the signaller using train regulation techniques.  To confuse matters somewhat analyses of delay tend to refer to primary delay (for example, delay experienced by a failed train), and reactionary delay (the knock-on effects of the failed train on subsequent services).  It is the management of reactionary delay that this project is focused on.

A series of interviews highlighted that margin tables are increasingly being used by signallers, but only in fairly straightforward situations (for example, simple junction layouts and train service patterns).  Some managers acknowledged the pressing need for computer-based tools to help signallers regulate in more complex environments.

At Integrated Electronic Control Centres (IECC) signallers already receive assistance from the Automatic Route Setting (ARS) tool, developed originally by British Rail Research and more recently by AEA Technology Rail (AEAT, 2005).  The main thrust of ARS is the automated management of the timetabled service, leaving signallers free to deal with irregularities.  As such, ARS is mainly about searching for conflict-free routes, but the system has also been developed over the years to minimise train delays that might result from that process.   The authors are not aware, however, of ARS having been installed outside an IECC facility, except at Wimbledon SCC, which means most signallers must cope with disruption on their own. Based on publicly available information, it appears that ARS works on the basis of a number of pre-programmed scenarios addressing a limited number of criteria, rather than by utilising a comprehensive optimisation algorithm.  As such, the managers were able to quote examples of situations where ARS does not provide an optimum operating solution as they saw it; for example, holding a late, in-coming train outside a terminal station because the route of an out-going service has already been set in response to ‘Train Ready to Start’.

When disruptive incidents occur on the railway, it is usually desirable to maintain some degree of service, using whatever residual capacity is available.  Contingency plans may be used to deal with certain foreseen scenarios (typical measures include the selective cancellation of services, and the provision of replacement buses), but many incidents will have to be dealt with on an ad hoc basis.  The responsibility for such responses lies chiefly with signalling and control staff, who monitor, control and, where necessary, regulate the movements of trains on a railway system, and who respond to operational problems by regulating trains that are running ‘out of course’.  The Strategic Rail Authority’s 2003 Network Utilisation Strategy document notes the importance of “better train regulation … to accommodate growing demand whilst also potentially improving performance” (SRA, 2003).  Suggested measures to improve regulation include the “revisit[ing of] prioritisation rules, class regulation practices and [the] use of passing facilities by passenger services.”

In the context of heavy rail operations in Britain, train movements are regulated by Network Rail’s signalling and control staff.  Network Rail’s 2005 Management Plan states that “train regulation is a key part of the signaller’s role [and a necessary activity] when trains are running outside the planned schedule and are causing pathing conflicts” (Network Rail, 2005b).  The Plan states the objective of train regulation, as set out in the Network Code, is to strike a fair and reasonable balance between: minimising overall delay to train movements; minimising overall delay to passengers and time sensitive goods; maintaining connections between railway passenger services; avoiding undue discrimination; protecting the commercial interests of Network Rail and each affected train operator; and promoting the interests of safety and security.

Given that both passenger and freight trains are of varying capacity and are likely to be unevenly loaded, the first and second objectives may be mutually exclusive.  Similarly, maintaining connections is likely to increase overall train, and possibly passenger, delay, since it inevitably requires trains to be held to meet late-running services.  It is also difficult to make trade-offs between delays to passengers and time-sensitive goods, without knowing the respective values (costs) of those delays.

Taking account of overall passenger and freight delay entails consideration of the relative loadings and priorities of different types of trains, as well as the extent of total and individual train delay.  Information about freight train loadings should be quite readily available prior to and during their journeys, but real time passenger loading data is more problematic; it may be possible to obtain approximate data from ticket sales and automatic barrier data, and, as in the case of London Underground operations, from measurements of train loadings in terms of total passenger weights.  For relative train priorities, the set of train classes currently used in British railway operations is listed in Table 1  (Hall, 2001).

Table 1: Train Classifications in British Railway Operations

| Train Class | Train Types in Class |
| --- | --- |
| 1 | Express passenger train; Nominated postal or parcels train; Breakdown or overhead line equipment train going to clear the line or returning therefrom (1Z99); Traction unit going to assist a disabled train (1Z99); Snowplough going to clear the line (1Z99); Class 9 - 373/1 or 373/2 train [Eurostar and Regional Eurostar] |
| 2 | Ordinary passenger train; Breakdown or overhead line equipment train not going to clear the line (2Z99); Officer’s Special train (2Z01) |
| 3 | Freight train capable of running at more than 75mph (121km/h), or a parcels train or an empty coaching stock train where specially authorised |
| 4 | Freight train permitted to run at more than 60mph (97km/h) |
| 5 | Empty coaching stock train |
| 6 | Freight train permitted to run at 50, 55 or 60mph (81, 89 or 97km/h) |
| 7 | Freight train permitted to run at 40 or 45mph (65 or 73km/h) |
| 8 | Freight train permitted or timed to run at 35mph (57km/h) or less |
| 9 | See Class 1. Class 9 formerly comprised non-fully fitted/unfitted/non-continuously braked freight trains |
| 0 | Light locomotive(s) |

This classification dates back to the early 1960s, when four-character train descriptions, or headcodes, were introduced by British Rail, with the first digit in a train’s headcode indicating its Class (Simmons and Biddle, 1997).  The classification reflects the much greater variety of freight that was then conveyed by rail than is now the case.  It can be seen that the classification represents a fairly obvious hierarchy, with train Classes declining in priority from 1 to 9 and then 0.  Network Rail staff have indicated that only Classes 1 and 2 are now explicitly used for regulation purposes, with Class 1 trains normally being given priority over their class 2 counterparts when a routeing conflict occurs.  This is not ‘written in stone’, however, and Class 2 services may on occasion be given priority over their Class 1 counterparts.

Network Rail’s current regulation policy comprises “three key components”. Firstly, there is a generic regulation statement, applicable across the network, which defines the regulation objective and the criteria to be applied by signallers in arriving at regulation decision.  The generic regulation statement defines the regulation objective as being to minimise overall train delay.  Secondly, there are margin tables that readily identify the relative performance characteristics of particular traction types, and available infrastructure for regulation purposes. Thirdly, an industry-agreed protocol for the management of long-distance trains on the network has been introduced. The protocol recognises that long-distance trains are vulnerable to a series of uncoordinated localised regulating decisions that have a tendency to transmit reactionary delays across the network.

3.	Initial Approach

Our starting point was the Object-Oriented Multi-Train Simulator (OOMTS) written by Lok-Kee Siu in the early 1990’s (Siu, 1995, Siu and Goodman, 1992). The program logic is based on a previous Fortran version that has been under development since 1973 (Mellitt et al., 1978).  OOMTS is written using the object-oriented programming language C++. The OOMTS model comprises five ‘subsystem managers’, each containing data (or the instances of objects necessary for running the simulation) for one ‘subsystem’. The Simulation Manager is at the centre of the structure, managing all these subsystem managers and the actual running of the simulation itself. The concept of the overall model structure is shown in Fig. 1.

The OOMTS model has been used to simulate Hong Kong’s ‘Island Line’ metro (Goodman and Ueda, 2004) and used as a research tool for various railway-related projects within the University of Birmingham. During the course of the project detailed in this report the OOMTS model was substantially updated. In particular, it was enhanced by adopting XML (eXtensible Markup Language) as the input data file format, ensuring complete separation of track profile data and train run data and introducing a new signalling model and an object-oriented framework for traffic control.

Fig. 1: OOMTS subsystem managers in OOMTS.

The redesigned OOMTS model was  used to simulate train operation near Abbotswood Junction on the Birmingham to Bristol Line. Abbotswood is approximately 20 miles north of Cheltenham Spa where the line from Worcester joins the Bristol to Birmingham main line.  The main line is twin track with a speed limit of 100 miles per hour (mph) except through the junction itself, where the limit is reduced to 90 mph.  There is a crossover between the up and down lines and a goods loop on the down line.  The line from Worcester is double track, but joins the main line by means of a single lead junction.  The train service is a mix of high-speed cross-country services, local commuter trains and freight.  Fig. 2 shows the track layout of Abbotswood Junction and  simulation results are shown in Fig. 3.

Fig. 2: Track layout of Abbotswood Junction

Fig. 3: Example simulation result using the modified OOMTS

The OOMTS program simulates train movements defined by the train service regulator. The order in which trains are to proceed, where there is a choice, must be defined before the simulation can be started. The optimisation program, which is external to the OOMTS and is based on classical linear programming, uses the train arrival delays and a pre-defined sequence of routing decisions to construct the data files that the OOMTS has to read before simulating the train movements. The interaction between the OOMTS and the optimisation program is inefficient in three ways. Firstly, the data files for each ordering possibility have to be constructed and written by the optimisation program and read back in by OOMTS.  Secondly, the optimisation program can do nothing until the OOMTS program has finished simulating the train movements for the given train ordering. Thirdly, the optimisation program has to ‘know’ how to construct valid train ordering through the network although the OOMTS might be able to provide some help with this process.  The upshot of the above is that the processing speed of the simulator tool, developed from an existing, general engineering multi-train simulator has proved to be too slow because of the unnecessary overhead carried. Furthermore, the use of classical optimisation techniques has proved difficult in the mainline railway case because of the highly discrete nature of the regulation decisions. As a result new methods have been developed.

### 4.	New Methods

As an alternative to ‘classical’ linear programming techniques, two new search procedures were developed based on genetic algorithms and a form of dynamic programming we have referred to as the guided search method. In addition, a simplified simulator has been developed to be used in conjunction with the guided search method. These new methods are discussed in turn.

  - Alternative Search Procedures

    - Genetic Algorithms

The genetic algorithm defines a chromosome (Rothlauf, 2002) that encodes the possible routing sequences through Abbotswood Junction. The chromosomes are restricted to feasible routing sequences by using state transitions. A state is defined by the number of trains at each junction source and the number at each exit path. The state is augmented with the train type and the train destination so a goods train can use the goods loop while a passenger train cannot, and so each train can only exit the junction along the proper path. For any given chromosome the OOMTS program can be called to evaluate the cost of the encoded routing sequence. The routing sequence is conveyed to the OOTMS model by generating data files specific for each case before the OOMTS model is invoked.

In normal genetic algorithms, chromosomes are subject to mutation and crossover. During mutation, the chromosome is modified in a small way. For our purposes, this operation has to be carefully controlled as random mutations of the chromosome generally lead to invalid state transitions. Crossover involves generating a new chromosome from two ‘parent’ chromosomes. Many pairs of chromosomes are incompatible in this problem because of the constraints on valid chromosomes. Such pairs are ‘infertile’. However, some pairs can form a union that results in viable offspring. The probability of certain combinations is based on a measure of the difference between two chromosomes based on the Levenstein distance (NIST, 2006).

The genetic algorithm search procedure begins with a number of initial valid chromosomes. These are evaluated using the OOMTS model, and the costs assessed. The cost depends on the transit times of the trains from their setting off from the boundary of the network to their arrival at the network exit. The cost is obtained by summing the transition times weighted according to different train types. The initial chromosomes are generally high cost. The next set of chromosomes is developed by discarding the worst half of the existing chromosomes and applying mutation and crossover to those remaining. Since the mutation and crossover operations may destroy the best solution already identified, this solution is also carried forward to the next pool of chromosomes. The next pool of chromosomes is evaluated using the OOMTS model (except for the ones for which the cost is already known). This procedure is continued for a number of generations. Note that the best cost can never increase as the best cost so far is always retained. The minimum cost typically decreases in fits and starts, but after a number of generations the cost generally stabilises at some cost close to the minimum cost.

As usual in genetic algorithms, there is no guarantee that the minimum cost will be identified, but the minimum identified cost will be a feasible solution. In practice, a decent solution is usually found. If the optimisation process is restarted every 5 minutes, as new trains appear on the network, the optimisation procedure has more opportunities to improve on the current solution.

It should be note that the genetic algorithm uses only the weighted sum of train transit times across the network

(1)

The sum is over all trains and the  are the weights for each train. The exit time minus the entry time is the transit time for the ith train. From the point of view of the optimisation method, the most important consequence of this choice of cost function is the cost is only available once every train has exited the network. This means that a sequence of routing decisions to be evaluated has to be followed through to the horizon time (which is chosen so that all trains complete their passage through the network).

### 4.1.2	Guided Search Approach

The second search procedure arose from a deterministic search. One simulation is created from the initial state of all trains on the network. This simulation is stepped forward until a decision has to be made, for example whether to allocate a route through the junction for a train or to hold it at the main signal. The simulation splits into one instance for each possible decision. The initial simulation can algorithmically generate all possible decisions in contrast to the genetic algorithm approach in which the possible decisions are generated externally to the simulation. Fig. 4 illustrates an example of the resulting decision tree. Rather than making a decision, all possible decisions are examined in parallel. Each path from ‘now’ to the prediction horizon corresponds to one combination of decisions and all possible paths are created from the simulations. Note that the figure shows only pairs of decisions but in practice more than two possibilities can be generated from a decision node in the real simulation. For example, a freight train approaching signal G26 (controlling entry to the junction from Bristol) can be routed into the goods loop, straight through, or held at the main signal.

Fig. 4: Decision tree

Fig. 5 shows a state transition diagram for a train requesting a single route. Note that the state ‘run in new simulation’ represents a simulation spawned from the original one.

Fig. 5: State Transition Diagram

Trains move between the ‘run, ‘hold’ and ‘wait’ states as resources are locked and released. Note that some additional complications arise when a train can use more than one route – the state considers not only the train but also the possible routes. Although not formally proved, all possible routing combinations should be generated once and only once using this arrangement. Some care must to be taken in the programming of resource locking and unlocking to ensure that the sequential operation of the simulation is logically correct. As an added precaution, the program implements certain checks such as ‘train-operated route release’ whereby the resources locked for use by a train must be used and released strictly in the expected order (a similar arrangement exists in UK signalling systems), and by the right train. These checks were invaluable for finding subtle programming errors arising from the order in which the program carried out various operations. Comparisons between the number of generated parallel simulations and the theoretical result for the Abbotswood Junction example for small numbers of trains suggest that all possibilities are correctly being generated.

The ‘guiding’ in the guided search method is provided by the provision of a partial cost function that can be computed at any time. The cost is a function of time (or at least defined at each time step)

(2)

where di(t) are the accumulated delays up to time t and ei are lower bounds on the future delay. As each train passes certain timing points, for which times are given in the nominal timetable, the known delay is updated and the future lower bound is then measured from this new timing point. Two effects can be exploited when the cost function can be evaluated mid-way through a simulation. First, if the cost function never decreases with increasing time, the cost provides a lower bound on the terminal cost. This can be used to avoid searching possibilities that have a high cost while there are other lower cost possibilities. Secondly, even if the cost is decreasing, the partial cost can be used to guide where simulation effort should be focussed.

4.1.3 	 Comparisons

In the genetic algorithm, as in many other search methods, the solution space is searched by evaluating some possibilities and using the result to guide the search in some way. The best possibilities are retained, the worst are discarded. New possibilities are created based on the best achieved so far, and using some method of generating variations on the best current solutions in the hope of finding a better solution. In the guided search method, a different approach is taken, in some ways linked to dynamic programming. Instead of defining a cost only at the terminal state, a means of finding a partial cost (i.e. a cost that can be evaluated at any time) is defined. This partial cost is used to guide the search in a deterministic manner. Note that this is different from using heuristic rules (rules of thumb) in the sense that the rules are based on the cost so far plus a determined minimum future cost. In the future, some heuristic rules may be added to avoid going down paths that are low cost but can be predicted to become high cost later (e.g. dead lock situations).

4.2	Alternative Simulator

An alternative simulator was written with the second optimisation approach in mind so there is much tighter integration between the simulation program and the optimisation program. In fact, the two parts operate as a single program. The advantages of this arrangement are:

- The routing decision to be followed by a simulation is made ‘just in time’ rather than being pre-determined before simulation begins.

- The possible routing decisions are determined by the simulation and reported back to the optimisation program.

- The progress of the cost evaluation is available during the simulation so the cost can be used to guide the optimisation program.

A new simulator was written in C#, including only sufficient features to accommodate the problem at hand. Acceleration and braking rates are constants; there is no gradient or curve radius information; only fixed block signalling is supported. The errors introduced by assuming constant acceleration are not thought to be significant compared to the errors introduced by uncertainty in the driving style of the driver.

One of the ways in which tight integration benefits the optimisation is that the simulator automatically generates possible routing sequences that are passed to the optimisation program. Fig. 6 shows the six possible routes available at Abbotswood Junction. The fast simulation program uses the setting and releasing of routes from a main signal as the mechanism for obtaining all possible decisions in a controlled order. A goods train approaching from the top left can take route R1 or R3, or it can be held at the main signal. If a route is chosen but cannot currently be allocated (for whatever reason) the train is held at the main signal until the route becomes available. Part of the software maintains a queue of route requests that are allocated as and when the routes become available.

Fig. 6: Routes at Abbotswood Junction

## 5.	Evaluation of New Approaches

Sample time-distance graphs from two methods, namely the genetic algorithm with the OOMTS model and the guided search approach with the fast simulator, are given in this section.

5.1 	Results from the Genetic Algorithm and OOMTS Model

One freight train and 12 passenger trains are simulated over an horizon of 90 minutes. The base behaviour is defined by all trains arriving on time and passing through the junction with no delays. The remaining scenarios are generated by assuming that the freight train is delayed and the following passenger trains entering the network from the same track retain their original order. The cost function is defined as the weighted sum of train transit times – an important point to be discussed later. A range of solutions is generated by varying the weighting applied to different train types. Also shown are the results of a ‘first-come, first-served’ algorithm with and without the use of the goods loop.

The time-distance graph resulting from the freight train arriving on time is shown in Fig. 7. The blue line is the freight train, the green lines are trains travelling on the main line, and red lines represent trains that come from, or go to, Worcester. The freight train travels more slowly than the other (passenger) trains but does not cause any knock-on delay because it clears the network well before it can interfere with any passenger train.

Fig.7: No delay (nominal timetable)

The passenger trains on the main line and those that use the Worcester branch are different train types, with provision for different weightings. However, the line speed limits force the trains to travel with identical maximum speeds. In the examples given here the two types of passenger train have identical weights – the weightings shown in the caption for Fig. 8 are ‘passenger:passenger:freight’.

Fig. 8 shows the result when the freight train enters the network with a 30 minutes delay. The freight train is six times less heavily weighted than the passenger trains. As a result the freight train waits in the goods loop until all passenger trains have passed by. Sensitivity tests were undertaken to examine the impact of different delay weightings. Changing the weighting applied to the freight train changes the ordering of trains through the junction in the manner expected. However, the time taken to compute the results is of the order of hours rather than minutes or seconds. This factor is discussed in more detail later.

Fig.8: Delay 30 minutes: Weighting 6:6:1

By way of comparison, results from the misnamed ‘first-come, first-served’ algorithm are examined. This means that as each train approaches the junction it enters a queue of trains waiting to use the junction. The routes through the junction are allocated in the order in which routes become available. The first-come first-served name is inaccurate as trains are not always serviced in order of arrival at the junction. It is possible to generate situations in which a train is held while trains that arrive later are routed through the junction. Nevertheless, the results of two cases of this algorithm are given here as a possible junction routing algorithm. The simulation program requires that the route to be taken by each train is defined before simulation begins. The use, or not, of the goods loop has to be defined in the train service definitions. Fig. 9 shows the ‘first-come, first-served’ result when the freight train is set to bypass the goods loop. The freight train passes straight through with consequent delays to the following trains.

Fig. 9: Delay 30 minutes: First-come, first-served (not using the goods loop)

Fig. 10 shows the result when the freight train is programmed to take the goods loop. Although the freight train allows one passenger train to pass it, the ‘first-come, first-served’ algorithm gets the freight train out of the goods loop fairly promptly.

Fig. 10: Delay 30 minutes: First-come, first-served (using the goods loop)

### Results from the Guided Search Algorithm and Fast Simulator

The guided search algorithm has been applied on a different arrangement of trains, with a different time horizon, and a different cost evaluation function. In this section there are 16 trains, a mix of fast and slow passenger trains and two goods trains. The time horizon is chosen as 60 minutes, to ensure that trains can exit the network. Two (fictitious) stations have been introduced to provide additional interest and to provide for some recovery time in the timetable. It was originally intended that the station stops could be used to allow the cost function to include a penalty for missed connections, but this has not been used so far.

The examples shown in this subsection follow a different pattern from those above. The hourly service has 2 freight trains per hour, 4 express passenger trains on the up line (top to bottom in the figures) and various stopping passenger services. There are neither freight nor express passenger services on the down line, but the main point of interest is provided by the goods loop and its use to reorder trains from top to bottom on the figures. Trains enter the network at the boundaries at a chosen time and with a chosen speed.  The source of primary delay is the freight train arriving late. However, in contrast to the situation used for the genetic algorithm, the late arriving freight train is timed to appear between the passenger trains arriving on the same track i.e. the passenger trains are not held back in a queue but are assumed to have got ahead of the late freight train somewhere outside of the network. In these examples an explicit nominal timetable exists with network arrival times and speeds, station arrival and departure times, and nominal times for passing certain other timing points (the signals controlling access to the junction in this case). Having the times for points within the network is critical for the search method to be made efficient – to be discussed later.

In Fig. 11 the trains follow their normal timetabled paths and station stops. The freight trains are shown in blue, the express passenger trains in green, and the remainder in black. Note that the trains leave the stations at the timetabled times but arrive slightly early because of recovery time in the timetable.

Fig. 11: Nominal timetable

The disturbance scenarios examined here is that the freight train appears in the network 5 minutes and 25 minutes late. The graphs coming from the optimisation search are shown in Fig. 12  and Fig 13 respectively. In Fig. 12 the freight train now follows a stopping passenger train from Worcester rather than passing ahead of this train. Note that if the freight train was to run 7 minutes late it would be diverted into the goods loop.

Fig. 12: Freight train delayed by 5 minutes

Fig. 13 shows the freight train delayed by 25 minutes. It is now so delayed that it does not give way to the fast passenger train even though the passenger train is weighted 6 times more highly than the freight train. It is likely that the fast passenger train would be given priority over the freight train on a real railway despite the lateness of the freight train. This suggests that a simple weighted sum of delay is not appropriate when some trains are running particularly late. Such a disturbance might be regarded as a situation in which the desire to reduce the delay of the freight train may depend on the cause of the original delay. If the original delay was caused by the train operator, the track operator may be entitled to count this late joining to the network as defining new timings through the rest of the freight train’s journey. However, if the cause of the delay lies with the track operator, it may be worthwhile reducing the delay at the expense of a passenger train to mitigate financial penalties.

Fig. 13: Freight train delayed by 25 minutes

Fig. 14: Freight train delayed by 8 minutes, passenger train by 5 minutes

Fig. 14 shows the freight train arriving 8 minutes late at the same time as a passenger train from Worcester arrives 5 minutes late. These two trains reach the junction at the same time with an express passenger train directly behind the freight train. The solution is to park the freight train in the goods loop and allow both passenger trains to pass. As far as is known, routing decision algorithms found in use on real railways only arbitrate between pairs of trains so the existence of a third train is ignored. Fig. 15 shows a similar situation where the freight train and two passenger trains compete to use the junction at the same time. This time the trains to and from Worcester use the short piece of common track in the opposite order to that in the previous example. The fast passenger follows a slower train, causing it to be delayed as the slower train waits at the station. The freight train exits the goods loop after the fast passenger train. The slow passenger train is allowed ahead of the fast passenger train because they are equally weighted and the slow train is behind schedule. Allowing the slower train to recover some lost minutes outweighs the resulting delay to the fast train. A change in weighting should change this behaviour. One important issue is that the fast passenger train leaves the network right behind the slow passenger train and subsequent delays are likely for the fast passenger train. This is one of the short-comings of the limited extent of the network around the junction.

Although Abbotswood Junction is one junction, additional complications arise because of the common piece of track on the route to Worcester. The simulation has no difficulty in generating the possible configurations of trains through the junction using the defined route interlocking rules – it does not require explicit understanding of the junction layout.

Fig. 15: Three trains compete for the junction

The results presented in this section involve a considerable number of trains over a one hour time horizon. Despite the huge number of possibilities of possible routing decisions (definitely more than 100,000 at which point the computer runs out of memory) the search algorithm finds the best solution in around 7 seconds (on a 3 GHz PC with a single processor). This is unexpectedly fast considering that a problem with 7 trains over a 30 minute prediction horizon was solved in around 1 second. It suggests that the guided search algorithm wastes little time following up useless solutions and spends most of its time on the right ‘track’.

5.3 Comparisons

It was originally intended that the guided search method should be compared to the genetic algorithm results on the same problem. However, there are significant differences between the two methods that make a fair comparison difficult. The primary practical difference is the way in which the two cost functions are defined. The guided search method requires certain conditions to be met by the cost function, in particular that the cost is available at any time. This is not the case for the genetic algorithm.

The examples used in both methods have as their primary cause of delay a freight train arriving late. However, different assumptions were then made about the subsequent order of arrival of trains on the same track. For the genetic algorithm it was assumed that the trains due to follow the freight train retain their original order. Therefore, a delayed freight train is followed by delayed passenger trains. Note that the genetic algorithm does not have any notion of the arriving trains being late as it does not have a nominal timetable. The guided search assumes that a freight train arrives late and is fitted into the train arrival order wherever it most conveniently fits. A following passenger train may have to be slightly delayed so that the trains do not run into one another before the signalling system can gain control of the trains. The actual arrival order and timing of trains on the real network depends on the behaviour outside of the region under consideration. The guided search method requires the existence of a nominal timetable against which it compares the progress of trains. The genetic algorithm simply tries to get the trains through the network in a minimum (train type)-weighted time.

Despite these caveats, some broad-brush comparisons of the Genetic Algorithm (GA) and Guided Search (GS) methods are made in Table 2. The results are given in weighted delay minutes, where passenger train delay has a weight of six and freight train delay has a weight of one. It can be seen that the GA and GS approaches have a broadly similar delay multiplier when similar delays are considered. The inefficiency of first in first out (FIFO) decision rules is illustrated by the GA results for Figures 9 and 10. The GS method provides particularly efficient results when both the freight and passenger trains are late (Figures 14 and 15).

Table 2: Estimated Primary and Reactionary Weighted Delays (rounded to the nearest minute).

|  |  | Primary Weighted Delay (P) (mins) | Primary and Reactionary Weighted Delay (P+R) (mins) | Delay Multiplier (P+R)/P |
| --- | --- | --- | --- | --- |
| GA | Figure 8 | 30 | 65 | 2.17 |
| GA | Figure 9 | 30 | 180 | 6.00 |
| GA | Figure 10 | 30 | 137 | 4.56 |
| GS | Figure 12 | 5 | 10 | 2.00 |
| GS | Figure 13 | 25 | 54 | 2.16 |
| GS | Figure 14 | 38 | 48 | 1.26 |
| GS | Figure 15 | 37 | 42 | 1.14 |

The idea of optimisation is to find a solution that minimises the cost or in this case the total weighted delay.  In many case, finding a ‘sufficiently’ low cost may be satisfactory, particularly when finding the true minimum cost takes much longer than finding a solution that is satisfactory. A rarely considered option is to trade optimality for robustness of the solution in the face of system uncertainties. In the train delay case the best solution may squeeze many trains through a junction at the limit of the signalling system in such a way that subsequent delays are much more serious than perhaps is the case for other solutions. Again, the best solution may result in a situation where a train passing a signal at danger results in a disaster where another slightly higher cost solution increases train separation. The cost function may be modified so that additional safety margins are enforced, or the optimisation routine may deliver several solutions from which the most robust is chosen, or a solution may be made robust by inserting delays into train movements where possible so that trains run further apart. Changes to the cost function or robustness requirements should be incorporated in parallel with the development of the optimisation procedure so that the procedure continues to be usable.

6. Conclusions

Current regulation strategies in use in the British rail industry are essentially pre-calculated and encapsulated in methods such as margin tables.  This paper has examined the possibilities for elaborating this essentially heuristic approach, but has also examined in depth, the feasibility of using true optimising search procedures.  A single, but fairly complex, junction was chosen as a test case, although some consideration was given to the study of larger areas.  A first attempt using a Genetic Algorithm to minimise weighted train delays and a detailed underlying simulator, showed that it is possible to find solutions this way.  The computing time required, however, rules out this method for real-time application.

An alternative method was tried using a guided search approach, whereby unpromising scenarios are quickly abandoned without wasting time completing the simulation.  Furthermore, a simpler, faster (but less accurate) simulator was introduced.  The results are promising in that valid (i.e. what an expert would do) solutions can be found in real-time.  The future challenge is primarily to co-ordinate this type of approach for a larger area with many routes. For example, researchers at the Technical University of Braunschweig  have successfully simulated a sector of Deutsche Bahn AG that involves 104 stations and more than 1000 daily train movements using Petri nets and genetic algorithms (Wegele and Schnieder, 2004). Similarly, D’Ariano and Pranzo (2007) have developed the ROMA dispatching system to minimise the propagation of delays on the Utrecht-Den Bosch network (the Netherlands), whilst Luethi (2007) has examined real time rescheduling in the Lucerne area (Switzerland).  Follow on work will be pursued in two ongoing RRUK projects on human-automation interactions in rail network control (project B6) and determining the costs of delay to different train types (project C6).

References

AEAT (2005) Automatic Route Setting (ARS) AEA Technology website www.aeat.co.uk/rail

Armstrong, J.H. (1998). The Railroad, What It Is, What It Does (4th ed.), Omaha: Simmons-Boardman

D’Ariano, A. and Pranzo, M. (2007) An Advanced Real-time Dispatching System for Minimizing the Propagation of Delays in a Dispatching Area Under Severe Disturbances. Presented to the Second International seminar on Railway Operations Modelling and Analysis. Hannover.

De Fontgalland, B. (1984) The World Railway System, University Press, Cambridge, 1984.

Goodman, C. and Ueda, N. (2004) Optimisation of Disturbed Traffic in Metro-Type Railways. Mimeo. Railway Research Centre. University of Birmingham.

Goodman, C., Preston, J., Weston, P., Takagi, R., Armstrong, J. and Bouch, C. (2006) Decision Support System for the Dynamic Re-scheduling of Trains under Disturbance. Final Report. RRUK/B1/3.

Hall, S. (2001). Modern Signalling Handbook, (3rd ed.), Ian Allan 	Publishing, Hersham, 2001.

Luethi, M. (2007) Evaluation of an Integrated Real-Time Rescheduling and Train Control System for Heavily Used Areas. Presented to the Second International seminar on Railway Operations Modelling and Analysis. Hannover.

Mellitt, B., Goodman, C. J. and Arthurton, R. I. M. (1978) Simulator for studying operational and power-supply conditions in rapid transit railways. Proc. IEE, Vol. 125, No. 4, pp.298-303.

Network Rail (2003) 2003 Technical Plan.  Section 10: Operational Performance.  Available from

http://www.networkrail.co.uk/cache/da746ddd58f844f3b1f7f212c47273e6.pdf [Accessed 31 August 2004].

Network Rail (2005a) The Network Code, 1st August 2004 amended 4th May 2005

Network Rail (2005b)  Business Plan: Management Plan http://www.networkrail.co.uk/Documents/BusinessPlan2005/B%20%202005%20Management%20Plan.pdf  [Accessed 28 April 2005].

NIST (National Institute of Standards and Technology) (2006) Dictionary of Algorithms and Data Structures. http://www.nist.gov/dads/HTML/Levenshtein.html

Rothlauf, F. (2002)  Representations for Genetic and Evolutionary Algorithms.  Physica-Verlag, Heidelberg, Germany.

Simmons, J. and  Biddle, G. (eds.). (1997)  The Oxford Companion To British Railway History, University Press, Oxford, 1997

Siu, L. K. and Goodman, C. J. (1992)  An object-oriented concept for simulation. Proc. COMPRAIL 1992 International Conference, Washington DC, USA.

Siu, L. K.(1995) An Object-oriented Railway System and Power Network Simulator. PhD Thesis, University of Birmingham.

SRA (2003) Network Utilisation Strategy http://www.sra.gov.uk/pubs2/stratpolplan/cup1/nus [Accessed 28 	April 2005].

Wegele, S. and Schnieder, E. (2004) Automated Dispatching  of Train Operations suing Genetic Algorithms. In Allan, J., Brebbia, C.A., Hill, R.J., Sciutto, G. and Sone, S. (Eds) Computer in Railways X. Southampton: WIT Press.

White, T. (2003) Elements of Train Dispatching Vol. 1, VTD Rail Publishing, Mountlake Terrace.

# Footnotes

For more details see: http://portal.railresearch.org.uk

Now Deltarail