Which costs for urban sustainable mobility? A four French cities comparison

Damien VERRY

Verry@entpe.fr

Phd student

Laboratoire d’économie des Transports ENTPE.

Rue Maurice Audin 69518 Vaulx-en-Velin cedex FRANCE.

Tel 33-4-72-04-77-66

Abstract

Territory attractivity is more and more evaluated with sustainability  criterion. This papers proposes a methodology that allows to compare pollutants emissions, consumptions and household monetary expenditure related to urban trips between four French urban area. To evaluate sustainability we try to connect, in a quantitative way, practices and mobility  behaviour  with environmental and economic costs. Four DEED (Diagnostics Energie Environnements Deplacements) based on COPERT III european model are calculated with mobility data from four household survey trips which describes mobility of more than 60 000 dwellers inquired on their trip made the day before.

The results shows if that differences exist between and inside agglomerations, environmental costs, especially CO2 emissions, are too high to reach France targets in greenhouse emissions level.  Disparities between household suggest that dwellers which can afford it try to maximize their accessibility   whereas the other try to reduce their transport consumption.

Key words : Urban mobility, CO2 emissions, household survey trips, household expenditure ,

Paris, Bordeaux, Lyon, Grenoble

# Introduction

The capacity of current transport system to satisfy on the long-term  needs for mobility with environmental and social cost bearable in urban area is questioned  by the increase in private motorised mobility. The regulation policies which tackle  with these issues are found under the generic name of sustainable mobility. “Sustainable mobility is a term that summarises what is at stake in contemporary attempts to redress the balance of costs and benefits in the transport sector. It marks a shift away from the traditional transport planning approach, which conceptualised transport as a derived demand and as a support infrastructure for economic growth, towards a policy approach that is informed by evidence and risk assessment and which recognises the pitfalls of unconstrained growth” (Giorgi, 2003, p 201). Many works in transportation research field deals with environmental impacts of daily mobility in urban area. Newman and Kenworthy show through international cities comparison that the quantity of fuel necessary to satisfy the need of  mobility of American north cities dwellers could be 8 times more important than those of Asian cites. This research which had strong repercussion for transport and land-use experts stigmatises environmental costs of urban spreading and advises to make  cities more compact and to develop efficient  public transport. This empirical work continues to provoke methodological discussions (Van de Coevering, Schwanen, 2006 ; Mindali et al., 2004) and conceptual issues (Gordon, Richardson, 1997). These results were used as starting points by many studies which aim to explain the level of private mobility (most often measured by vehicles-km) by multiple factors: urban form, households socio-economics characteristics, price and quality of transport offer. These studies which tempt to clarify the relations between urban systems components are  methodologically limited  by the explanatory variable interdependence, the level of complexity makes difficult to establish any univocal causality links (Handy, 2005). But with growing concerns about climate change and energy prince increase, the question should rapidly become how current urban system transport could afford new sustainability costs without scarifying  urban accessibility ?  With growing concerns about climate change and energy prince increase, we are certainly passing from a world of choices to a world of constraints.

According to us,  very little empirical studies  have tried to evaluate a system of transport with holistic perspective of sustainable development in terms of constraints. The article, which  is a first methodological step of a PhD research, is centred on the question of mobility costs, view as the constraints, and try to describe the link between travel behaviour and mobility costs in four French cities. To our knowledge, no empirical studies have compared mobility cost produced by different French cities. The aim of this paper is to know if in a homogenous context of French cities the urban transport system produces different costs of mobility and if it possible to measure it in quantitative way. In this first step, we don’t try to explain the different  private travel behaviour which characterize each city, but we try to show how these differences influence the cost of urban  mobility.

First part consist of the conceptual framework adopted to define sustainable mobility and the methodology used to answer the questions. The work is based on the use of four household travel survey (Lyon 1995, Bordeaux 1998, Paris 2002, Grenoble 2002). More than 55 000 people describe all the trip that they have made the day before the survey. The environmental and economic costs of each system of transport are calculated from this data.

This is followed by the presentation of the results and more particularly those about pollutant emission and household expenditure which are detailed according to households  localization  and  level of incomes. Secondly, brief analysis comment the main results and deal with the question of the choice of analyse spatial area.

# Conceptual framework: assessing sustainable mobility

An agglomeration can be divided in three subsystems (Bonnafous and Puel, 1983, p 44):

- A subsystem of localisation

- A subsystem of social practices and relations

- A subsystem of displacements

Those three subsystems could be linked by the concept of accessibility (Geurs and Ritsema, 2001)  defines as "a local measurement of the facility to reach  place starting from one or several places, for a motivation related to a need and by one or several means of transport" (Bloy and al. 1976)".  We use this schematic conception of city to define our approach of sustainable mobility. We define sustainable mobility at macroscopic level  in a systemic approach with measurements built on the microscopic levels. We define a transport system associated to population given as the set of trips made by the population and the set of infrastructures and services which allow this mobility. This definition can be held at international, national or urban level and for each time period given.

This system of transport is characterized then via three notions:  those of need, cost and service.

- The needs are defined through a measure of  "mobility". The mobility is at the same time perceived like a satisfaction of a need, the system of transport like a response to a demand, and the generation of a need, the system of transport generated by a demand.

- The costs represent all  the counterparts generated by the system of transport considered. The costs are taken in a multidimensional point of view: the environmental impacts, the monetary costs, the disparities of access are considered. The transport system produces some costs and the way of these costs are afforded influence the transport system.

- The services are defined through a measure of accessibility. Accessibility characterizes the service provides by the system considered, as a finality of the system, it is the level of accessibility required which determines the nature of the system.

Consequently, we measure the sustainability of a system of transport through balance between the concepts of needs, costs and services attached to the system considered.

In this article, we are specially interested in constraints that sustainability could lead, and we will try to determine empirically current cost of urban mobility in four French cities to know if growing interest in climate change have started to change travel behaviour. The main idea of this methodological work is to use individual data to calculate average cost for each city. We try to understand how household choices in localization and transportation influence those costs.

# Methodology

## Data

This research is based on the exploitation of four household trip survey: Lyon 1995, Bordeaux 1998, Paris 2002 and Grenoble 2002. These survey follow a standard nation wide procedure  supervised by CERTU (CERTU, 1998). Households inquired, who are representative or the area under study, must describe all the trips they have made the day before the survey and precise the reason for moving and the means use. A  socio-economic description of each household is also given and the characteristics of cars are also asked. One of the objectives of this work is to estimate mobility cost at the  macroscopic level by aggregating this individual data .

It is important to notice that only the trip which are inside the study area are taken account, for people who go outside this perimeter we don’t estimate environmental costs. The four selected cities chosen have different size,  the population in Lyon, Bordeaux and Grenoble are quite similar because of difference for study perimeters.

Table 1 Household trip surveys used

|  | Paris (2002) | Lyon (1995) | Bordeaux (1998) | Grenoble (2002) |
| --- | --- | --- | --- | --- |
| Individuals inquired | 23 656 | 13 996 | 11 321 | 17 254 |
| Population estimated | 10 049 401 | 1 195 131 | 801 302 | 711 584 |
| Trips inquired | 82 586 | 53 213 | 40 406 | 67 254 |
| Trips estimated | 35 160 034 | 4 659 777 | 2 869 941 | 2 782 616 |
| Study area (km²) | 12 072 | 1 057 | 1 724 | 3 493 |
| Density (cap/km²) | 832 | 1131 | 465 | 204 |

## Vehicles description

The first step to estimation pollutant emission is to characterise precisely the private vehicle owned by the household surveyed. The vehicle are described in the survey  by their age, their engine rating and by the fuel which they use. To evaluate pollutant emission is also necessary to know the capacity of the vehicle. The three capacity classes needed to the model are simulated with the data of age, engine rating and fuel use under nation average distribution given by the INRETS studies. With all this information we can create 42 types of car which are used to calculate pollutant emissions (see annex 1).

## Distance, time and speed of trips

Mobility characteristics are calculated as the usual way from the household travel surveys (Gallez,Hivert, 1996, ADEME, 1998). Two set of data are created from the information given for each trips (origin, destination, mode…). In the first one the distance are calculated by GIS on the finest spatial division, the time is the time declared and the speed is the division of the distance by the time. This first set is used to determine the whole time spent by the household in the transport. The second set is used to calculate pollutant emission. As we know the origin and the destination of each trips, we use a traffic model, Davisum, to estimate average speed and distance. The two set are different because for example in the first one we take in transport time, the time to walk to reach a car, whereas we count only the time spent in the car. The second one is more precise to calculate emission and allow to take in consideration the congestion effect but not necessarily to estimate the real time lost in transport by the household.

Table 2 Distance, time and speed for an average (median) trip  (all modes)

|  | Time declared | Time modelled |
| --- | --- | --- |
|  | Distance (km) | Time (min) | Speed (km/h) | Distance (km) | Time (min) | Speed (km/h) |
| Lyon | 3,8 (2, 1) | 17,2 (15,0) | 15.4 (11,4) | 3.7 (2.0) | 15,8 (10,0) | 15.1 (14, 1) |
| Bordeaux | 5.6 (3.8) | 16,9 (11,0) | 23,3 (17.9) | 6, 1 (4,2) | 14,4 (10,0) | 25,7 (22,2) |
| Grenoble | 4,7 (1.7) | 16,2 (10,0) | 17,0 (11,5) | 4.9 (1.7) | 12,8 (10,0) | 20,5 (15,0) |
| Paris | 4.9 (1,7) | 17,8 (13,5) | 13,4 (8,0) | 4.9 (1,7) | 17,8 (13,5) | 13,4 (8,00) |

Source : : calculated from  Household Travel Survey Lyon 1995, Bordeaux 98, Grenoble 2002 and Paris 2002

The data show important differences: the trips in Bordeaux are longer and faster than in the other cities. Displacements are almost half slower in Paris than in Bordeaux. The Parisians even if they move on shorter distances spend more time in transport than the inhabitants of Bordeaux. The proximity trips are relatively fewer in Bordeaux. The time devoted to daily mobility is more constant than the other parameters.

## Pollutant emission and consumption

We follow the main hypothesis of the DEED methodology to estimate pollutant emission (ADEME, 1998). CO – carbon monoxide, NOx – nitrogen oxides, VOCs – volatile organic compounds, PM – particulate matter, CO2– carbon dioxide emissions, and fuel consumption are estimated for each motorized trip (public transport and two wheels included).Emission and consumption equations are given by COPERT III (Ntziachristos, Samaras, 2000) and we have made all the calculus under SAS system (SAS institute inc.). This method consider hot and cold emissions for the 42 types of vehicles . By convention, all the emissions are affected to the driver of the vehicle. For each trip,  he model takes into account mean of transport, total distance, distance driven with cold engine, average speed, ambient temperature and occupancy rate (only for public transport). For soft means of transport (walk, cycle) the emissions and consumption are considered as null.

## Monetary expenditure

To estimate the household expenditure for urban mobility we have used the methodology developed by Gallez (2000, pp 85-112) and (Nicolas and al., 2003). This empirical methodology try to estimate for each household the percentage of income devoted to urban mobility. If the variable costs (fuel, maintenance, parking) could be directly estimated from the data given by the traffic models, fix costs have to be calculated with other data sources. We used the results of the National Household Consumption Survey (INSEE, 2001) to estimate those costs and the National Transport and Communication Survey to determine the share of urban mobility in household mobility.

Table 3 Annual household expenditure by vehicles (euros 2001)

|  | Paris (2001) | Lyon (1995) | Bordeaux (1998) | Grenoble(2001) |
| --- | --- | --- | --- | --- |
| Purchase | 1 377 | 1 333 | 1 209 | 1 180 |
| Fuel | 906 | 1 233 | 1 230 | 1 031 |
| Maintenance | 728 | 676 | 1 104 | 856 |
| Insurance | 504 | 455 | 436 | 434 |
| Parking | 217 | 257 | 169 | 161 |
| Taxes, fees | 48 | 58 | 30 | 42 |
| Total | 3 780 | 4 013 | 4 178 | 3 705 |

Table 4 Annual household expenditure by vehicles-kilometres (euros 2001)

|  | Paris (2001) | Lyon (1995) | Bordeaux (1998) | Grenoble(2001) |
| --- | --- | --- | --- | --- |
| Purchase | 0,123 | 0,097 | 0,063 | 0,082 |
| Fuel | 0,081 | 0,090 | 0,064 | 0,072 |
| Maintenance | 0,065 | 0,049 | 0,057 | 0,060 |
| Insurance | 0,045 | 0,033 | 0,023 | 0,030 |
| Parking | 0,019 | 0,019 | 0,009 | 0,011 |
| Taxes, fees | 0,004 | 0,004 | 0,002 | 0,003 |
| Total | 0,337 | 0,291 | 0,216 | 0,258 |

Source : : calculated from  Household Travel Survey Lyon 1995, Bordeaux 98, Grenoble 2002 and Paris 2002, National Household  Consumption survey 1995, 2001

# Results

After this work of calculation based on data from more than 66 000 people, we can compare the environmental and economic costs of mobility between the different cities.

## Average environmental costs and travel demand

For the environmental costs, we consider pollutants emission and fuel consumption. All the results are given by capita and for a average day of week.

Table 5 Daily pollutants emissions and individual mobility behaviour

|  | Lyon (1995) | Bordeaux (1998) | Grenoble (2002) | Paris (2002) |
| --- | --- | --- | --- | --- |
| Distance budget (km) | 13,8 | 21,5 | 19,2 | 21,8 |
| Time budget (min) | 64 | 67 | 63 | 79 |
| Consumption (gep/cap/day) | 727 | 940 | 818 | 673 |
| CO2 emissions (g/cap/day) | 1950 | 2741 | 2402 | 1978 |
| CO emissions (g/cap/day) | 153 | 109 | 63 | 65 |
| VOC emissions (g/cap/day) | 19 | 15 | 8 | 7 |
| NOx emissions (g/cap/day) | 15 | 21 | 14 | 8 |
| VP emissions (g/cap/day) | 0,9 | 1, 1 | 0,7 | 0,6 |

Source : Household Travel Survey Lyon 1995, Bordeaux 98, Grenoble 2002 and Paris 2002

The analyse of travel behaviour shows that daily individual distance budget is the highest in Paris but quite close from Bordeaux which can be quite surprising when we compare the size of the two towns. Parisians spend everyday  more than fifteen minutes that resident in Grenoble or in  Lyon in transports.

In term of pollutants emissions strong differences have to be noticed between cities. For the local pollutants (CO, VOC, NOx, PM),  emissions are the highest in Lyon, where the survey is the oldest. The nature of the fleet vehicle should explain these differences.

For the consumption and CO2 emission,  Paris and Lyon residents emit less than 40% of Bordeaux resident and 20% for Grenoble resident. Paris is the conurbation that allows to satisfy his needs of mobility with the lowest rate of CO2 emission (1978g/capita/day), on the contrary Bordeaux  is the urban area where the dwellers emit the most of CO2 (2741g/capita/day). The little surprise is that even if Parisian move on average at longer distance, the environmental cost that they produce are lower. The modal share could  explain these differences, in Lyon and Paris the use of public transport allow to reduce emission even if many people who live in suburbs have to drive on longer distance. The first conclude is even in a homogenous context,  environmental costs are very different between the four agglomerations.

## Average economics costs

The results on the levels of household monetary expenditure reveal some homogeneity between agglomerations. In average, for their urban and daily mobility the households of the four studied agglomerations spend between 2400 and 2800 euros per year.

Table 6 Annual household expenditure (euros 2001/household)

|  | Paris (2001) | Lyon(1995) | Bordeaux (1998) | Grenoble (2001) |
| --- | --- | --- | --- | --- |
| Urban public transport | 339 | 203 | 61 | 70 |
| Other public transport | 50 | 50 | 54 | 96 |
| Two wheels | 43 | 8 | 29 | 11 |
| Personal vehicles urban trips | 2352 | 2086 | 2441 | 2552 |
| Urban mobility | 2785 | 2347 | 2584 | 2728 |

In Paris and Lyon where motorization rate are lower, the expenditure for private vehicle are compensated by urban public expenditure.

## Travel demand, mobility cost and access for household by level of income and residence area

First results are the average costs calculated for each system, the question is to know if these averages do not hide strong disparities between household inside a same system.  We try to know which effects can have income and localisation on household cost of mobility.

We have divided each agglomeration  into three concentric circles: center, 1st ring, 2nd ring.  The center corresponds to the historical city of urban area. The 1st ring is composed by all the towns around the historical city, the 2nd ring regroup all the other towns. The household are also divided in three equal levels of income. For the four agglomeration, travel demand, mobility cost and access for nine type of household are analysed in the table 7, 8, 9 and 10.

The need of mobility are measured by number of daily trips, the individual distance budget, the distance covered in private vehicle and public transport. The mobility costs are measured by the individual time budget, the CO2 emission and the expenditure for urban mobility. Accessibility is measured by the motorization rate, the average trip distance, the average time trip, the average speed and the % of income devoted to urban mobility.

The first result is that, in the French context, the differences for mobility costs are higher inside each city than between them. For example, a resident of Grenoble who lives in the centre emit only 1363 g of CO2 a day whereas a resident of Grenoble who live in the second ring will emit more than 3209 g of CO2 a day. In the same time,  the difference between Paris wich is the conurbation that allows to satisfy his needs of mobility with the lowest rate of CO2 emission (1978g/capita/day) and Bordeaux which  is the urban area where the dwellers emit the most of CO2 (2741g/capita/day) are lower. More the households live far from the center more they spend to move and their CO2 emission are important.

Result show that people who have choice (highest household income) not to try to minimize their mobility costs but to maximize their access to urban amenities. Their % of income devoted to urban mobility are quite low (about 6-7%), they spend most time in transport than the other, they spend more money to satisfy their mobility needs, they move faster  and more often by cars. Their average trip distance is high that shows that they don’t search proximity. Consequently, their CO2 emissions are the highest, and often rich household who live in 2nd ring emit twice more CO2 a day than average household in the agglomeration.

On the other hand, we  note that % of income devoted to urban mobility for household with low income could reach more that 20%. We can assume that many of them could not pay more for urban daily mobility, they are in a logic of minimization. They use more public transport (except in Paris where rich people use  more), they move on shorter distance and more slowly.  Conseqently, their CO2 emission are lower and they spend less to their mobility.

Table 7 Travel demand, mobility cost and access for household in Paris by level of income and residence area

| Paris | Level income | Number of resident | Motorization rate (veh/ household) | Average income (euros /year/household) | Distance Budget (km/cap/ day) | Time budget (min/cap/ day) | Vehicle distance (km/ cap/day) | Public transport distance (km/cap/ day) | Numbers of daily trips(trips/ cap/day) | Average trip distance (km) | Average time trip(min) | Average speed (km/h) | CO2 Emission (g/cap/day) | Urban mobility expenditure (euros/year/ household) | % of income devoted to urban mobility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Centre | Poor | 643 358 | 0,29 | 13 036 | 12,4 | 76,1 | 2,7 | 6,0 | 3,5 | 3,6 | 22,0 | 9,8 | 453 | 873 | 6,7% |
|  | Middle | 551 980 | 0,49 | 26 998 | 14,3 | 79,6 | 4,5 | 5,7 | 3,6 | 4,0 | 22,1 | 10,8 | 871 | 1 289 | 4,8% |
|  | Rich | 775 234 | 0,80 | 63 847 | 18,0 | 84,5 | 7,9 | 5,9 | 3,7 | 4,8 | 22,5 | 12,8 | 1 482 | 2 295 | 3,6% |
|  | All | 1 970 572 | 0,54 | 37 259 | 15,1 | 80,4 | 5,2 | 5,9 | 3,6 | 4,2 | 22,2 | 11,3 | 975 | 1 516 | 4,1% |
| 1st ring | Poor | 1 535 682 | 0,69 | 16 495 | 15,3 | 75,0 | 6,3 | 4,3 | 3,3 | 4,7 | 22,9 | 12,2 | 1 126 | 1 832 | 11,1% |
|  | Middle | 1 145 576 | 0,96 | 29 062 | 19,5 | 82,4 | 9,8 | 4,0 | 3,5 | 5,7 | 23,8 | 14,2 | 1 876 | 2 611 | 9,0% |
|  | Rich | 1 009 395 | 1,33 | 61 464 | 22,5 | 85,7 | 13,3 | 3,9 | 3,6 | 6,3 | 24,0 | 15,7 | 2 726 | 3 952 | 6,4% |
|  | All | 3 690 653 | 0,96 | 33 530 | 18,6 | 80,2 | 9,3 | 4,1 | 3,4 | 5,4 | 23,5 | 13,9 | 1 796 | 2 679 | 8,0% |
| 2nd ring | Poor | 1 735 327 | 1,04 | 18 194 | 22,4 | 71,3 | 13,3 | 4,5 | 3,3 | 6,9 | 21,8 | 18,8 | 1 810 | 2 708 | 14,9% |
|  | Middle | 1 420 992 | 1,32 | 31 421 | 27,6 | 77,9 | 18,1 | 4,6 | 3,4 | 8,1 | 22,8 | 21,3 | 2 665 | 3 621 | 11,5% |
|  | Rich | 1 231 857 | 1,69 | 64 014 | 34,7 | 88,3 | 23,6 | 5,6 | 3,6 | 9,6 | 24,3 | 23,6 | 3 576 | 5 015 | 7,8% |
|  | All | 4 388 176 | 1,32 | 36 360 | 27,5 | 78,2 | 17,7 | 4,8 | 3,4 | 8,1 | 22,9 | 21,1 | 2 582 | 3 684 | 10,1% |
| All area | Poor | 3 914 367 | 0,74 | 16 403 | 18,0 | 73,6 | 8,8 | 4,6 | 3,3 | 5,4 | 22,3 | 14,7 | 1 318 | 1 961 | 12,0% |
|  | Middle | 3 118 548 | 1,00 | 29 539 | 22,3 | 79,8 | 12,6 | 4,6 | 3,5 | 6,4 | 23,1 | 16,8 | 2 057 | 2 722 | 9,2% |
|  | Rich | 3 016 486 | 1,36 | 63 124 | 26,3 | 86,5 | 16,1 | 5,1 | 3,6 | 7,2 | 23,7 | 18,3 | 2 753 | 3 854 | 6,1% |
|  | All | 10 049 401 | 1,04 | 35 546 | 21,8 | 79,4 | 12,2 | 4,8 | 3,5 | 6,3 | 23,0 | 16,5 | 1 978 | 2 785 | 7,8% |

Source: Household Travel Survey Paris 2001

Table 8 Travel demand, mobility cost and access for household in Lyon by level of income and residence area

| Lyon | Level income | Number of resident | Motorization rate (veh/ household) | Average income (euros /year/household) | Distance Budget (km/cap/ day) | Time budget (min/cap /day) | Vehicle distance (km/ cap/day) | Public transport distance (km/cap/ day) | Numbers of daily trips(trips/cap/day) | Average trip distance (km) | Average time trip(min) | Average speed (km/h) | CO2 Emission (g/cap/day) | Urban mobility expenditure (euros/year/ hsld)) | % of income devoted to urban mobility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Centre | Poor | 176 544 | 0,60 | 12085 | 9,5 | 67,7 | 5,4 | 3,0 | 3,9 | 2,5 | 17,4 | 8,4 | 1 022 | 1 231 | 9,4% |
|  | Middle | 169 493 | 0,86 | 22719 | 11,2 | 68,3 | 7,5 | 2,6 | 4,0 | 2,8 | 16,9 | 9,8 | 1 513 | 1 617 | 6,6% |
|  | Rich | 184 128 | 1,33 | 51096 | 11,3 | 64,1 | 8,4 | 1,9 | 4,2 | 2,7 | 15,1 | 10,6 | 1 693 | 2 738 | 5,0% |
|  | All | 530 166 | 0,93 | 28711 | 10,7 | 66,6 | 7,1 | 2,5 | 4,1 | 2,6 | 16,4 | 9,6 | 1 412 | 1 852 | 6,0% |
| 1st ring | Poor | 112 077 | 0,93 | 15985 | 11,2 | 61,6 | 6,9 | 3,3 | 3,7 | 3,0 | 16,8 | 10,9 | 1 441 | 1 970 | 11,4% |
|  | Middle | 81 204 | 1,13 | 24296 | 13,1 | 64,9 | 9,7 | 2,7 | 3,7 | 3,5 | 17,4 | 12,1 | 1 937 | 2 248 | 8,6% |
|  | Rich | 93 504 | 1,67 | 52321 | 16,9 | 69,5 | 14,4 | 2,0 | 4,2 | 4,1 | 16,6 | 14,6 | 2 794 | 3 967 | 7,0% |
|  | All | 286 785 | 1,24 | 30754 | 13,6 | 65,1 | 10,1 | 2,7 | 3,9 | 3,5 | 16,9 | 12,5 | 2 023 | 2 717 | 8,2% |
| 2nd ring | Poor | 131 622 | 1,24 | 18501 | 15,2 | 59,7 | 11,2 | 2,9 | 3,9 | 3,9 | 15,4 | 15,3 | 1 971 | 2 259 | 11,3% |
|  | Middle | 129 140 | 1,45 | 27704 | 17,9 | 57,1 | 14,9 | 2,2 | 4,0 | 4,5 | 14,4 | 18,8 | 2 623 | 2 620 | 8,8% |
|  | Rich | 117 418 | 1,86 | 53023 | 22,4 | 64,5 | 19,9 | 2,0 | 4,2 | 5,3 | 15,2 | 20,8 | 3 437 | 4 127 | 7,2% |
|  | All | 378 181 | 1,51 | 33216 | 18,4 | 60,3 | 15,2 | 2,4 | 4,0 | 4,6 | 15,0 | 18,3 | 2 649 | 2 988 | 8,3% |
| All area | Poor | 420 243 | 0,84 | 14661 | 11,7 | 63,6 | 7,6 | 3,1 | 3,8 | 3,1 | 16,6 | 11,1 | 1 431 | 1 667 | 10,5% |
|  | Middle | 379 838 | 1,08 | 24419 | 13,9 | 63,8 | 10,5 | 2,5 | 4,0 | 3,5 | 16,1 | 13,0 | 1 981 | 2 030 | 7,7% |
|  | Rich | 395 051 | 1,55 | 51882 | 15,9 | 65,5 | 13,2 | 2,0 | 4,2 | 3,8 | 15,5 | 14,6 | 2 472 | 3 384 | 6,0% |
|  | All | 1 195 131 | 1,15 | 30365 | 13,8 | 64,3 | 10,4 | 2,5 | 4,0 | 3,5 | 16,1 | 12,9 | 1 950 | 2 348 | 7,2% |

Source: Household Travel Survey Lyon 1995

Table 9 Travel demand, mobility cost and access for household in Bordeaux by level of income and residence area

| Bordeaux | Level income | Number of resident | Motorization rate (veh/household) | Average income (euros /year/household) | Distance Budget (km/cap/day) | Time budget (min/cap/day) | Vehicle distance (km/ cap/day) | Public transport distance (km/cap/ day) | Numbers of daily trips(trips/cap/day) | Average trip distance (km) | Average time trip(min) | Average speed (km/h) | CO2 Emission (g/cap/ day) | Urban mobility expenditure (euros/year/ hsld)) | % of income devoted to urban mobility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Centre | Poor | 73 018 | 0,58 | 7 811 | 13,8 | 76,3 | 8,0 | 3,8 | 3,7 | 3,7 | 20,4 | 10,8 | 1 551 | 932 | 11,5% |
|  | Middle | 54 513 | 1,01 | 21 537 | 14,6 | 71,3 | 10,7 | 2,1 | 3,8 | 3,9 | 18,9 | 12,3 | 1 880 | 1 652 | 7,4% |
|  | Rich | 60 411 | 1,32 | 45 062 | 17,3 | 75,2 | 14,5 | 1,3 | 4,0 | 4,3 | 18,6 | 13,8 | 2 474 | 2 374 | 5,1% |
|  | All | 187 942 | 0,91 | 22 991 | 15,1 | 74,5 | 10,9 | 2,5 | 3,8 | 3,9 | 19,4 | 12,2 | 1 943 | 1 554 | 6,5% |
| 1st ring | Poor | 130 055 | 0,98 | 10 367 | 16,3 | 63,2 | 12,0 | 2,9 | 3,3 | 4,9 | 18,9 | 15,5 | 2 054 | 1 693 | 15,7% |
|  | Middle | 164 759 | 1,46 | 24 694 | 19,2 | 62,2 | 16,4 | 1,5 | 3,4 | 5,7 | 18,4 | 18,5 | 2 534 | 2 757 | 10,7% |
|  | Rich | 139 821 | 1,65 | 46 525 | 22,5 | 68,9 | 20,4 | 1,2 | 3,7 | 6,0 | 18,5 | 19,6 | 3 270 | 3 447 | 7,1% |
|  | All | 434 636 | 1,37 | 28 130 | 19,4 | 64,7 | 16,4 | 1,8 | 3,5 | 5,6 | 18,6 | 18,0 | 2 627 | 2 653 | 9,1% |
| 2nd ring | Poor | 44 198 | 1,43 | 12 669 | 26,3 | 57,9 | 22,4 | 2,1 | 3,2 | 8,2 | 18,1 | 27,2 | 2 731 | 2 986 | 22,7% |
|  | Middle | 76 134 | 1,68 | 26 450 | 33,0 | 61,6 | 29,5 | 1,9 | 3,5 | 9,3 | 17,4 | 32,1 | 3 730 | 3 906 | 14,2% |
|  | Rich | 58 393 | 1,87 | 50 395 | 39,8 | 75,5 | 36,0 | 1,7 | 3,8 | 10,4 | 19,8 | 31,6 | 4 881 | 4 787 | 9,1% |
|  | All | 178 724 | 1,69 | 32 707 | 33,5 | 65,2 | 29,8 | 1,9 | 3,5 | 9,5 | 18,4 | 30,8 | 3 859 | 4 013 | 11,8% |
| All area | Poor | 247 271 | 0,89 | 9 629 | 17,3 | 66,1 | 12,7 | 3,0 | 3,4 | 5,0 | 19,3 | 15,7 | 2 026 | 1 573 | 15,7% |
|  | Middle | 295 406 | 1,41 | 24 409 | 21,9 | 63,7 | 18,7 | 1,7 | 3,5 | 6,3 | 18,2 | 20,6 | 2 722 | 2 769 | 10,9% |
|  | Rich | 258 625 | 1,61 | 46 938 | 25,2 | 71,9 | 22,5 | 1,3 | 3,8 | 6,6 | 18,8 | 21,0 | 3 448 | 3 439 | 7,1% |
|  | All | 801 302 | 1,30 | 27 487 | 21,5 | 67,1 | 18,1 | 2,0 | 3,6 | 6,0 | 18,7 | 19,3 | 2 741 | 2 589 | 9,1% |

Source: Household Travel Survey Bordeaux 1998

Table 10 Travel demand, mobility cost and access for household in Grenoble by level of income and residence area

| Grenoble | Level income | Number of resident | Motorization rate (veh/household) | Average income (euros /year/household) | Distance Budget (km/cap/day) | Time budget (min/cap/day) | Vehicle distance (km/ cap/day) | Public transport distance (km/cap/day) | Numbers of daily trips(trips/cap/ day) | Average trip distance (km) | Average time trip(min) | Average speed (km/h) | CO2 Emission (g/cap/day) | Urban mobility expenditure (euros/year/ hsld) | % of income devoted to urban mobility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Centre | Poor | 31 071 | 0,63 | 9 081 | 11,4 | 70,9 | 5,8 | 3,7 | 4,0 | 2,9 | 17,8 | 9,6 | 937 | 996 | 11,0% |
|  | Middle | 21 787 | 0,90 | 21 167 | 13,8 | 68,7 | 8,8 | 2,9 | 3,8 | 3,7 | 18,2 | 12,0 | 1 463 | 1 570 | 7,4% |
|  | Rich | 23 400 | 1,22 | 44 844 | 15,1 | 70,4 | 12,1 | 1,4 | 4,3 | 3,6 | 16,6 | 12,9 | 1 859 | 2 289 | 5,1% |
|  | All | 76 258 | 0,89 | 23 446 | 13,2 | 70,1 | 8,5 | 2,8 | 4,0 | 3,3 | 17,5 | 11,3 | 1 363 | 1 557 | 6,6% |
| 1st ring | Poor | 31 508 | 0,97 | 11 999 | 14,2 | 61,2 | 10,2 | 2,9 | 3,8 | 3,7 | 16,0 | 13,9 | 1 737 | 1 821 | 15,2% |
|  | Middle | 30 183 | 1,38 | 25 407 | 15,7 | 65,6 | 12,6 | 2,0 | 4,1 | 3,9 | 16,2 | 14,4 | 2 218 | 2 674 | 10,5% |
|  | Rich | 29 614 | 1,61 | 50 614 | 18,5 | 68,7 | 15,4 | 2,1 | 4,3 | 4,3 | 16,1 | 16,2 | 2 756 | 3 669 | 7,3% |
|  | All | 91 305 | 1,32 | 29 965 | 16,1 | 65,1 | 12,6 | 2,3 | 4,0 | 4,0 | 16,1 | 14,8 | 2 223 | 2 702 | 9,0% |
| 2nd ring | Poor | 41 363 | 1,52 | 15 791 | 21,0 | 54,5 | 17,2 | 2,5 | 3,6 | 5,7 | 14,9 | 23,1 | 2 356 | 2 901 | 18,4% |
|  | Middle | 45 654 | 1,53 | 26 670 | 23,5 | 58,7 | 20,4 | 1,9 | 3,8 | 6,3 | 15,6 | 24,0 | 2 988 | 3 146 | 11,8% |
|  | Rich | 40 654 | 1,79 | 50 702 | 28,0 | 63,7 | 25,5 | 1,7 | 4,0 | 7,0 | 16,0 | 26,4 | 3 707 | 4 355 | 8,6% |
|  | All | 127 671 | 1,61 | 31 680 | 23,9 | 58,7 | 20,8 | 2,1 | 3,8 | 6,3 | 15,5 | 24,5 | 2 976 | 3 452 | 10,9% |
| All area | Poor | 103 941 | 1,09 | 12 402 | 16,7 | 60,4 | 12,4 | 2,9 | 3,8 | 4,4 | 16,0 | 16,6 | 1 836 | 2 004 | 16,2% |
|  | Middle | 97 624 | 1,35 | 24 883 | 19,2 | 62,7 | 15,8 | 2,1 | 3,9 | 5,0 | 16,3 | 18,4 | 2 468 | 2 648 | 10,6% |
|  | Rich | 93 668 | 1,59 | 49 195 | 22,2 | 66,8 | 19,4 | 1,8 | 4,1 | 5,4 | 16,1 | 20,0 | 3 012 | 3 622 | 7,4% |
|  | All | 295 234 | 1,33 | 28 831 | 19,2 | 63,1 | 15,7 | 2,3 | 3,9 | 4,9 | 16,1 | 18,3 | 2 402 | 2 730 | 9,5% |

Source: Household Travel Survey Grenoble 2001

# Discussions

A fine description of the mobility  behaviours mobility of the four agglomerations brings interesting results on the various levels of CO2 emission and monetary expenditure measured. Analyse of results has not yet been finished but few remarks could start discussion .

First results make  possible to confirm internal differences already measured in French agglomerations (Hivert, 1994, 1998; Gallez, 1995, Fouchier, 1997). Central zones with high density know a mobility made up with short trips, a modal share in favour of  soft modes and public transport, car trips with  low speed (congestion) and finally relatively low level of CO2 emissions. The area far for centre with low density know the opposite situation. The  first question was to know which urban size has to be selected to compare cities and if finally it make sense to compare city with different size ?

## Scale of studies: does it make sense to compare different cities?

The four cities compared can be qualified as monocentric, density population is maximum in the center and decrease from center to suburbs. To compare these four systems of transport, we propose to calculate the CO2 emissions per capita by the distance of the center, every kilometers for the first ten kilometers, every two kilometers between the tenth and the twentieth kilometers, then every 5 kilometers. Emissions are  cumulated, we estimate how much all the people who live between the center and a particular distance emit CO2. For example, on the graph for distance 10, we divide all the pollutant emissions emitted by the inhabitants residing at less than 10 km of the center by the number of inhabitants in this zone.

Then each point represents the individual level of CO2 emission which would correspond to the calculations carried out on a given perimeter. This representation classifies the agglomerations between them and clarifies simultaneously the effect of the center distance on the emissions levels. The emissions described in the total results (table 5). correspond to the last points of each curve. Paris seems there having emissions slightly higher than that of Lyon. The graph shows in what the values of emissions are correlated with the definition of study perimeter. the emissions on Paris are systematically lower than those of Lyon what total measurement ( table 5) did not make it possible to note.

We suggest systematically carrying out this type of representation for all comparisons between on the environmental impacts related to urban mobility. It allows to compare cities in French context with less issues related to study perimeters and show clearly that city have different environmental costs.

## Environmental costs: technology, length and speed effect

Years of studies are not the same  for the four agglomeration and it is necessary to take account technology change to give sense to comparison. With our data we can compare the evolution of unit pollutant emission between 1995 and 2001 (appendix 1 shows the changes of car fleet). Data show that for local pollutant (CO, VOC, NOX, PM), the decrease of emission by veh-km is quite important. The European norms (Euro I, Euro II, Euro III,…) which fix emission values to be respected by  car manufacturers, have permitted to improve eco-efficiency.

Table 11 Pollutant emission by veh-km (g/veh-km)

|  | Lyon 1995 | Bordeaux 1998 | Paris 2001 | Grenoble 2001 |
| --- | --- | --- | --- | --- |
| Consumption | 78 | 68 | 66 | 67 |
| CO2 | 210 | 198 | 192 | 198 |
| CO | 16,5 | 7,9 | 5,0 | 6,5 |
| VOC | 2,05 | 1,10 | 0,66 | 0,70 |
| NOX | 1,64 | 1,49 | 1,09 | 0,77 |
| PM | 0,09 | 0,08 | 0,06 | 0,06 |

Those results explain why in Lyon local pollutants (table 5) emissions are higher in Lyon.  For fuel consumption and CO2 emission norms did not exist, and the progresses are less clear. If motor engine became increasingly effective, household wants always heavier  vehicles: with climax, more space, more safety equipments…. Moreover, no new technology seems ready to strongly reduce CO2 emission. Even if household bought hybrid vehicle (approximately 110g CO2/veh-km for an average car) it will last more than 10 years to reduce by 2, CO2 emissions, if the travel demand stay at the same level. So technology could not be considered as a solution to reduce CO2 emissions. As unit emission of CO2 are quite similar in the four cities, we use it to compare the effect of trip length and speed on emission level.

In the Table 12, we have divided all the trips in private vehicle in seven classes of distance for the agglomeration of Paris and Grenoble. The shortest trip (<2,5 km) are the most numerous the slowest and the least eco-efficient (measured as CO2 (g/km)) but represent only a small part of total CO2 emissions. On the contrary, the longest trips (>20 km) are the fastest, the most eco-efficient but even if they are not very numerous they represent nearly 30% of total CO2 emissions.

Table 12 Speed and CO2 emission (Trips in private vehicle only)

|  | Grenoble | Paris |
| --- | --- | --- |
| Class trips | Trips (%) | CO2 (%) | V (km/h) | CO2(g/km) | Trips (%) | CO2 (%) | V (km/h) | CO2(g/km) |
| <2,5 km | 43 | 14 | 13 | 313 | 33 | 9 | 11 | 342 |
| 2,5-5 km | 13 | 10 | 30 | 219 | 20 | 13 | 18 | 282 |
| 5-7,5 km | 11 | 11 | 37 | 195 | 11 | 11 | 22 | 254 |
| 7,5-10 km | 7 | 8 | 44 | 179 | 8 | 10 | 25 | 235 |
| 10-15 km | 9 | 14 | 46 | 171 | 11 | 17 | 29 | 212 |
| 15-20 km | 6 | 13 | 52 | 160 | 6 | 12 | 33 | 188 |
| >20 km | 10 | 29 | 56 | 146 | 11 | 29 | 39 | 151 |
| Ensemble | 100 | 100 | 29 | 179 | 100 | 100 | 21 | 204 |

With these data, we see that even we could change modal choice for all the shortest trip, CO2 emission would not be strongly decreased.  In the same kind of idea, speed management could not be the only solution to reduce directly CO2 emissions. The numbers show that unit CO2 emission decrease with speed in urban condition, it means that congestion increase pollution. But in the same time congestion make public transport attractive, and reduce travel demand.

Under these conditions, the only way to reduce CO2 emission is to reduce travel demand in private vehicle.

## Increasing mobility cost and household disparities:

We are face of new issues related to sustainability: the objective of environmental preservation could increase social inequity. It seems to exist a consensus on necessity to reduce environmental cost of urban mobility quite quickly. To develop coherent urbanism, public transport, pedestrian and bike friendly area take long time and require important expenditure and public action. Technology progresses are efficient for local pollutant (CO, NOx, COV,PM) but  for the moment CO2 emission are still increasing and it seems hard to make real progress quickly. Economic efficacy and environmental preservation criterion justify to increase mobility tax (congestion charge, parking fees, fuel taxes,..): the well-off household consume more transport activity and emit more CO2.  As we have seen in table 7 to table 10, well-off household do not optimise their choice of localisation to reduce environmental cost of their mobility and prefer to maximize their access to urban amenities. Signal price, by internalising environmental costs, could change behaviour and funds collected could be invested in public transport or green technology.  But because of car dependency, some household would lost most of their accessibility if mobility taxes grow. Some household with few income who live in suburbs spend sometimes more than 20% of their income in their mobility. If mobility tax increase , the risk exists that to  decrease their expenditure in housing those household will live still further from the center, or to reduce their transportation expenditure by buying older car more pollutant. It seems necessary during the period where mobility cost will increase to help these household.

In the French context an other risk is to reinforce spatial income distribution polarization. As we can see   in Paris case (table 7), the rich household live in the center of agglomeration where access to amenities are the best, due to a good public transport system. If costs for private mobility trips increase, by more mobility taxes or speed reduction, household would live closer to the center. Segregation could be a consequence of growing concern about climate change.

Conclusion

The first result of this methodological paper is that it is  possible to determine quite precisely the cost of mobility attached to an urban system of transport without too many methodological bias. The household travel survey traffic model (here those used by the French ministry of transport), the model of pollutant emission (the European model COPERT III), the economic data extracted for each city allow such determination in a quite homogenous context.

The numbers show that if current household monetary expenditure for mobility are quite similar in the four cities, differences are important for environmental costs, more especially for CO2 emissions. We proposed a methodology that allows to classify agglomeration.  Inside agglomerations, urban sprawl explain differences measured. The result also show disparities between household, on the one hand, well-off household try to maximize access to urban amenity, on the other hand some household with low income level try to reduce mobility expenditure.  The high levels of CO2 emission and the growing concern about global warming should lead to increase monetary cost of mobility. The main challenge for public policies to reach sustainable urban  mobility will be to reduce environmental mobility costs without sacrificing accessibility of one part of dwellers.

References

ADEME,, 1998, Emissions de polluants et consommation liées à la circulation routière. Paramètres déterminants et méthodes de quantifications. Paris : ADEME, 112 p.

CERVERO R., KOCKELMAN K. 1997, Travel demand and the 3Ds: Density, Diversity and Design. Transport Research D, vol. 2, pp. 199-219.

FOUCHIER V., 1997, Les densités urbaines et le développement durable. Le cas de l'Ile-de-France et des villes nouvelles, Paris : Edition du SGVN (Secrétariat Général du Groupe Central des Villes Nouvelles), 212 p.

GALLEZ C., HIVERT L., 1998, BEED: mode d'emploi. Synthèse méthodologique pour les études "budget-énergie-environnement des déplacements". Rapport INRETS n°690-9306-RB. Paris: ADEME-INRETS, 1998, 86 p.

GALLEZ C., 1995, Budgets Energie Environnement des Déplacements (BEED) en Ile-de-France. Analyse de la dépense énergétique et des émissions de polluantes liées à la mobilité des franciliens. Arcueil: INRETS, 110 p.

GIORGI L., 2003, Sustainable mobility. Challenges, opportunities and conflicts – a social science perspective. International Social Science Journal,volume 55, n°176, pp 179-184

GORDON P., RICHARDSON H.W,1997, Are compacties a desirable planning goal ? Journal of the American Planning Association 63 (1), pp 95-106

HANDY S., 2005, Critical assessment of the litterature on the relation-ship among transportation, land use and physical activities. Ressource paper for TBR Special Report 282. Washington DC.

HIVERT L., 1994, Budget Energie-Pollution. Bilan de la mobilité des ménages de l'agglomération grenoblois. Arcueil: INRETS, 98 p.

HIVERT L., 1998, Budgets Energie Environnement des Déplacements (BEED) dans l'agglomération bordelaise. Arcueil: INRETS, 95 p.

KAUFFMAN V., 2000, Mobilité quotidienne et dynamiques urbaines. Lausanne: Presses polytechniques et universitaires romandes, 252 p.

MINDALY O., RAVEH A., SALOMON I., 2004,  Urban density and energy consumption: a new look at old statistics. Transportation Research Part A 38, pp 143-162

NEWMAN P. W. G., KENWORTHY J. R., 1989, Gasoline consumption and cities: a comparison of U.S. cities with a global survey, Journal of the American Planning Association, 55 (1), pp. 24-37

NEWMAN P. W. G., KENWORTHY J. R., 1998, Sustainability and cities - Overcoming automobile dependence, Washington D.C., Island Press.

NICOLAS J.-P, POCHET P., POIMBOEUF H., 2003, Towards sustainable mobility indicators : application to the Lyons conurbation. Transport policy, 10, 197-208.

NICOLAS J.-P, POCHET P., POIMBOEUF H., 2001, Indicateurs de mobilité durable : application à l'agglomération de Lyon, méthodes et résultats. LET-APDD Lyon, LET: 237 p.

Disponible sur http://www.ish-lyon.cnrs.fr/let/francais/indexpub.htm en juin 2005

NTZIACHRISTOS L., . SAMARAS Z.., 2000, Copert III Computer programme to calculate emissions from road transport. Technical report n°69. Agence Européenne de l'Environnement, 86 p.

Disponible sur http://reports.eea.eu.int/Technical_report_No_49/en/tab_content_RLR (janvier 2006)

POUYANNE G., 2004, Forme urbaine et mobilité quotidienne. Thèse de Doctorat de Sciences Economiques Université Montesquieu-Bordeaux IV, 307p .

VAN de COEVERING P., SCHWANEN T, 2006, Re-evaluating the impact of urban form on travel patterns in Europe and North –America. Transport policy 13, pp 229-239

Appendix

Appendix  1 : Vehicles owned and used by household

n.v: number of vehicles

p.s: % vehicles (static)

p.d:  % vehicles-km (dynamic)

CO2: CO2 emissions (g/km)

|  | Lyon (1995) | Bordeaux (1998) | Grenoble (2002) | Paris (2002) |
| --- | --- | --- | --- | --- |
| Classes véhicules | n.v | p.s | p.d. | CO2 | n.v | p.s | p.d. | CO2 | n.v | p.s | p.d. | CO2 | n.v | p.s | p.d. | CO2 |
| VP ess. <1,4l Pre ECE | 1817 | 0,3 | 0,2 | 246 | 464 | 0, 1 | 0,2 | 183 | 722 | 0,2 | 0, 1 | 174 | 11632 | 0,3 | 0, 1 | 159 |
| VP ess. <1,4l ECE 15/01 | 7348 | 1,2 | 1,0 | 216 | 5591 | 1,6 | 1,4 | 161 | 706 | 0,2 | 0, 1 | 136 | 10001 | 0,2 | 0, 1 | 123 |
| VP ess. <1,4l ECE 15/02 | 13014 | 2, 1 | 1,2 | 192 | 1782 | 0,5 | 0,5 | 154 | 982 | 0,3 | 0, 1 | 161 | 9322 | 0,2 | 0, 1 | 181 |
| VP ess. <1,4l ECE 15/03 | 74191 | 12,0 | 10, 1 | 192 | 23942 | 6,9 | 5,9 | 146 | 9095 | 2,4 | 1,2 | 149 | 88037 | 2,0 | 1,3 | 148 |
| VP ess. <1,4l ECE 15/04 | 175695 | 28,4 | 26,6 | 176 | 60636 | 17,4 | 16,2 | 149 | 56462 | 14,8 | 10,7 | 149 | 542944 | 12,2 | 9,0 | 146 |
| VP ess. <1,4l Euro I | 36150 | 5,9 | 5,9 | 218 | 48525 | 13,9 | 11,3 | 171 | 39080 | 10,2 | 8,6 | 172 | 476318 | 10,7 | 8,8 | 193 |
| VP ess. <1,4l Euro II | 0 | 0,0 | 0,0 | 0 | 22105 | 6,3 | 5,5 | 179 | 47202 | 12,4 | 11,0 | 174 | 562376 | 12,7 | 10,8 | 195 |
| VP ess. <1,4l Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 7401 | 1,9 | 1,9 | 167 | 125945 | 2,8 | 3,0 | 184 |
| VP ess. <1,4l Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 |
| VP ess. 1,4 à 2l Pre ECE | 650 | 0, 1 | 0,0 | 0 | 262 | 0, 1 | 0, 1 | 192 | 465 | 0, 1 | 0,0 | 198 | 4296 | 0, 1 | 0, 1 | 273 |
| VP ess. 1,4 à 2l ECE 15/01 | 925 | 0,2 | 0, 1 | 276 | 555 | 0,2 | 0,2 | 208 | 150 | 0,0 | 0,0 | 273 | 5016 | 0, 1 | 0,0 | 263 |
| VP ess. 1,4 à 2l ECE 15/02 | 1988 | 0,3 | 0,2 | 262 | 1003 | 0,3 | 0,2 | 170 | 759 | 0,2 | 0,0 | 156 | 6909 | 0,2 | 0,0 | 202 |
| VP ess. 1,4 à 2l ECE 15/03 | 20544 | 3,3 | 3,3 | 251 | 10069 | 2,9 | 2,3 | 185 | 3655 | 1,0 | 0,7 | 180 | 44770 | 1,0 | 0,4 | 223 |
| VP ess. 1,4 à 2l ECE 15/04 | 87427 | 14,2 | 12,7 | 231 | 30900 | 8,9 | 8,2 | 186 | 21081 | 5,5 | 3,9 | 182 | 309273 | 7,0 | 5,0 | 182 |
| VP ess. 1,4 à 2l Euro I | 19523 | 3,2 | 3, 1 | 303 | 16538 | 4,7 | 3,9 | 227 | 14939 | 3,9 | 3,2 | 218 | 231771 | 5,2 | 4,6 | 254 |
| VP ess. 1,4 à 2l Euro II | 0 | 0,0 | 0,0 | 0 | 11015 | 3,2 | 2,4 | 238 | 18174 | 4,8 | 4,7 | 232 | 279474 | 6,3 | 6,0 | 256 |
| VP ess. 1,4 à 2l Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 4941 | 1,3 | 1,4 | 221 | 68293 | 1,5 | 1,4 | 255 |
| VP ess. 1,4 à 2l Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 |
| VP ess. >2l Pre ECE | 428 | 0, 1 | 0,0 | 462 | 0 | 0,0 | 0,0 | 0 | 86 | 0,0 | 0,0 | . | 4753 | 0, 1 | 0, 1 | 322 |
| VP ess. >2l ECE 15/01 | 381 | 0, 1 | 0,0 | 373 | 0 | 0,0 | 0,0 | 0 | 150 | 0,0 | 0,0 | 325 | 770 | 0,0 | 0,0 | 0 |
| VP ess. >2l ECE 15/02 | 331 | 0, 1 | 0,0 | 402 | 0 | 0,0 | 0,0 | 0 | 26 | 0,0 | 0,0 | . | 1550 | 0,0 | 0,0 | 124 |
| VP ess. >2l ECE 15/03 | 3286 | 0,5 | 0,3 | 343 | 773 | 0,2 | 0,4 | 225 | 372 | 0, 1 | 0,0 | 281 | 7608 | 0,2 | 0,0 | 148 |
| VP ess. >2l ECE 15/04 | 7336 | 1,2 | 1,2 | 344 | 870 | 0,3 | 0,4 | 232 | 2676 | 0,7 | 0,5 | 221 | 36601 | 0,8 | 0,6 | 241 |
| VP ess. >2l Euro I | 3006 | 0,5 | 0,4 | 390 | 1458 | 0,4 | 0,3 | 304 | 1319 | 0,4 | 0,4 | 281 | 28099 | 0,6 | 0,4 | 327 |
| VP ess. >2l Euro II | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 1528 | 0,4 | 0,3 | 252 | 32568 | 0,7 | 0,7 | 340 |
| VP ess. >2l Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 236 | 0, 1 | 0,0 | 233 | 8343 | 0,2 | 0,2 | 381 |
| VP ess. >2l Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 |
| VP diesel <2l conv. | 86332 | 14,0 | 17,7 | 247 | 24139 | 6,9 | 7,7 | 183 | 33072 | 8,7 | 9,4 | 170 | 295350 | 6,6 | 6,7 | 187 |
| VP diesel <2l Euro I | 36831 | 6,0 | 8,2 | 215 | 29774 | 8,5 | 11,0 | 168 | 29921 | 7,8 | 10, 1 | 159 | 304550 | 6,9 | 7,9 | 162 |
| VP diesel <2l Euro II | 0 | 0,0 | 0,0 | 0 | 11648 | 3,3 | 4,8 | 170 | 36960 | 9,7 | 13,3 | 158 | 404190 | 9, 1 | 12,4 | 158 |
| VP diesel <2l Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 13237 | 3,5 | 4,9 | 159 | 144919 | 3,3 | 5,4 | 162 |
| VP diesel <2l Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0, 1 | 139 |
| VP diesel >2l conv. | 31798 | 5,2 | 5,2 | 250 | 35282 | 10, 1 | 13,5 | 178 | 1071 | 0,3 | 0,2 | 170 | 97643 | 2,2 | 2,2 | 195 |
| VP diesel >2l Euro I | 8896 | 1,4 | 2,3 | 216 | 5918 | 1,7 | 2,0 | 168 | 17372 | 4,6 | 4,7 | 163 | 96736 | 2,2 | 2,3 | 169 |
| VP diesel >2l Euro II | 0 | 0,0 | 0,0 | 0 | 3980 | 1, 1 | 1, 1 | 173 | 10999 | 2,9 | 3,6 | 162 | 127494 | 2,9 | 4,4 | 169 |
| VP diesel >2l Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 3238 | 0,9 | 1, 1 | 154 | 57449 | 1,3 | 2,0 | 156 |
| VP diesel >2l Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 |
| VP GPL conv. | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 3761 | 0, 1 | 0, 1 | . |
| VP GPL Euro I | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 1893 | 0,5 | 0,6 | 152 | 5693 | 0, 1 | 0, 1 | . |
| VP GPL Euro II | 0 | 0,0 | 0,0 | 0 | 2068 | 0,6 | 0,6 | 167 | 1397 | 0,4 | 0,5 | 155 | 11571 | 0,3 | 0,4 | . |
| VP GPL Euro III | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 265 | 0, 1 | 0, 1 | 154 | 953 | 0,0 | 0,7 | . |
| VP GPL Euro IV | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 | 0 | 0,0 | 0,0 | 0 |
| Total parc enquêté | 617896 | 100 | 100 | 218 | 349297 | 100 | 100 | 174 | 381631 | 100 | 100 | 171 | 4446978 | 100 | 100 | 215 |

# Text boxes

demand

offer

demand

Passagers transport

Infrastructures definition and localisation

Transport component

offer

Transport demand definition and localisation

Amenities definition and localisation

Spatial component

Socio-economic characteristic

- Income , family status…

- Motorization rate

Timetable characteristics

- Time available

- Temporality of the activities

Social interactions component

# Accessibility

Needs, capacities, opportunities

Time

constraints

Costs (time, effort)

Amenities available

Com

Com

Services

Accessibility

Needs :

Mobility

Costs

environmental social

economic

Transport

System

Figure 1 Urban system divided in three subsystems

Figure 2 Transport system defined with the notion of need, service and cost